## Slide 1: WF on transmit signal quality
CATT
3GPP TSG-RAN WG4 Meeting #95-e Draft R4-2008783
Electronic Meeting, 25 May – 5 June, 2020

## Slide 2: Background (1/2) - Frequency error
The following contributions were provided in RAN4#95e
  R4-2007402, frequency error requirement for IAB, ZTE
  R4-2007573, IAB-MT Frequency error, Ericsson
  R4-2006799, RAN4 implication due to Sync from multiple parents for “Case 1” OTA timing, Samsung
The synchronization source issue and the spec impact were discussed in the meeting.
There was also a proposal to send LS to RAN1/RAN2 on the signaling aspect.

## Slide 3: Background (2/2) - Transmit modulation quality
The followings are the agreements related to IAB-MT transmit modulation quality before RAN4#95e
  EVM
    Re-use UE EVM requirements, excluding the low output power range, do not define PI/2 BPSK support for IAB-MT. Introduce QPSK, 16QAM, 64QAM modulation for both FR1 and FR2 and 256QAM only for FR1.
  Carrier leakage, In-band emissions
    IAB-MT In-band emissions, carrier leakage and image rejection shall be specified at maximum power level.
    The requirement in FR2 shall be
  EVM equalizer spectrum flatness:
    The zero-forcing equalizer used in EVM measurement shall meet the same flatness requirement as detailed in 38.101-1 and 38.101-2 for FR1 and FR2, respectively
In RAN4#95e R4-2006276 revisited the above agreements and EVM test procedure was also discussed in the same contribution.
Parameter description | Unit | Limit (NOTE 1) | Applicable Frequencies
General | dB |  | Any non-allocated RB
IQ Image | dB | -25 | Image frequencies
Carrier leakage | dBc | -25 | Carrier frequency
Parameter description | Unit | Limit (NOTE 1) | Applicable Frequencies
General | dB |  | Any non-allocated RB
IQ Image | dB | -25 | Image frequencies
Carrier leakage | dBc | -25 | Carrier frequency

## Slide 4: Way Forward (1/2) - Frequency error
No LS on frequency error needed
No need to capture additional details to specification

## Slide 5: Way Forward (2/2) - Transmit modulation quality
Wide area IAB-MT
  No carrier leakage, in-band emission and EVM equalizer spectrum flatness requirements are defined for both FR1 and FR2.
  EVM test procedure FFS.
Local area IAB-MT
  FFS if carrier leakage, in-band emission and EVM equalizer spectrum flatness requirements will be defined and how to define them.
    Reuse current agreement is also an option.
  EVM test procedure FFS.