## Slide 1: WF on IAB-MT unwanted emissions
Nokia, Nokia Shanghai Bell
Draft R4-2008784
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, May 25th – June 5th 2020

## Slide 2: Contributions in RAN4#95-e
R4-2006800, Samsung
R4-2007130, Qualcomm Incorporated
R4-2007576, Ericsson
R4-2007909, Huawei
R4-2007403, ZTE corporation
R4-2007120, Nokia, Nokia Shanghai Bell

## Slide 3: Way forward on FR1 IAB-MT relative ACLR
IAB-MT ACLR minimum requirement in FR1 is 45 dBc

## Slide 4: Way forward on OBUE and SEM
For FR2:
  Wide Area IAB-MT shall meet wide area BS OBUE requirements
    Pending agreements on feature level discussion of IAB-MT transmission in DL timeslot, it can be further discussed if in addition, when IAB-MT is configured to transmit in DL timeslot, wide area IAB-MT needs to meet the OBUE requirements of IAB-DU of the same IAB-Node
  FFS for local area IAB-MT
For FR1
  Pending relative ACLR is agreed as 45 dBc, Wide Area IAB-MT shall meet wide area BS OBUE requirements
    Pending agreements on feature level discussion of IAB-MT transmission in DL timeslot, it can be further discussed if in addition, when IAB-MT is configured to transmit in DL timeslot, wide area IAB-MT needs to meet the OBUE requirements of IAB-DU of the same IAB-Node
  FFS for local area IAB-MT
For both FR1 and FR2 the boundary between in-band and spurious region will follow BS requirements.

## Slide 5: Way forward on absolute ACLR
Absolute ACLR to be discussed further in future meetings.

## Slide 6: Way forward on spurious emissions
Spurious emissions are regulatory requirements. Being a network node, IAB-MT shall meet the same spurious emissions requirements as base stations.
  Both category A and category B spurious emissions shall be specified for IAB-MT