## Slide 1: WF on power saving demodulation
Agenda Item: 8.7.3
Document for: Approval
Source: CATT……
3GPP TSG-RAN WG4 #95e Tdoc R4-2008802
Electronic Meeting, 25th May – 5th June, 2020

## Slide 2: Background
In RAN4#95-e meeting, there were extensive discussions on UE demodulation requirements for Rel-16 UE power saving. The following contributions were reviewed.
[Companies inputs are to be added here later]

## Slide 3: Background
The discussions in RAN4#95-e are focused on the following two issues
Issue 1: Whether to introduce joint test for PDCCH-WUS during DRX OFF and PDCCH during DRX ON for power saving UE?
The motivation for such a test case is based on the following points,
  PDCCH-WUS is used to indicate UE to wake up for PDCCH/PDSCH reception in DRX-ON.
  PDCCH-WUS is demodulated in DRX-OFF state which is different from normal PDCCH and its performance has impact on the following PDCCH/PDSCH performance.
  RAN1 assumption on PDCCH-WUS misdetection performance is 10^-3 which is far below 10^-2 for normal PDCCH.
  In order not to degrade the PDCCH performance in DRX-ON, PDCCH-WUS performance and UE behavior need to be guaranteed by proper test case for UE supporting this feature.
Issue 2: Applicability of 4Rx demodulation performance for UEs with max MIMO layer adaption.
  How to clarify the applicability for 4Rx demodulation performance
  Whether additional requirements are needed for 4Rx UE with maxMIMO-layers-r16=2

## Slide 4: Way Forward (1)
Issue 1: Whether to introduce joint test for PDCCH-WUS during DRX OFF and PDCCH during DRX ON for power saving UE?
After several rounds of discussion in RAN4#94ebis and RAN4#95e meeting, the following 2 options are still pending,
  Option 1: To define a joint test case for PDCCH-WUS in DRX OFF and PDCCH in DRX ON.
  (CATT, CMCC, Qualcomm, MediaTek, vivo , NTT DoCoMo?)
  Option 2: No new requirements are needed.
  (Huawei, Intel)
Recommended WF:
  Adopt option 1
  Finalize simulation assumption by the end of August meeting.

## Slide 5: Way Forward (2)
Issue 2: Applicability of 4Rx demodulation performance for UEs with max MIMO layer adaption.
  Proposal 2b: Add a note in TS 38.101-4 to clarify that ‘maxMIMO-Layers-r16’ is not configured in IE PDSCH-Config “Note: ‘maxMIMO-Layers-r16’ is not configured in IE PDSCH-Config during the performance requirements testing for UE supporting Release 16 per BWP MIMO layer adaptation.”(exact wording will be reviewed in R4-2008804)
  No additional requirements for 4Rx UE with maxMIMO-layers-r16=2.