## Slide 1: WF on A-MPR requirements for PSSCH/PSCCH transmission
LG Electronics, ...
3GPP TSG-RAN WG4#95-e Meeting R4-2008439
Electronic Meeting, 25th May – 05th June, 2020

## Slide 2: Background
In this meeting, RAN4 discuss the MPR/A-MPR requirements for PSSCH/PSCCH for NR V2X UE as follow.
Issue 1-1-1: A-MPR for PSSCH/PSCCH transmission
  To derive A-MPR requirements, the worst A-MPR values from interested companies are chosen.
  Define NS_33 and NS_52 with current regulatory requirements in TS at this moment. A-MPR for update ETSI regulation will be captured in TR only.
Tentative agreement:
  NS_33(existing ETSI), NS_52(FCC) and New_NS (Update ETSI in future) will be captured in TR.
  NS_33 and NS_52 will be captured in TS38.101-1 in this meeting. The new_NS (Update ETSI in future) will be added in TS38.101-1 in Rel-16 when ETSI release the revised EN302 571 requirement
Recommendations for 2nd round:
  WF will assign to complete A-MPR for PSSCH/PSCCH transmission based on the tentative agreement. The detail table format and A-MPR level will be proposed in WF.

## Slide 3: WF1 on MPR for PC3 NR V2X UE at n47
Maximum power reduction (MPR) for PSSCH/PSCCH for power class 3 NR V2X UE
Above MPR requirements will be used for PSSCH/PSCCH transmission.
Modulation |  | MPR (dB) | 
 |  | Outer RB allocations | Inner RB allocations
CP-OFDM | QPSK | ≤ 4.5 | ≤ 2.5
 | 16 QAM | ≤ 4.5 | ≤ 2.5
 | 64 QAM | ≤ 4.5 | 
 | 256 QAM | ≤ 7.0 | 

## Slide 4: WF2-1 on A-MPR for PC3 NR V2X UE at n47
For ETSI regulation at 10MHz with NS_33
A-MPRstep is decided as follow
  AMPRstep = 1.2 for RBstart 0 and 1, and 0.7 for all other RBstart
Carrier frequency(MHz) | Resources Blocks (LCRB) | Start Resource Block | A-MPRbase (dB) |  | 
 |  |  | QPSK/16QAM | 64QAM | 256QAM
5860 | ≥10 and ≤ 15 | 0 | ≤ 24 |  | 
 |  | ≥ 1 and ≤ 3 | ≤19 |  | 
 | ≥10 and ≤ 15 | ≥ 26 and ≤ 38 | ≤6 |  | 
 | ≥ 10 and ≤ 20 | ≥ 12 and ≤ 14 | ≤11 |  | 
 |  | ≥ 15 and ≤ 19 | ≤9.5 |  | 
 |  | ≥ 20 and ≤ 25 | ≤8.0 |  | 
 | ≥ 10 and ≤ 30 | ≥ 4 and ≤7 | ≤ 16 |  | 
 |  | ≥ 8 and ≤ 11 | ≤ 13.5 |  | 
 | ≥ 20 and ≤ 30 | ≥ 0 and ≤ 3 | ≤ 22 |  | 
 | ≥ 25 and ≤ 30 | ≥ 16 and ≤ 21 | ≤ 9.5 |  | 
 |  | ≥ 22 and ≤ 27 | ≤ 8.0 |  | 
 | ≥ 25 and ≤ 40 | ≥ 12 and ≤ 15 | ≤ 12 |  | 
 | ≥ 40 and ≤ 45 | 0 and 1 | ≤ 19 |  | 
 |  | ≥ 2 and ≤ 5 | ≤ 16 |  | 
 |  | ≥ 6 and ≤ 11 | ≤ 13.5 |  | 
 | ≥ 50 | ≥ 0 | ≤ 16 |  | 

## Slide 5: WF2-2 on A-MPR for PC3 NR V2X UE at n47
For ETSI regulation at 10MHz with NS_33
  At Fc=5870, 5880, 5890, 5900, 5910,5920
A-MPRstep is decided as 0.5 dB for all RBstart
Carrier frequency(MHz) | RB allocations | A-MPRbase (dB) |  |  | 
 |  | QPSK | 16QAM | 64QAM | 256QAM
5870, 5880, 5890, 5900, 5910, 5920 | Inner | ≤ 3.0 |  | ≤ 5.0 | ≤ 6.0
 | Outer | ≤ 4.5 |  |  | 

## Slide 6: WF2-3 on A-MPR for PC3 NR V2X UE at n47
For ETSI regulation at 10MHz with New_NS
  At Fc=5860, 5870, 5880, 5890, 5900, 5910,5920
A-MPRstep is not define due to the unwanted emission requirements will be tested as conducted mode with New_NS
  Please refer latest ETSI draft version EN302.571
Carrier frequency(MHz) | RB allocations | A-MPR (dB) |  |  | 
 |  | QPSK | 16QAM | 64QAM | 256QAM
5860, 5870, 5880, 5890, 5900, 5910, 5920 | Inner | ≤ 3.0 |  | ≤ 5.0 | ≤ 6.0
 | Outer | ≤ 4.5 |  |  | 

## Slide 7: WF2-4 on A-MPR for PC3 NR V2X UE at n47
For FCC regulation at 40MHz with NS_52
  Option 1
Only define A-MPR level without A-MPRstep due to conducted test
Carrier frequency(MHz) | Modulation | A-MPR(dB) |  | 
 |  | Edge RB allocations | Outer RB allocations | Inner RB allocation
5885 | QPSK | ≤ (10.0 + ΔNote1) | ≤ 8.0 | ≤ 5.5
 | 16QAM |  | ≤ 8.0 | ≤ 5.5
 | 64QAM |  | ≤ 8.5 | ≤ 5.5
 | 256QAM |  | ≤ 8.5 | ≤ 6.0
Note1: Δ is 0, 3, and 5 for 60kHz, 30kHz, and 15kHz SCS, respectively. |  |  |  | 

## Slide 8: WF2-4 on A-MPR for PC3 NR V2X UE at n47
For FCC regulation at 40MHz with NS_52
  Option 2
Only define A-MPR level without A-MPRstep due to conducted test
Carrier frequency(MHz) | Modulation | A-MPR(dB) | 
 |  | Outer RB allocations | Inner RB allocation
5885 | QPSK | 15 | ≤ 5.5
 | 16QAM |  | ≤ 5.5
 | 64QAM |  | ≤ 5.5
 | 256QAM |  | ≤ 6.0

## Slide 9: Conclusion of PSSCH/PSCCH
RAN4 make consensus on MPR of PSSCH/PSCCH in WF1 (slide #3)
RAN4 make consensus on A-MPR of PSSCH/PSCCH for NS_33 in WF2-1 and WF2-2 (slide #4 & #5)
RAN4 make consensus on A-MPR for PSSCH/PSCCH for New_NS in WF 2-3 (slide #6)
RAN4 will further discuss A-MPR for PSSCH/PSCCH for NS_52 in WF 2-4 based on two options (slide #7 & #8)
  Other revised A-MPR table is not precluded.

## Slide 10: References
# | TDoc | Title | Source | Type | Agenda item
1 | R4-2006701 | TP on NR V2X A-MPR for PSSCH/PSCCH | LG Electronics Inc. | pCR | 6.4.3.1
2 | R4-2006746 | TP on remaining issues for NR V2X UE (Coexistence table to remove n47 ETSI requirements -30dBm/MHz, configured Tx power) | LG Electronics France | pCR | 6.4.3
3 | R4-2006820 | TP on 5G V2X MPR A-MPR for S-SSB transmission | Qualcomm Incorporated | pCR | 6.4.3.1
4 | R4-2007880 | TP to TR38.886 V2X PSSCH PSCCH A-MPR | Qualcomm Austria RFFE GmbH | pCR | 6.4.3.1
5 | R4-2007881 | TP to TR38.886 A-MPR for 10 and 40MHz V2X PSFCH | Qualcomm Incorporated | pCR | 6.4.3.1
6 | R4-2008079 | Discussion on ETSI NS issue, NS_33 AMPR and spurious emission for UE co-existence for V2X | Huawei, HiSilicon | other | 6.4.3.1
7 | R4-2008080 | TP to update MPR\AMPR requirements for both PC3 and PC2 NR V2X in band n47 | Huawei, HiSilicon | pCR | 6.4.3.1
8 | R4-2008081 | DraftCR to specify MPR\AMPR requirements for PC3 NR V2X in band n47 | Huawei, HiSilicon | draftCR | 6.4.3.1
9 | R4-2004471 | MPR A-MPR results for PSSS/SSSS/PSBCH transmission | Qualcomm Incorporated | other | 6.4.4.1