## Slide 1
3GPP TSG-RAN WG4 Meeting #95-e R4-2008627
Electronic Meeting, 25 May – 5 June, 2020
Agenda Item: 6.17.1
WF on RRM for NR HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-1912781 WF on RRM for NR HST, RAN4#92BIS
  R4-1915887 WF on RRM for NR HST, RAN4#93
  R4-2002253 WF on RRM for NR HST, RAN4#94-e
  R4-2005358 WF on RRM for NR HST, RAN4#94-e-bis

## Slide 3: Cell re-selection requirements
  FFS whether additional note such as Note x: Operation with scaling factor M=1.5, M=2 may not be sufficient in all high speed deployments considered in this release of the specifications should be added in NR high speed specifications
    Instead of adding the note in the spec, the note is captured in the WF.
  Requirements with 2.56s DRX cycle have not been enhanced for high speed operation.

## Slide 4: Cell re-selection requirements
  No need to align the serving cell measurement requirements with the proposal for intra-frequency neighbour cell measurement

## Slide 5: Cell identification delay requirements for DRX case in connected mode
FFS whether additional note such as Note x: Operation with scaling factor 1.5 may not be sufficient in all high speed deployments considered in this release of the specifications should be added in NR high speed specifications
  Instead of adding the note in the spec, the note is captured in the WF.

## Slide 6: Applied DRX cycle in connected mode for HST
  FFS whether additional note is added to the spec, such as “Requirements with 0.64s and 1.28s DRX cycle may not be sufficient in all high speed deployments considered in this release of the specifications” should be added in NR high speed specifications”
  Instead of adding the note in the spec, the note is captured in the WF.
  Requirements with 2.56s DRX cycle have not been enhanced for high speed operation.

## Slide 7: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Cell re-selection requirements on NR- EUTRA inter-RAT measurement in idle mode
DRX cycle length [s] | Tdetect,EUTRAN [s] (number of DRX cycles) | Tmeasure,EUTRAN [s] (number of DRX cycles) | Tevaluate,E-UTRAN [s] (number of DRX cycles)
0.32 | 4.16(13) | 0.64 (2) | 0.96(3)
0.64 | 7.68 (12) | 1.28 (2) | 1.92 (3)
1.28 | 8.96(7) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)
  Whether the introduction of per carrier flag will have impact on the higher priority measurement can be further checked in next meeting

## Slide 8: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  NEUTRA_carrier issue in the cell re-selection requirements on NR- EUTRA inter-RAT measurement taking the per inter-RAT carrier flag into account.
    The requirement for non-HST carrier = the requirement for HST carrier = NEUTRA_carrier_HST * Tdetect,EUTRAN_HST + NEUTRA_carrier_nonHST * Tdetect,EUTRAN_nonHST
    Where:
      NEUTRA_carrier is the total number of configured E-UTRA carriers,
      NEUTRA_carrier = NEUTRA_carrier_HST + NEUTRA_carrier_nonHST,
      NEUTRA_carrier_HST is the total number of configured high speed carriers,
      NEUTRA_carrier_nonHST is the total number of configured non-high-speed carriers.
      Tdetect,EUTRAN_HST is the requirements specified for high speed scenario.
      Tdetect,EUTRAN_nonHST is the requirements specified for normal scenario.

## Slide 9: Inter-RAT measurement
Notation issue for CR on NR- EUTRA Inter-RAT measurement in idle mode
  For non-high-speed carriers
    NEUTRA_carrier is used in the spec
  For high-speed carriers
    NEUTRA_carrier_HST is used in the spec

## Slide 10: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Cell identification with DRX in connected mode
DRX cycle length (s) | TIdentify, E-UTRAN TDD (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.2.2 apply | Non-DRX requirements in clause 9.4.2.2 apply
0.16<DRx cycle<=0.32 | Note1 (15*CSSFinterRAT) | 
0.32<DRx cycle <= 0.64 | Note1 (10* CSSFinterRAT) | 
DRx cycle = 1.024 | Note1 (10* CSSFinterRAT) | Note1 (10* CSSFinterRAT)
DRx cycle = 1.28 | Note1 (8* CSSFinterRAT | Note1 (8* CSSFinterRAT)
1.28< DRX-cycle ≤10.24 | Note1 (20* CSSFinterRAT) | Note1 (20* CSSFinterRAT)
NOTE 1: The time depends on the DRX cycle length. NOTE 2: CSSFinterRAT is as defined in clause 9.4.3.2. |  | 

## Slide 11: Inter-RAT measurement
EUTRA-NR Inter-RAT measurement
  Cell re-selection requirements on EUTRA-NR inter-RAT in idle mode
DRX cycle length [s] | Tdetect,NR[s] (number of DRX cycles) | Tmeasure,NR[s] (number of DRX cycles) | Tevaluate,NR[s] (number of DRX cycles)
0.32 | 4.16 x M2 (13 x M2) | 0.64 x M3 (2 x M3) | 0.96 x M4 (3 x M4)
0.64 | 7.68 (12) | 1.28 (2) | 1.92 (3)
1.28 | 12.8(10) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)
Note 1: M2 = M3 = M4 = 1 when SMTC < =40, and M2 = 1.5, M3 = M4 = 2 when SMTC >40 |  |  | 
  Whether the introduction of per carrier flag will have impact on the higher priority measurement can be further checked in next meeting

## Slide 12: Inter-RAT measurement
EUTRA-NR Inter-RAT measurement
  NNR_carrier issue in the cell re-selection requirements on EUTRA-NR inter-RAT measurement taking the per inter-RAT carrier flag into account.
    The requirement for non-HST carrier = the requirement for HST carrier = NNR_carrier_HST * Tdetect, NR_HST + NNR_carrier_nonHST * Tdetect, NR_nonHST,
    Where:
      NNR_carrier is the total number of configured NR carriers,
      NNR_carrier = NNR_carrier_HST + NNR_carrier_nonHST,
      NNR_carrier_HST is the total number of configured high speed carriers,
      NNR_carrier_nonHST is the total number of configured non-high-speed carriers.
      Tdetect, NR_HST is the requirements specified for high speed scenario.
      Tdetect, NR_nonHST is the requirements specified for normal scenario.

## Slide 13: Inter-RAT measurement
Notation issue for CR on EUTRA-NR Inter-RAT measurement in idle mode
  For non-high-speed carriers
    NNR_carrier is used in the spec
  For high-speed carriers
    NNR_carrier_HST is used in the spec

## Slide 14: Inter-RAT measurement
EUTRA - NR Inter-RAT measurement
  Cell identification without DRX and cell identification with DRX in connected mode
DRX cycle | TPSS/SSS_sync_NR | TSSB_measurement_period_NR | TSSB_time_index_NR
No DRX | Max(600ms, 8 x max(MGRP, SMTC period))×Nfreq | Max(200ms, 8 x max(MGRP, SMTC period))×Nfreq | Max(120ms, 3 x max(MGRP, SMTC period)) ×Nfreq
DRX cycle < 320ms | Max(600ms, ceil( 8 × M) × max(MGRP, SMTC period, DRX cycle)) ×Nfreq | Max(200ms, ceil(8 × M) x max(MGRP, SMTC period, DRX cycle))×Nfreq | Max(120ms, ceil(3 × M) x max(MGRP, SMTC period, DRX cycle)) ×Nfreq
DRX cycle≥320ms | 8 × DRX cycle ×Nfreq | 4× M  DRX cycle ×Nfreq | [3] × DRX cycle ×Nfreq
Note 1: M = 1 when SMTC < =40, and M = 1.5 when SMTC >40 |  |  | 

## Slide 15: Release independent
Rel.16 NR HST RRM requirements can be release independent from Rel-15.
  Send LS to RAN2 to check with RAN2 whether “early implementation” approach is applicable for NR HST RRM enhancement
  If Rel.16 NR HST RRM requirements are release independent from Rel-15. The requirements are optional for Rel-15 UEs.

## Slide 16: Applicability of requirements
Non-HST RRM requirement applies to HST scenario when no corresponding HST RRM enhancement is specified.