## Slide 1: Way Forward on ultra-low BLER requirements
R4-2008805
Moderator (Ericsson)

## Slide 2: Agreements in first round
For the UE, MCS 14 is agreed
For the UE, antenna assumption is changed to 1x2, 1x4
UE applicability agreement: Requirements are applicable for UEs that support both MCS Table 3 (dl-64QAM-MCS-TableAlt) and CQI Table 3 (cqi-TableAlt).
BS TDD pattern: 3D1S1U (S=10:2:2) for 15kHz, 7D1S2U (S=6:4:4) for 30kHz
X is confirmed as 0.5dB for the UE and 1dB for the BS
For the BS, the test applicability rule means that either typeA mapping or typeB mapping is tested (depending on declaration) but not both.

## Slide 3: Agreements in second round
How to capture X in the UE specifications: X is captured in the RAN5 specification. “Extra Margin” EM needed to ensure that the RAN4 requirement is suitable to achieve 10^-5 is discussed and captured implicitly in the core specification as usual in RAN4.
How to capture in the BS specifications: Capture in the conformance specification by adding 1dB to test requirement and documenting as below. “Extra Margin” EM needed to ensure that the RAN4 requirement is suitable to achieve 10^-5 is discussed and captured implicitly in the core specification as usual in RAN4.
Test | Minimum Requirement in TS 38.104 [2] | Test Tolerance (TT) | Test requirement in the present document
8.2.X Performance requirements for PUSCH high reliability | SNRs as specified | 0.6 dB | Formula: SNR + TT + 1dB PUSCH false detection limit unchanged

## Slide 4: Agreements in the second round
Number of UE test cases for the FMCS requirement: 4 (FDD/2RX, FDD/4RX, TDD/2RX, TDD/4RX)
For UE, both TDD and FDD are tested with maximum supported RX

## Slide 5: Open issues
CQI requirement
Proposals
  Option 1: No CQI requirement
  Option 2: CQI requirement with median CQI and BLER with higher/lower CQI followed, together with test applicability rule on CQI/FMCS
Recommended WF
-> Keep it open, further check test feasibility for CQI reporting and make decision in Q3 2020.
-> If RAN4 can concluded test time is comparable to FMCS test cases, then RAN4 decide to introduce static CQI test case with ultra-low BLER
-> FFS whether we need to introduce test applicable rules among CQI/FMCS test cases if CQI test cases introduced
-> Companies also encourage to bring analysis whether static CQI/fading CQI test with non-ultra-BLER can serve test purpose
FR2 requirements
Proposals
  Option 1: FR2 requirements
  Option 2: No FR2 requirements
  Option 3: Defer decision to next meeting

## Slide 6: Open issues
Test applicability rule for FMCS and CQI
Only applicable if CQI test is introduced
Proposals
  Option 1: Introduce applicability rule
  Option 2: No rule; both tested
BS SCS test applicability
Proposals
  Option 1: All supported SCS tested
  Option 2: Only 15kHz SCS tested if both supported
  Option 3: Only 30kHz SCS tested if both supported

## Slide 7: Agreed simulation assumptions (UE)
Parameter |  | Value
Frequency range |  | FR1
Transform precoding |  | Disabled
Duplex mode |  | FDD/TDD
Antenna configuration |  | 1x2, ULA low 1x4, ULA low
PDSCH configuration | Mapping type | Type A
 | Starting symbol (S) | 2
 | Length (L) | 12
 | PUSCH aggregation factor | 1
PDSCH DMRS configuration | DMRS Type | Type 1
 | DM-RS duration | Single-symbol DM-RS
 | Number of additional DMRS | 1
Number of HARQ Transmissions |  | 1
PT-RS |  | Disabled
Propagation condition |  | AWGN
MCS Table |  | Table 3, MCS14
SCS and BW |  | FDD:15KHz, 10MHz TDD:30KHz, 40MHz
Frequency domain resource |  | Full BW
TDD pattern |  | 7D1S2U (S=6:4:4)
Testing metric |  | Target BLER: 10-5

## Slide 8: Agreed simulation assumptions (BS)
Parameter |  | Value
Frequency range |  | FR1
Transform precoding |  | Disabled
Antenna configuration |  | 1x2, ULA low
PUSCH configuration | Mapping type | Type A and Type B
 | Starting symbol (S) | 0
 | Length (L) | 14
 | PUSCH aggregation factor | 1
PUSCH DMRS configuration | DMRS Type | Type 1
 | DM-RS duration | Single-symbol DM-RS
 | Number of additional DMRS | 1
Number of HARQ Transmissions |  | 1
PT-RS |  | Disabled
Propagation condition |  | AWGN
MCS Table |  | Table 3, MCS 5
SCS and BW |  | 15 kHz for 10 MHz (see NOTE) 30 kHz for 40 MHz (See NOTE)
Frequency domain resource |  | Full Bandwidth
TDD pattern |  | 15 kHz SCS: 3D1S1U, S=10:2:2 30 kHz SCS: 7D1S2U, S=6:4:4
Testing metric |  | Target BLER: 10-5
NOTE: It was previously agreed to follow the decision for slot aggregation regarding supported bandwidths. Thus if decided for slot aggregation, then 5MHz should be added for 15k SCS and 10MHz for 30k SCS. Other parameters will remain the same in these cases.

## Slide 9: Agreements regarding testing
X is 0.5dB for UE and 1dB for BS
X is captured in the RAN5 specification for the UE and the conformance specification for the BS according to the agreements in slide 3.
The RAN5 statistical test methodology is assumed, adapted for CL = 99.999%