## Slide 1: WF on Rel-16 NR IAB demodulation requirements
3GPP TSG-RAN WG4 Meeting #96-e
Electronic Meeting, 17 – 28 Aug., 2020
Agenda: 7.4.5.1
draftR4-2012644
Document for: Approval
Nokia, Nokia Shanghai Bell,…

## Slide 2: Background
This is the first meeting, where NR_IAB_Demod is discussed.
The following chair guidance was given on the scope of the first meeting:
  Considering RF core still ongoing, well control scope for email discussion recommended to focus on work plan and overall performance impact.
Corresponding Email summary in RAN4#96-e
  R4-2012732 Email discussion summary for [96e][327] NR_IAB_Demod, RAN4#96-e.

## Slide 3: General

## Slide 4: General - Workplan
Issue 1-1-1: Workplan
  Option 1: Tentative workplan:
    RAN4#96-e:
      1. Discussion and initial agreement on work plan.
      2. Discussion on overall performance impact
    RAN4#97-e:
      1. Finish discussions on work plan and performance impact.
      2. Start discussions per physical backhaul channel.
      3. Start discussion on conformance test specification.
    RAN4#98:
      1. Continue discussions per physical backhaul channel.
      2. Simulation configuration alignments and FRC for backhaul channels.
      3. Development of conformance test specification.
    RAN4#98-bis:
      1. Finish discussions per physical backhaul channel.
      2. Simulation results collection and alignment.
    RAN4#99:
      1. Final round of simulation results collection and alignment.
      2. Draft CR frameworks for introducing IAB demodulation requirements.
    RAN4#100:
      1. CRs for TS 38.174 IAB demodulation performance requirements for backhaul links
      2. CRs for TS 38.xxx IAB demodulation performance tests for backhaul links
  Option 2: Postpone discussion on workplan, potentially until after RAN#89-e.
  Tentative agreement: option 2.

## Slide 5: General - Test specification
Issue 1-2-2: Working group to create and maintain the IAB demod conformance test specification
  RAN4 should create and maintain the complete IAB demod conformance test specification.
Issue 1-2-1: Is a new test specification required?
  Option 1: Yes.
  Option 3: Align with RF session.
  Option 4: A new conformance test specification is preferred by the Demod group. Come back to this discussion in case the RF group comes to a different conclusion.
  Tentative agreement: option 4.

## Slide 6: General - Subdivision of IAB demodulation topic
Issue 1-3-1: IAB-DU and IAB-MT topics in Rel-16
  Option 1: The topics are discussed in separate agenda items.
  Option 2: The topics are discussed in the same agenda item.
  Tentative agreement: option 1.

## Slide 7: General - General limitations in scope
Issue 1-4-2: Parent node, IAB node, child node
  Following WID, limit the scope of IAB Demod to only IAB-nodes, excluding the IAB-donor DU, and CU.
Issue 1-4-1: Backhaul and access links
  Option 1: Limit the scope of IAB Demod to UL and backhaul DL links.
  Option 3: One set of performance requirements for the IAB node, covering both MT and DU, with DU considering both access (from UEs) and backhaul (from parent). Specification section headings FFS. DU requirements are selective copy/paste from BS requirements, MT requirements need further discussion.
  Tentative agreement: Limit the scope of IAB demod to UL (access and backhaul) and DL (backhaul) links.

## Slide 8: IAB-DU

## Slide 9: IAB-DU - Test setup
Issue 2-1-1: New test setup
  Re-use the BS test setup for both OTA and conducted requirements, with IAB-MT functionality disabled during the test.

## Slide 10: IAB-DU - Requirement re-use
Issue 2-2-1: Define what “re-use” means in the context of BS demod requirements
  Clarification of terminology
    “Re-use”: Copy and paste the existing requirements, including all definitions, side-conditions, and SNR values.
    “Adapt”: Attempt to copy as much as possible of the existing requirement, but change a small number of parameters where needed (e.g. TDD pattern). The SNR value is not expected to change.
    “Follow the principle of”: Keep one or two characteristics of the existing requirement; e.g. channel model, MCS, number of requirements etc... In this case, it should be stated which principles are followed.
Issue 2-2-2: Re-use of BS demod requirements
  Option 1: Re-use BS demod requirements.
  Option 2: Re-use a strict subset of BS demod requirements, chosen based on IAB deployment scenario. Consider applicability rule to define reduced subset.
  Option 3: “Re-use”, i.e., copy paste, from BS demod requirements to the extent possible to avoid additional work. All conditions to be kept. For some cases “adapt” or “follow the principle of” may be needed.
  Tentative agreement: option 3.

## Slide 11: IAB-DU - Detailed scope of requirement re-use
Issue 2-3-6 (new): Detailed scope of BS demod requirement re-use
  Option 1: Requirement matrix. A matrix is made of all current requirements is to be created and then a decision made on which are applicable for IAB-DU and which are not.
  Option 2: Not is scope for this meeting.
  Recommended WF: All participants are invited to provide a first overview of requirements to re-use/adapt/follow the principle of, for the next meeting.

## Slide 12: IAB-DU - Additional requirements
Issue 2-4-1: Additional new DU demod requirements (w.r.t. BS demod re-use)
  Option 7: Not define any additional new DU demod requirements in Rel-16.
  Option 8: This issue requires more study.
  Tentative agreement: Preliminary evaluations indicate no need to define any additional new DU demod requirements in Rel-16.

## Slide 13: IAB-MT

## Slide 14: IAB-MT - Test setup
Issue 3-1-1: New test setup
  Option 1: Re-use the BS demod test setup for both OTA and conducted, with minimum required adaptation.
  Option 2: Design test setups by disabling IAB DU functionality during the test in order to reuse the existing UE performance requirements (demodulation and CSI) to verify IAB MT performance.

## Slide 15: IAB-MT - Test setup
Issue 3-1-2 Feasibility of BS demod based test setup:
  Evaluate for next meeting, if the BS demod based test setup is feasible to be applied to IAB-MT testing.
    I.e., is one way or two-way connection needed?
    I.e., "full link setup" vs. "test mode and digital feedback" vs. other solutions.
Issue 3-1-3 Feasibility of BS demod based test setup:
  Evaluate for next meeting, if/how it is possible to reduce the UE demod based test and test setup complexity, when applied to IAB-MT testing.

## Slide 16: IAB-MT - Requirement re-use
Issue 3-2-1: Define what “re-use” means in the context of UE demod requirements
  Clarification of terminology
    “Re-use”: Copy and paste the existing requirements, including all definitions, side-conditions, and SNR values.
    “Adapt”: Attempt to copy as much as possible of the existing requirement, but change a small number of parameters where needed (e.g. TDD pattern). The SNR value is not expected to change.
    “Follow the principle of”: Keep one or two characteristics of the existing requirement; e.g. channel model, MCS, number of requirements etc... In this case, it should be stated which principles are followed.

## Slide 17: IAB-MT - Requirement re-use
Issue 3-2-1: Define what “re-use” means in the context of UE demod requirements
  Option 1: “Re-use”, i.e., copy paste.
  Option 3: “Follow the principle of”.
  Proposed WF: Postpone discussion until the IAB-MT test setup has become clearer.
Issue 3-2-2: Form of MT demodulation requirements
  Option 1: Specify IAB-MT FRCs using the BS spec approach (i.e. single slot FRCs that are applicable for any TDD pattern).
  Option 3: UE test definition should be followed as much as possible.
  Proposed WF: Postpone discussion until the IAB-MT test setup has become clearer.

## Slide 18: IAB-MT - Requirement re-use
Issue 3-2-3: Re-use of UE demod requirements
  Option 2: Apply the UE performance requirements for IAB MT, which are based on the mandatory features for it.
  Option 3: Re-use a strict subset of UE demod requirements, chosen based on IAB deployment scenario (especially very low mobility).
  Option 4: Follow the principle of UE demod requirements pertaining to DL backhaul links, but modify the FRC and test setup to align with the single slot and error free feedback principles of BS demod requirements testing.
  Option 5: More discussion is needed on which requirements to take and adapt.
  Proposed WF: Postpone discussion until the IAB-MT test setup has become clearer. Please also evaluate how requirement re-use would look exactly under different test setups.

## Slide 19: IAB-MT - Detailed scope of requirement re-use
Issue 3-3-2 (new): Detailed scope of UE demod requirement re-use
  Option 1: Requirement matrix. A matrix is made of all current requirements is to be created and then a decision made on which are applicable for IAB-MT and which are not.
  Option 2: Not is scope for this meeting.
  Recommended WF: All participants are invited to provide a first overview of requirements to re-use/adapt/follow the principle of, for the next meeting.

## Slide 20: IAB-MT - Additional requirements
Issue 3-4-1: Additional new MT demod requirements (w.r.t. UE demod re-use)
  Option 5: Not define any additional new MT demod requirements in Rel-16.
  Option 6: We do not need demod tests for these requirements or any kind of “joing testing” of demod+RRM.
  Option 7: This issue requires more study.
  Tentative agreement: Option 7.

## Slide 21: IAB-MT - Wide area and local area IAB-MT nodes
Issue 3-5-1: Distinction of wide area and local area IAB-MT
  Differentiate the IAB-MT performance requirements between the wide area class and local area class, if/where needed. FFS if/where needed.