## Slide 1: WF On inter-band CA and UE BM type
Qualcomm
R4-2006918
3GPP TSG-RAN WG4 Meeting #97-e
Online Meeting, Nov 2020
Agenda: 12.3.2.1.2, 12.3.2.1.3, 12.3.2.2.1, 12.3.2.2.2
Email Thread: #136

## Slide 2: Background
This WF captures agreeable outcome of discussion in Email discussion summary for [97e][136] NR_RF_FR2_req_enh2_Part_2

## Slide 3: WF on IBM for DL CA between bands in the same frequency group
Typical inter-band CA deployment between bands in the same frequency group cannot be limited to co-located deployments
IBM UEs are implementable
Feasibility to support is left to UE vendor choice
Companies are encouraged to evaluate requirements based on non-co-located test cases

## Slide 4: WF on CBM for DL CA for bands across different frequency groups
RF requirements will be set assuming co-location of both bands
Companies are encouraged to provide input:
  Regarding MRTD, beam switch can also be carried out when there is no DL data scheduled on one of the CCs and in the U-D switch. How often is BM carried out in relation to expected changes in the channel conditions?
  What is the impact on the DL throughput due to PDCCH interruptions in case of non-co-location and an MRTD up to 3 us?
  What is the time needed for beam switch (typically)?

## Slide 5: WF on inter-band UL CA
RAN4 shall put off development of inter-band UL CA requirements until there is a clear or urgent demand for this feature
For the case of simultaneous uplink in multiple bands, companies are encouraged to study:
  max TRP and max EIRP limit requirements
  Power sharing between bands if applicable (configured power)
  Emissions requirements
  P-MPR and PHR