## Slide 1
3GPP TSG-RAN WG4 Meeting # 98-e R4-2100103
Electronic Meeting, 25th January– 5th Febuary, 2021
Motivation for new WI on PC1.5 for NR band n79
CMCC

## Slide 2: Justification
RAN4 has completed PC1.5 HPUE feature to improve the uplink coverage for 5G SA deployments on NR bands n41. NR Band n79 with frequency range 4400-5000MHz is an NR TDD band, 5G NR UE may use a larger transmission bandwidth, if increase bandwidth but not increase the UE transmission power, power spectral density will reduce, and the uplink coverage will be reduced.
It is more urgent need to increase the UE output power for n79 in order to guarantee uplink coverage. It is proposed to specify Power Class 1.5 UE for NR band n79 supporting +29 dBm. This Work Item is to develop a new feature to enable HPUE (power class 3) for NR band n79.

## Slide 3: Objective
Objective of Core and performance part WI
The core objectives of the WI are:
Introduction of high power UE (power class 1.5) NR band n79 to enable single component carrier UL operation for SA NR operation.
Specify RF characteristics for n79 (dual-PA)), including UE maximum output power, Tx power tolerance and UL-MIMO for PC1.5 n79.
Reuse existing SAR mechanism for PC1.5 n79,
Release independent issue is to be considered for PC1.5 n79
The performance objectives of the WI are:
Release independence requirements if needed (TS 38.307)

## Slide 4
Thanks!