## Slide 1: Way Forward on NR TxD & Power Class
vivo
3GPP TSG-RAN WG4 Meeting # #98-bis-e
Electronic Meeting, Apr. 12 -20, 2021
R4-210xxxx

## Slide 2: CR related - EVM
Proposals:
  Option 1: As in agreed WF R4-2008465
  Option 2: As in R4-2107369:
  Option 3: RAN4 considers to update the endorsed draft CR for UL Tx diversity EVM measurement method with the method presented in R4-2107112. (R&S)
      Agreements(GTW):
  Option 2
  For UL MIMO, Option 3 or options along those lines can be further considered. Once a solution is agreed, RAN4 can discuss from which release onwards it applies

## Slide 3: CR related - MPR
Proposals:
  Option 1: As in last meeting’s Endorsed CR R4-2107307
  Option 2: Base on the proposals in R4-2104538
    1.5dB offset for Edge and outer, 0.5dB offset for inner compared to 1Tx
  Option 3: Reconsider separating MPR requirements for UL-MIMO and TxD
    Also consider A-MPR impact in next issue and as in R4-2107283
  Option 4: Keep the same MPR with 1Tx
  Option 5: Other solution
      Agreements (GTW) :
  RAN4 to start a evaluation campaign to derive the MPR values for both UL-MIMO and TxD, with agreed evaluation assumptions and UE implementations. Decisions will be made in the May meeting

## Slide 4: CR related - A-MPR
Proposals
  Option 1: A-MPR as band specific requirements could be decoupled from the general TxD requirements
  Option 2: Keeping the agreement of applying same MPR for UL MIMO and Tx Diversity would mean changed to the UL MIMO AMPR, too.
      Agreements:
  Postpone the discussion and treat MPR first

## Slide 5: Other Issues - Relation with SRS antenna switching
Proposals
  Option 1: UE that supports transparent TxD can have antenna switching SRS configured in the same band.
    Option 1a. The ∆TRxSRS needs to be increased by 3 dB overall except for the PC2 case which accommodates the use of PA with 3 dB lower power for SRS antenna switching.
    Option 1b. Other solutions or requirements.
  Option 2: UE that supports transparent TxD can not have antenna switching SRS configured in the same band.
      Agreements:
  Option 1
  Further confirm SRS
    Requirements based on transmission from physical antenna connector and not by transparent TxD
  Detailed requirements FFS

## Slide 6: Other Issues - Concept clarification for TxD
Background: There are following concept:
    Concept 1: TxD
    Concept 2: Transparent TxD
    Concept 3: One layer 2 port configuration with full power transmission: mode 0/1/2
  Tentative understanding: Concept 3 is defined in UL-MIMO scope, while current definition work for TxD is actually for transparent TxD. Concept 1 is one general concept including 2/3.
Proposals
  Discuss whether the tentative understanding is correct or not.
Agreements
  Further discuss the concept of TxD / Transparent TxD
    Note: May used for requirements definition / applicability Etc.

## Slide 7: Other Issues - Relation with full power capability
Proposals
  Option 1: UEs can support only one of full power capability and transparent TxD capability in a given band.
  Option 2: No restriction related to full power capability.
      Agreements :
  FFS

## Slide 8: Other Issues - TxD antenna and channel models
Proposals
  Option 1: Further discuss the relevant antenna and channel models and their impact as part of, and prior to, concluding on conformance testing methodologies and reference receivers for TxD with conducted measurements.
  Option 2: No more discussion on these issues.
      Agreements :
  FFS

## Slide 9: Rel-15 NSA power class
Proposals
  Option 1: The Pcmax for NR is modified according to the declared NR power capability for NSA so that the PHR becomes correct. (Ericsson)
  Option 2: The Pcmax for NR is modified to use the lower possible power class to decide the lower bound of the configured power. (Huawei)
  Option 3: Reusing the IE dualPA-Architecture to distinguish the two cases where the NR parts has PC2 or PC3 in PC2 EN-DC mode. (ZTE)
  Option 4: Wait for feedback from Ran2 or wait for ran2 to conclude the work to add TX diversity capability and conclusion on applicable release. (Qualcomm)
  Option 5: Others
Agreements
  Option 4