## Slide 1: WF on SAR solutions for PC2 NR inter-band CA and SUL configurations
China Telecom
R4-2105341
3GPP TSG-RAN WG4 Meeting # 98-bis-e
Electronic Meeting, Apr. 12-20, 2021
Agenda: 7.19.1

## Slide 2: Background
The contributions submitted in RAN4 #98e meeting for SAR solutions:
  R4-2104527, Discussion on PC2 inter-band NR CA, vivo
  R4-2104572, Exploiting full potential of UE Tx power, Nokia Japan
  R4-2105085, More on methods for faciliating SAR compliance for inter-band UL CA, Ericsson
  R4-2105086, Higher BC power class for UL CA, Ericsson
  R4-2106275, Further discussion on SAR schemes for UE power class 2 NR inter-band CA with 2UL, China Telecom
  R4-2106276, Further discussion on SAR schemes for UE power class 2 NR SUL configurations, China Telecom
  R4-2106363, Further discussion on SAR solution for NR PC2 inter-band CA, ZTE Corporation
  R4-2106541, Discussion on SAR issue for HP UE inter-band UL CA, Xiaomi
  R4-2106557, R17 Discussion on UE power class high limit, OPPO
  R4-2106559, R17 Inter band CA HPUE, OPPO
  R4-2106905, Power class consideration for NR inter-band UL CA, Apple

## Slide 3: WF on SAR solutions
Duty Cycle based solutions
  Report the total duty cycle capability per band combination with SARratio factor consideration and not need to report SARratio
    The Dutycycle threshold calculation procedure is based on formula (1), which is to be specified in the spec.
      DutyNR, x *( PNR,x/ P26)*SARratioNR, x + DutyNR, y *(PNR, y/ P26)* [SARratioNR, y ] ≤ Duty threshold (1)
    How to define the SARratio will be further discussed, considering but not limit to the following options
      Option 1: The SARratio calculation formula (2) could be a reference
      [Formula (2): SARratioNR, x = 50%/DutycycleNR, x ; SARratioNR, y = 50%/DutycycleNR, y]
      Option 2: Depend on UE implementation
“Blind scheme” solution can be discussed further