## Slide 1: WF on the introduction of band n85
Ericsson
R4-2105372
3GPP TSG-RAN WG4 Meeting # 98-bis-e
Electronic Meeting, April 12-20, 2021

## Slide 2: Band n85 – WF scope
In RAN4#98-e meeting, a WF (R4-2103219) listing all TS 38.104 and TS 38.101-1 impacts was agreed.
The n85 WID was updated, adding 15 MHz channel BW support for consistency with band n12.
This WF is listing the additional changes to R4-2103219 required for this WID update.

## Slide 3: Band n85 - System parameters agreement
Supported channel BWs
NR band / SCS / BS channel bandwidth |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NR Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 70 MHz | 80 MHz | 90 MHz | 100 MHz
 | 15 | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  | 
n85 | 30 |  | Yes | Yes |  |  |  |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 4: Band n85 – UE Rx requirements agreement
REFSENS
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NR Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 70 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode
n85 | 15 | -97.0 | -93.8 | -84.0 |  |  |  |  |  |  |  |  |  |  | FDD
 | 30 |  | -94.1 | -84.1 |  |  |  |  |  |  |  |  |  |  | 
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NR Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 70 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode
n85 | 15 | 20 | 20 | 20 |  |  |  |  |  |  |  |  |  |  | FDD
 | 30 |  | 10 | 10 |  |  |  |  |  |  |  |  |  |  | 

## Slide 5: References
R4-2103219, WF on the introduction of band n85, Ericsson
R4-2106895, New NR band n85 - BS RF additional impacts, Ericsson
R4-2106896, New NR band n85 - UE RF additional impacts, Ericsson
R4-2105190, Email discussion summary for [98-bis-e][117] NR_n67_n85_NWM, Moderator (Ericsson)