## Slide 1: Way forward on Inter-band UL CA
RAN4#98-Bis-e R4-2105393
e-Meeting, Apr. 12-20, 2021
Samsung, Nokia

## Slide 2: Applicability
Agreement:
  According to latest WID RP-210914, in Rel-17 FR2 RF enhancement, specify requirements for inter-band UL CA for two bands between different frequency groups based on IBM

## Slide 3: Max EIRP
Options
  Option 1: per UE
  Option 2: per band with max EIRP limit of each band set to 43 dBm (PC3/PC4) and 55 dBm (PC1).
  Option 3: per band but the max EIRP limit for overlapping bands where the UL of both bands are in the over lapping region needs to be discussed further.
Issues
  Regulation requirements dependent
  Whether an aligned approach applies for L+H, L+L, H+H band combinations
  Whether an aligned approach applies for max EIRP and min peak EIRP
Agreement:
  For current scope, i.e., IBM between different frequency group, down-select from option 1 and option 2 in RAN4#99 meeting

## Slide 4: Min peak EIRP
Options
  Option 1: per band with relaxed requirement compared to single-CC, i.e., n257=22.4-X dBm, n259=18.7-Y dBm. The value of relaxation (e.g., X, Y) can equal the MBR.
  Option 2: per band with 3dB relaxed requirement compared to single-CC
  Option 3 (revision of option 1): per band with relaxed requirement compared to single-CC, i.e., n257=22.4-X dBm, n259=18.7-Y dBm, value of X and Y for FFS)
    Option 3-1: X and Y is 2.5dB
    Option 3-2: X and Y is 3dB + MBR
    Option 3-3: X and Y FFS
Issues
  How to define the relaxation value X and Y, especially how to handle MBR
  Whether min peak EIRP for two bands achieved simultaneously at the same direction
Agreement:
  per band with relaxed requirement compared to single-CC, i.e., n257=22.4-X dBm, n259=18.7-Y dBm, value of X and Y for FFS

## Slide 5: Spherical coverage
Options
  Option 1: EIRP spherical coverage requirement is specified per band, while allowing the relaxation per CA band combination.
  Option 2: EIRP spherical coverage requirement is specified per band, while allowing 3 dB relaxation per band.
  Option 3: Other
    Option 3-1: relaxation as 2.5dB
    Option 3-2: relaxation as 3dB + MBR
Issues
  Whether common spherical coverage shall be the baseline as downlink CA
  Dependent on the agreement for min peak EIRP
Agreement:
  Common spherical coverage requirement shall be defined for inter-band UL CA as that in downlink CA
  EIRP spherical coverage requirement is specified per band rather than per UE, while the relaxation value per CA band combination is FFS.

## Slide 6: Reference
R4-2105203 Email discussion summary for [98-bis-e][130] NR_RF_FR2_req_enh2_Part_1, Moderator (Nokia)