## Slide 1: WF on further RRM enhancement for NR and MR-DC – Handover with PSCell
Apple, …
R4-2105787
3GPP TSG-RAN4 Meeting #98bis-e
Online, 12 – 20 April, 2021
Agenda item: 8.4
Document for: Approval
Agreement in 1st round
Agreement in GTW (Apr. 16th)
Agreement in 2nd round

## Slide 2: Sub-topic 2-1 Scenarios for RRM requirement of HO with PSCell (1/2)
Issue 2-1-1: Scenarios for RRM requirement of HO with PSCell
  FFS
    Option 1(Apple, HW, QC, OPPO, Xiaomi, vivo, CATT, MTK, Ericsson): RAN4 specifies RRM requirement for HO with PSCell for following scenarios:
      from NR SA to EN-DC
      from EN-DC to EN-DC
      from NE-DC to NE-DC
      from NR-DC to NR-DC
    Option 2(NEC, Nokia): RAN4 specifies RRM requirement for HO with PSCell for following scenarios:
      from NR SA to EN-DC
      from EN-DC to EN-DC
      from NE-DC to NE-DC
      from NR-DC to NR-DC
      from NR SA to NE-DC (newly added)
      from NR SA to NR-DC (newly added)
      from LTE SA to EN-DC (newly added)
    Option 3(MTK): RAN4 specifies RRM requirement for HO with PSCell for following scenarios:
      from NR SA to EN-DC
      from EN-DC to EN-DC
      from NE-DC to NE-DC
      from NR-DC to NR-DC
      And RAN4 to clarify whether requirements from LTE-SA to EN-DC and from NR-SA to NR-DC are needed

## Slide 3: Sub-topic 2-1 Scenarios for RRM requirement of HO with PSCell (2/2)
Issue 2-1-2: NR-DC and NE-DC mode in HO with PSCell
  FFS:
    Option 1(CATT, Apple, OPPO, MTK, Huawei): In R17 RAN4 only considers:
      FR1+FR2 NR-DC for HO with PSCell from NR-DC to NR-DC,
      FR1+LTE NE-DC for HO with PSCell from NE-DC to NE-DC.
    Option 2 (NEC, Intel, vivo, QC, Ericsson, MTK):
      FR1+FR2 NR-DC and FR1+FR1 NR-DC for HO with PSCell from NR-DC to NR-DC,
      FR1+LTE NE-DC for HO with PSCell from NE-DC to NE-DC.
    Option 2a (Apple):
      FR1+FR2 NR-DC and FR1+FR1 NR-DC for HO with PSCell from NR-DC to NR-DC,
      FR1+LTE NE-DC for HO with PSCell from NE-DC to NE-DC.
      Note: the baseline PSCell addition requirement for FR1+FR1 NR-DC would be discussed in TEI16.
    Option 3 (Ericsson):
      FR1+FR2 NR-DC and FR1+FR1 NR-DC for HO with PSCell from NR-DC to NR-DC,
      FR1+LTE NE-DC for HO with PSCell from NE-DC to NE-DC,
      FFS on FR2+LTE NE-DC for HO with PSCell from NE-DC to NE-DC.
    Option 4 (Nokia):
      FR1+FR2 NR-DC and FR1+FR1 NR-DC for HO with PSCell from NR-DC to NR-DC,
      FR1+LTE and FR2+LTE NE-DC for HO with PSCell from NE-DC to NE-DC,
      FR1+LTE and FR2+LTE NE-DC for HO with PSCell from NR SA to NE-DC.

## Slide 4: Sub-topic 2-2 Delay requirement design of HO with PSCell (1/6)
Issue 2-2-1: timeline for HO with PSCell
  Agreements:
    Timeline for HO with PSCell
      Option 1 (Xiaomi, Apple, OPPO): PCell HO and PSCell addition is performed in a sequential order.
      Option 2 (CATT, CMCC, Huawei, MTK, QC, ZTE, NEC, Ericsson): PCell HO and PSCell addition is performed in parallel.
      Option 3 (NTT DOCOMO, Intel, OPPO, Nokia, Ericsson, NEC): Some of procedures of HO with PSCell should be able to be performed in parallel, but RACH processing is performed in a sequential order (RACH procedure of PSCell will happen after the RACH procedure of PCell).
      Other options are not precluded
    Send LS to RAN2 to clarify possible restrictions on parallel or sequential RACH processing from RAN2 perspective
Issue 2-2-2: starting point of the delay requirement for HO with PSCell
  Agreement
    For delay requirement of HO with PSCell, the starting point is the end of the last TTI containing the RRC command of handover with PSCell.

## Slide 5: Sub-topic 2-2 Delay requirement design of HO with PSCell (2/6)
Issue 2-2-3: ending point of the delay requirement for HO with PSCell
  FFS:
    Option 1 (Xiaomi, Intel, ZTE, Nokia):
      When the UE shall be capable to transmit PRACH preamble towards target PSCell within Thandover_with_PSCell from the end of the last TTI containing the RRC command implying handover with PSCell. Where Thandover_with_PSCell is the delay requirement of HO with PSCell.
    Option 2 (CATT, CMCC, OPPO, QC, Ericsson, MTK, NEC):
      the later timing between “timing when UE shall be capable to transmit PRACH preamble towards target PCell” and “the timing when UE shall be capable to transmit PRACH preamble towards target PSCell”
    Option 2a (Ericsson):
      the later timing between “timing when UE shall be capable to transmit PRACH preamble towards target Pcell” and “the timing when UE shall be capable to transmit PRACH preamble towards target PSCell”
      In case RAN4 defines scenarios where PRACH preamble transmission towards PSCell is not needed, ending point for those scenarios is PRACH preamble transmission towards Pcell.
    Option 3 (Apple, OPPO):
      if sequential processing is used, the timing when UE shall be capable to transmit PRACH preamble towards target PSCell
      if the parallel processing is used, the later timing between “timing when UE shall be capable to transmit PRACH preamble towards target Pcell” and “the timing when UE shall be capable to transmit PRACH preamble towards target PSCell”
    Option 4 (HW, vivo, ZTE, CMCC, Ericsson, QC, NEC, MTK):
      Define delay requirements for HO and PSCell addition/change separately with the ending points defined as Pcell PRACH and PSCell PRACH respectively. No need to define overall delay requirement.

## Slide 6: Sub-topic 2-2 Delay requirement design of HO with PSCell (3/6)
Issue 2-2-4: checking point of the delay requirement for HO with PSCell
  Agreement: This issue is closed and focus on issue 2-2-3
    Issue 2-2-5: optimisation for the case when PSCell is not changed during HO with PSCell
      Option 1(Xiaomi, CATT, Apple, OPPO, vivo, QC, HW, Intel, MTK, NEC, DCM, ZTE): For UE which is already configured with DC, the UE’s behaviour is same when the configured PSCell is same as the original one or not.
      Option 2 (Ericsson, Nokia, NEC): When source and target PSCell is the same cell, then fine time tracking T∆=0 shall apply.
    Issue 2-2-6: RRC processing delay for HO with PSCell
      Agreement: RAN4 waits for the reply LS from RAN2 on RRC processing delay for HO with PSCell

## Slide 7: Sub-topic 2-2 Delay requirement design of HO with PSCell (4/6)
Issue 2-2-7: UE SW processing and RF warm-up(if needed) time for HO with PSCell
  FFS:
    Option 1 (CATT): Tprocessing for HO with PSCell can be used the values for handover requirements and for PSCell addition requirement
    Option 2 (Apple):
      If UE only supports sequential processing for HO with PSCell, the total UE processing time for HO with PSCell is the sum of UE processing timing of HO and UE processing timing of PSCell addition.
      If UE can support parallel processing for HO with PSCell, the total UE processing time for HO with PSCell could be the maximum one between UE processing timing of HO and UE processing timing of PSCell addition
UE processing margin (Tprocessing) | Target PCell and PSCell is in the same FR as old PCell | Target PCell and/or target PSCell is in the different FR from old PCell
Sequential processing capable UE | 40ms | 60ms
Parallel processing capable UE | 20ms | 40ms

## Slide 8: Sub-topic 2-2 Delay requirement design of HO with PSCell (5/6)
Cont. from last slide:
  FFS:
    Option 3 (NEC, Huawei):
      Tprocessing is the UE processing time. Tprocessing is the maximum value of PCell HO and PSCell addition;
    Option 4 (Intel):
      For HO with PSCell from NR-DC to NR-DC, Tprocessing can be split into software processing (Tprocessing_SW) and RF warm up time(Tprocessing_RF). Tprocessing_SW=[20]ms needs further discussion if some extension is needed. Tprocessing_RF will be dependent on different scenarios, i.e. whether PCell or PSCell change across FRs.
      For HO with PSCell from NR SA to EN-DC, Tprocessing only includes software processing time (Tprocessing_SW). Tprocessing_SW=[20]ms needs further discussion if some extension is needed.
    Option 5 (Ericsson):
      The value of Tprocessing_SW for PSCell is as follows:
        Tprocessing_SW_PSCell = 0 ms, when source and target PSCells are the same cell,
        Tprocessing_SW_PSCell = 20 ms, when source and target PSCells are different cells but in same FR
        Tprocessing_SW_PSCell = 40 ms, when source and target PSCells are different cells in different FRs
      How Tprocessing_SW_PSCell impacts the handover with PSCell timeline depends on assumptions on parallel or sequential processing.
    Option 6 (vivo): RF chain activation and retuning time needs to be considered in the timeline of HO with PSCell.
    Option 7 (QC, MTK):
      Extending the UE processing time for NRSA to EN-DC joint handover by [FFS]ms and [FFS] can be 10ms as the starting point, i.e. Tprocessing = [30]ms.
      For NRDC to NRDC, the UE processing time to be 20ms without FR mode switch on PSCell; otherwise, the UE processing time shall be 40ms as the legacy PSCell change requirement.
        For NRDC to NRDC, only consider FR1 for PCell.

## Slide 9: Sub-topic 2-2 Delay requirement design of HO with PSCell (6/6)
Issue 2-2-8: Delay requirement design if sequential processing is assumed (from issue 2-2-1)
  Up to the conclusion from issue 2-2-1 and other issues. The options could be found in section 2.2.2 issue 2-2-8 in R4-2105818
Issue 2-2-9: Delay requirement design if parallel processing is assumed (from issue 2-2-1)
  Up to the conclusion from issue 2-2-1 and other issues. The options could be found in section 2.2.2 issue 2-2-9 in R4-2105818

## Slide 10: Sub-topic 2-3 Interruption requirement design of HO with PSCell
Issue 2-3-1: whether or not RAN4 assumes PCC could be scheduled for UE when PCell HO is completed but PSCell addition is not completed
  FFS:
    Option 1 (Apple, QC, vivo, CMCC, Ericsson, Nokia, MTK, NEC, Xiaomi, CATT, Intel, HW): Yes
    Option 2 (OPPO): No.
Issue 2-3-2: Interruption requirement for HO with PSCell
  FFS:
    Option 1 (Xiaomi, HW, vivo, QC, ZTE, DOCOMO, CATT): No interruption requirement should be defined during HO with PSCell
    Option 2 (CATT): Interruption in legacy handover delay requirement can be applied for PCell. No interruption is defined on PSCell.
    Option 3 (Apple):
      If sequential processing is used for HO with PSCell, UE would have an interruption on new PCell due to the PSCell addition.
      If parallel processing is used for HO with PSCell and PSCell addition is completed earlier than PCell HO, no need to define interruption requirement since interruption has been reflected by HO delay.
      If parallel processing is used for HO with PSCell and PSCell addition is completed later than PCell HO, UE may have an interruption on new PCell due to RF tuning for PSCell addition.
    Option 4 (ZTE): For interruption requirements, consider the following options:
      Specify a total interruption for handover and PSCell addition
      Specify separate interruptions for handover and PSCell addition.
    Option 5 (MTK): RAN4 to specify the PCell interruption time for the overall HO with PSCell procedure.

## Slide 11: Sub-topic 2-4 Generic RACH assumption for HO with PSCell (1/2)
Issue 2-4-1: 2 step and 4 step RACH for HO with PSCell
  FFS:
    Option 1 (CATT, QC, Ericsson(if parallel is agreed)): The delay requirements for HO with PSCell are not relative with 2 step or 4 step RACH if the ending point of delay is defined as PRACH transmission of UE.
    Option 2 (Apple, vivo, OPPO, Xiaomi, MTK, Intel): for requirement of HO with PSCell, RAN4 starts the discussion with 4 step RACH first and FFS on 2 step RACH.
    Option 3 (NEC, Ericsson, ZTE, Nokia, Apple): RAN4 to define both 2-step and 4-step RACH requirements for handover with PSCell.
Issue 2-4-2: RACH occasion collision between Pcell and PSCell
  FFS:
    Option 1 (CATT, Nokia): There is no need to further consider the RO collision issue from RAN4’s perspective.
    Option 2 (Apple, OPPO(support sequential part), HW(support 2nd bullet), MTK(support 2nd bullet), QC(support 2nd bullet)):
      If sequential processing is used, there is no need to consider RACH occasion (RO) collision between PCell and PSCell.
      If parallel processing is used:
        for FR1+FR1 EN-DC, an additional uncertainty delay due to PSCell RACH collision with PCell UL channels may be introduced if the PSCell RACH cannot be transmitted based on the criteria in TS38.213 section 7.6.1;
        for FR1+FR1 NE-DC, an additional uncertainty delay due to PCell RACH collision with PSCell RACH may be introduced if the PCell RACH cannot be transmitted based on the criteria in TS38.213 section 7.6.2;
        otherwise, if the PCell and PSCell are on the different FRs, no need to consider RO collision issue.
    Option 3 (NEC):
      RAN4 to agree that components that contribute to TIU delay are the TA acquisition delay in Pcell, delay uncertainty in acquiring resources for RRC connection Reconfiguration Complete message on Pcell and PRACH acquisition uncertainty delay in PSCell.
      RAN4 to agree that interruption uncertainty (TIU) for Pcell and PSCell is sequential process.
    Option 4 (vivo): PRACH occasion collision is considered as one factor in the requirements for HO with PSCell, if UE only supports single uplink in the NE-DC or EN-DC.
    Option 5 (MTK): For the scenario from NE-DC to NE-DC, RAN4 to clarify whether to remove the delay uncertainty of Pcell PRACH preamble transmission from the delay requirement of HO with PSCell procedure.

## Slide 12: Sub-topic 2-4 Generic RACH assumption for HO with PSCell (2/2)
Issue 2-4-3: RACH occasion on NR-U CC for HO with PSCell
  FFS:
    Option 1 (Ericsson): RAN4 to further study whether RA for spCell on unlicensed carrier with CCA shall be prioritized over RA for spCell on licensed carrier, once CCA is successful.
    Option 2 (Apple, QC, OPPO, HW, vivo, DCM, CATT, MTK, Nokia): The NR-U scenario is out of scope of this WID, no need to discuss.

## Slide 13: Sub-topic 2-5 Others
Issue 2-5: Failure case definition for HO with PSCell
  Agreement: RAN4 waits for the reply LS from RAN2 before any decision