## Slide 1: WF on NR UE Power Saving Enhancements (All agreements in RAN4#98-bis-e in email thread #224)
MediaTek, vivo
3GPP TSG-RAN WG4 Meeting #98-bis-e R4-2105797
Electronic Meeting, 12th – 20th April, 2021
Agenda Items: 8.9

## Slide 2: Evaluation assumption
Issue 2-1-2: assumption on other RRM measurement
Background for information: The guidance from RP-91-e,
  “For Rel-17 WI of UE power saving enhancements for NR, no specification impact to RRM measurement procedure requirements and measurement performance requirements is expected.“
Issue 2-1-3: Impact on PDCCH monitoring
RAN4 shall assess the interaction between PDCCH relaxation (as being discussed in RAN1) and RLM/BM relaxation (as being discussed in RAN4) from power consumption perspective once there is more progress in RAN1 on PDCCH relaxation.

## Slide 3: Feasible scenarios for relaxation
RAN4 conclude the feasible scenario and will define the RLM/BFD requirements for R17 UE measurements relaxation for RLM and/or BFD in work phase for the following cases,
  Case 1: SSB based RLM/BFD measurement relaxation in FR1
  Case 2: CSI-RS based RLM/BFD measurement relaxation in FR1
  Case 3: CSI-RS based RLM/BFD measurement relaxation in FR2
  Case 4: SSB based RLM/BFD measurement relaxation in FR2
  Note: UE is allowed but not mandatory to perform relaxed RLM/BFD measurements when the relaxation criteria is met in above feasible scenarios.
  For the feasible cases with positive power saving gain
    Option 1: When defining relaxation requirement, RAN4 should consider the maximum additional delay of RLF declaration within a confidence level due to power saving, i.e., the probability of maximum additional delay within x is larger than y, for power saving evaluation on different schemes.
  further considerations as bellows are considered
    Option 1: Negative system level impact due to RLM/BFD relaxation should be minimized
    Option 2: RAN4 can further discuss whether the beneficial scenario is a reasonable case for network configuration.

## Slide 4
Issue 2-2-6: DRX cycle applicability
Relaxation is applicable for DRX<=80ms.
  FFS adjustment to other DRx cycles is needed to keep the monotonicity of DRx cycles w.r.t. evaluation time
  FFS Maximum relaxation factor should be related to DRX cycle and RS periodicity.
Issue 2-2-7: Potential spec impact
  The spec impact of R17 power saving will be discussed in the work phase.

## Slide 5: Relaxation criteria
Issue 2-3-1: Criteria of RLM/BFD relaxation – General
whether relaxed RLM/BFD requirements can be applied depends on both the serving cell quality and UE mobility state
FFS the precise and robust metric for serving cell quality and UE mobility state
Issue 2-3-2/2-3-3/2-3-4: Good serving cell quality criteria of RLM/BFD relaxation
Good serving cell quality criteria of RLM/BFD relaxation is defined as the radio link quality is better than a threshold.
  FFS radio link quality > Qout + X (dB) for RLM
  FFS radio link quality > Qout,LR + Y (dB) for BFD relaxation.
  FFS how to derive the values of X, Y
The radio link quality in good serving cell quality criteria for R17 RLM/BFD relaxation is based on SINR
  FFS how to derive the corresponding SINR level of the threshold used in good serving cell quality criteria
  FFS which SINR is used
    Option 1: Reuse SINR for RLM/BFD evaluation
  FFS whether RSRP is also needed for BFD as additional condition
FFS: The thresholds are configured or pre-defined.
  FFS: Different threshold configuration (i.e. different IEs in RRC signaling )for SSB based and CSI-RS based RLM/BFD is allowed

## Slide 6: Relaxation factors
FFS on following:
  Option 1: Evaluation period based on fixed sample number
    The relaxation factor is implicitly defined, similar to the beam sweeping factor implicitly defined in FR2 RRM measurement requirements.
  Option 2: Evaluation period scaling with the relaxation factor
    The relaxation factor is explicitly defined
    FFS whether Different relaxation factors between FR1 and FR2
    FFS whether Different relaxation factors for different SINR range
    FFS whether Different relaxation factors for SSB and CSI-RS
    FFS What UE speed is used as reference for derving the relaxation factor
  Option 3: Up to UE implementation as long as the additional delay for RLM/BFD declaration is within the (to be defined) relaxed requirement
  Other options are not precluded.

## Slide 7: Issue 2-3-5: Low mobility criteria of RLM/BFD relaxation
Low mobility criterion for identifying low mobility scenario under which the UE is allowed to apply the RLM/BM requirements is determined and configured to UE by the network, and it is up to the UE whether to apply relaxed RLM/BM requirements when configured.
Given the this feature is enabled by the network, the low mobility criterion is defined based on
  FFS until RAN4 #99e
    Option A: UE will need to verify whether the low mobility criterion is fulfilled based on the channel condition
      Option A1: RSRP variation (reuse R16 low mobility criterion and procedure)
      Option A2: SINR variation
    Option B: UE will not need to verify whether the low mobility criterion is fulfilled based on the channel condition
      Option B1: UE defines if the low mobility criterion is fulfilled (e.g. fixed UE) or not fulfilled (e.g. vehicular UE).
      Option B2: Network configures whether the low mobility criterion is fulfilled or not
    Option C: The low mobility criterion can be left for RAN2 to decide. Send LS to RAN2 to trigger RAN2 discussion.
    Option D: Other options on how often UE verifies the low mobility criterion is open for discussions at next meeting.

## Slide 8: Issue 2-3-6: Exiting criteria of RLM relaxation
Background:
  Following agreement was made at last meeting [R4-2103670]:
    “The UE while performing relaxed RLM upon detecting certain number of out-of-sync indications or upon triggering T310 or upon observed link quality degradation or mobility state change reverts to the normal RLM operation (i.e. without relaxation).”
Following additional options are listed below:
FFS which of the following options can be used as the exiting criteria of RLM relaxation
Option 1: exit relaxation mode when any relaxation criterion is not met
  Option 1a: a hysteresis value (e.g. 3dB) could be used to avoid ping-ping effect.
    Relaxation exiting condition: Qualitymeasured + Hys < Thresh
Option 2: exit relaxation mode when the radio link quality is worse than a certain SINR threshold Thexit, which is higher than Qout.
  Option 2a: set different radio link quality threshold for entering and exiting the relaxation
  Option 2b: either the averaged SINR based on reduced number of samples is below Thexit, or the one-shot SINR is below Qout.
Option 3: exit relaxation mode based on out-of-sync indication.
  Option 3a: exit when N310 starts to count, i.e. 1 out-of-sync indication.
  Option 3b: exit when T310 is running witch is triggered by a new counter
  Option 3c: exit when certain number of out-of-indications
  Option 3d: exit when certain consecutive out-of-sync indications
Option 4: Additional time is allowed for UE to evaluate first OOS indication when UE is in power saving mode. UE is in normal mode after first OOS indication. The additional delay for RLF declaration is guaranteed to be within OOS evaluation time (TEvaluate_out_SSB) in normal mode. Relaxation factor and exit SINR threshold (for good cell quality condition) is up to UE implementation, but the “first OOS indication” requirement has to be satisfied.

## Slide 9: Issue 2-3-7: Exiting criteria of BFD relaxation
FFS which of the following options can be used as the exiting criteria of BFD relaxation
Option 1: exit relaxation mode when any relaxation criterion is not met
  Option 1a: a hysteresis value (e.g. 3dB) could be used to avoid ping-ping effect.
    Relaxation exiting condition: Qualitymeasured + Hys < Thresh
Option 2: exit relaxation mode when the radio link quality is worse than a certain threshold Thexit , which is higher than Qout_LR.
  Option 2a: set different radio link quality threshold for entering and exiting the relaxation
  Option 2b: either the averaged SINR based on reduced number of samples is below Thexit, or the one-shot SINR is below Qout_LR.
Option 3: exit relaxation mode based beam failure instance indication
  Option 3a: exit upon detecting the 1 beam failure instance indication.
  Option 3b: exit after BFI_COUNTER add to the value of a new counter or a new parameter, the new counter or the new parameter is configured by network.
Other options are not precluded

## Slide 10: Relaxation scheme
Issue 2-4-1: Relaxed evaluation period of RLM/BFD
Scaling factor defining the relaxed RLM/BFD evaluation period is defined based on max(TDRX, TSSB). FFS the following options
Option 1:The similar definition of RLM/BFD evaluation period in Rel-15 can be reused as Max(T, Ceil([Y] x P x N) x Max(TDRX,TSSB))
Option 2: If power saving conditions are satisfied, allow TEvaluate_ps_out_SSB for the first OOS indication and the original TEvaluate_out_SSB doesn’t apply
Option 3: modify the Rel-15 wording in the requirements as follows
  the new evaluation period TEvaluate_out_SSB-Relaxed is specified as K1* TEvaluate_out_SSB, where TEvaluate_out_SSB is as specified in clause 8.1.3.2 in TS 38.133 .
  the new indication period TIndication_interval-Relaxed is specified as K2* TIndication_interval where TIndication_interval is as specified in clause 8.1.6 in TS 38.133.
  FFS whether K1=K2
Other options are not precluded.
Configuration | TEvaluate_ps_out_SSB (ms)
no DRX | Max(200, Ceil(10  P)  TSSB)
DRX cycle≤80ms | Max(200, Ceil(30  P)  Max(TDRX,TSSB))
80ms<DRX cycle≤320ms | Max(200, Ceil(20  P)  Max(TDRX,TSSB))
DRX cycle>320ms | Ceil(10  P)  TDRX
NOTE: TSSB is the periodicity of the SSB configured for RLM. TDRX is the DRX cycle length. | 
Configuration | TEvaluate_ps_out_SSB (ms)
no DRX | Max(200, Ceil(10  P)  TSSB)
DRX cycle≤80ms | Max(200, Ceil(15  P)  Max(TDRX,TSSB) + (K-1)  Max(TDRX,TSSB))
80ms<DRX cycle≤320ms | Max(200, Ceil(15  P)  Max(TDRX,TSSB))
DRX cycle>320ms | Ceil(10  P)  TDRX
NOTE: TSSB is the periodicity of the SSB configured for RLM. TDRX is the DRX cycle length, K is the relaxation factor. | 
Option 2a
Option 2b

## Slide 11: Issue 2-4-2: Are the parameters of relaxation criteria predefined or configurable
The parameters of relaxation criteria can be configured by the network.
  Option 1: The relaxation criteria shall be configured by the network to the UE. If the threshold (criteria) is not configured, it means the UE cannot go into relaxation mode.”
  Option 2: The parameters of relaxation criterion of low mobility and entering condition of good cell quality can be configured by the network. Exit condition of good cell quality is FFS.
  Option 3: The parameters used in good serving link quality criteria are predefined. FFS other potential parameters.

## Slide 12
Issue 2-4-3: network or UE to determine the relaxation criteria is fulfilled or not
UE determines whether the relaxation criteria can be fulfilled or not based on the relaxation criteria.
Issue 2-5-4: Applicability for BFD relaxation requirement
As the legacy BFD requirement, the BFD relaxation requirement is applicable for PCell, PSCell and all configured SCells.
Issue 2-5-2/2-5-3
scenarios for which RAN4 is going to develop relaxation requirements for RLM/BFD is FFS

## Slide 13: Relaxation in intra-band CA
Issue 2-5-2: Exiting relaxation mode in intra-band CA/DC
Option 1: For intra-band CA, if UE has fulfilled the criterion for operating RLM/BFD in relaxed mode in one serving cell, then it is allowed to operate RLM/BFD in relaxed mode in all other serving cells if same type of RS are used for RLM/BFD in the serving cell and other serving cells.
Other options are not precluded
Issue 2-5-3: Relaxation criteria in intra-band CA/DC
Option 1: For intra-band CA, if UE meets the conditions of reverting to the normal RLM/BFD in one serving cell, it is expected the reversion operations are applied to other serving cell(s) if same type of RS are used for RLM/BFD in the serving cell and other serving cells.
Other options are not precluded

## Slide 14: For information: Observations on the simulation results
On power saving gain:
  Based on simulation results submitted for RAN4#98e and RAN4 #98-bis-e meeting, it can be observed that
    With FTP or VoIP model is considered, if L1 measurement intervals for RRM are also extended K times
      For FR1 SSB-based RLM/BFD relaxation with 40ms DRX cycle, at least 3 sources show that the power saving gain is 3.89% to 16.4% for K=2, 13.3% to 20.0% for K=4.
      For FR1 CSI-RS based RLM/BFD relaxation with 40ms DRX cycle, at least 1 source shows that the power saving gain is 4.49% to 6.80% for K=2, 13.41% to 20.34% for K=4
      For FR2 CSI-RS based RLM/BFD relaxation with 40ms DRX cycle, at least 1 source shows that the power saving gain is 5.84% to 9.31% for K=2, 17.79% to 28.63% for K=4.
      For FR1 SSB-based RLM/BFD relaxation with 160ms DRX cycle, at least 1 source show that the power saving gain is 4.95% for K=2, 7.42% for K=4.
    By extending only RLM/BFD measurement interval without reducing RRM measurement samples within RRM measurement period
      At least 2 sources show minimal or no power saving gain.
    Note: Number of RRM measurement samples within RRM measurement period is up to UE implementations
  Therefore, it is concluded that the beneficial scenarios for R17 RLM BFD relaxation are
    When L1 measurement interval for RLM/BFD/RRM can be extended, i.e. number of samples can be reduced, which means SINR is high enough and mobility is low enough, and
    When FTP traffic or Voip traffic is considered, and
    When DRX cycle length is not longer than 80 ms, and
    It is more beneficial if PDCCH-WUS is configured

## Slide 15: For information: Observations on the simulation results
On mobility impact:
  Based on simulation results submitted for RAN4#98e and RAN4 #98-bis-e meeting, it can be observed that
    Regarding delta SINR, for FR1 SSB-based RLM OOS relaxation, when DRX cycle is not longer than 80ms
      with mobility of 3 km/h, at least 6 sources show that the delta SINR of max(5%, 95%) is 0.39 dB to 2.15 dB for K=2 , 0.8 dB to 3.02 for K=4, 1.35dB to 4.5dB for K=8.
      with mobility of 30 km/h, at least 3 sources show that the delta SINR of max(5%, 95%) is 1.05 dB to 2.42 dB for K=2 , 2.4 to 5.06 dB for K=4, 3.6 to 7.57 dB for K=8.
    Regarding delta SINR, for FR1 CSI-RS-based RLM OOS relaxation, when DRX cycle is not longer than 80ms
      with mobility of 3 km/h, at least 3 sources show that the delta SINR of max(5%, 95%) is 1.3 dB to 1.5 dB for K=2 , 1.75 dB to 2.08 dB for K=4.
    Regarding delta SINR, for FR2 CSI-RS-based RLM OOS relaxation, when DRX cycle is not longer than 40ms
      with mobility of 3 km/h, at least 2 sources show that the delta SINR of max(5%, 95%) is 1.1 to 3.2 dB for K=2 , 1.27 to 3.8 dB for K=4, 1.4 to 4.2 dB for K=8.
    Regarding delta SINR, for FR2 SSB-based RLM OOS relaxation, when DRX cycle is not longer than 80ms
      with mobility of 3 km/h, at least 2 sources show that the delta SINR of max(5%, 95%) is 1.1 to 1.7 dB for K=2 , 1.69 to 2.67 dB for K=4, 2.05 to 4.87 dB for K=8.
  Therefore, the feasible scenarios for R17 RLM and BFD relaxation are
    When DRX cycle length is not longer than 80 ms, and
    When SINR is above a proper threshold, and
    When UE mobility is below a certain speed.

## Slide 16: For information: Observations on the simulation results
On mobility impact:
  Based on simulation results submitted for RAN4#98e and RAN4 #98-bis-e meeting, it can be observed that
    Regarding 95%-tile increased RLF latency, for FR1 SSB-based RLM OOS relaxation, when DRX = 40ms
      with mobility of 3 km/h, at least 2 sources show that the increased latency is less than 40ms for K=2, less than 120ms for K=4, and less than 280ms for K=8.
        The increase is less than 2.5% for K=2, less than 7.5% when K=4 and less than 17.5% when K=8, as T310 = 1000ms and N310 = 1.
      with mobility of 30 km/h, at least 2 sources show that the increased latency is less than 40ms for K=2, less than 120ms for K=4, and less than 280ms for K=8 with 95% probability.
        The increase is less than 2.5% for K=2, less than 7.5% when K=4 and less than 17.5% when K=8, as T310 = 1000ms and N310 = 1.
    Regarding averaged increased RLF latency, for FR1 SSB-based RLM OOS relaxation, at least 2 sources show that the averaged increased RLF latency are less than 0.02% for 3km/h mobility and 0.2% for 30km/h, when DRX is not longer than 80ms.
Following observations were made based on simulation results submitted in R4-2106851 and analyzed in R4-2106852:
  Up to 3 km/h and at high SINR (in-sync), relaxation by factor 4 can be allowed for FR1.
  Up to 3 km/h at low SINR (out-of-sync), relaxation if allowed should be smaller than factor 2 for FR1.
  Up to 30 km/h and at high SINR (e.g. in-sync), relaxation if allowed should be smaller than factor 2 FR1.
  Up to 30 km/h at low SINR (e.g. out-of-sync), no relaxation shall be allowed for FR1.
  Up to 3 km/h at higher SINR (e.g. in-sync), relaxation if allowed should be smaller than factor 2 for FR2.
  Up to 30 km/h, no relaxation should be allowed for FR2.