## Slide 1: WF on neighbour cell measurement in NB-IoT RRC_CONNECTED state in Rel-17
Ericsson, […]
3GPP TSG-RAN WG4 Meeting #98bis-e R4-2105801
Electronic Meeting, 12th – 20th April, 2021
Agenda Items: 5.1.2

## Slide 2: Neighbour cell measurements in scenarios A/C
UE can perform neighbour cell measurement without gaps and without causing interruptions to serving cell when the carrier frequencies of serving cell and of measurement neighbour cell are same (scenarios A/C).

## Slide 3: Neighbour cell measurements in scenarios B/D/E
When the carrier frequencies of serving cell and of measurement neighbour cell are different (scenarios B/D/E), UE can perform neighbour cell measurement without gaps without causing interruptions to serving cell using any occasion where the UE is not scheduled which includes any of the following:
  Vacant slots not scheduled for data transmission, i.e. when not required to do data transmission/reception
  When not required to do NPDCCH monitoring
  during the DRX inactive period i.e. when the UE is configured with DRX.

## Slide 4: Measurement triggering conditions
The UE starts performing the neighbour cell measurements when the serving cell quality deteriorates, e.g.
  When X number of out-of-sync indications is detected by the UE
  Other options are not precluded.
The UE stops the neighbour cell measurements when the serving cell quality improves, e.g.
  When Y number of in-sync indications is detected by the UE
  Other options are not precluded.
Values of X and Y are TBD.
  There should be mechanism to stop the neighbour cell measurement.
  It is up to RAN2 to decide the triggering condition for starting and stopping the neighbor cell measurements

## Slide 5: Cell detection time
Normal coverage:
  1400 ms in DRX and non-DRX for an unknown cell.
  80 ms in DRX and non-DRX for an unknown cell when signal quality is sufficient for cell detection on first attempt, whilst for a known cell it is 0 ms.
    Note: no definition in RAN4 about conditions of sufficient signal quality for the first attempt cell detection
Enhanced coverage:
  14800 ms in DRX and non-DRX for an unknown cell.
  80 ms in DRX and non-DRX for an unknown cell when signal quality is sufficient for cell detection on first attempt, whilst for a known cell it is 0 ms.
    Note: no definition in RAN4 about conditions of sufficient signal quality for the first attempt cell detection
The time needed for cell detection subjects to the actual measurement occasions, and the overall time for cell detection will be longer if UE is configured to perform neighbour cell measurement on multiple frequency layers.

## Slide 6: Measurement time
Coverage mode | Measurement period in DRX and non-DRX | 
 | NRS based NRSRP | NSSS based NRSRP
Normal coverage | 800 ms | 1600 ms
Enhanced coverage | 1600 ms | 1600 ms
The time needed for measurement subjects to the actual measurement occasions, and the overall time for measurement will be longer if UE is configured to perform neighbour cell measurement on multiple frequency layers.

## Slide 7: Known cell conditions
The neighbour cell can be considered as known if it has been measured within the last 5 seconds and during which the cell remains detectable; otherwise the neighbour cell can be considered as unknown.

## Slide 8: Valid NRSRP measurement definition
RAN4 has discussed the validity time of a NRSRP measurement and concluded that there is no such definition in current specification.