## Slide 1: Way forward on multiple link tests for NR V2X demodulation performance
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #98-bis-e
E-meeting, 12 – 20 April 2021
Agenda Item: 5.2.1.3
R4-2106034

## Slide 2: HARQ buffer soft combining test
      Agreements from RAN WG4 Meeting #97-e and #98-e
  Test purpose
    The main test purpose is to verify HARQ buffer combining. Configuring of high MCS and long interval between transmission and retransmission is not precluded.
  Test design
    CBW: 20 MHz
    For verification of n16 and n24, 16 or 24 UEs transmit signal one by one circularly for every slot and in the first subchannel.
    For verification of n32, the first 31 UEs transmit signal one by one circularly for every slot and in the first subchannel. The 32nd UE transmit signal in the same slot as the first UE but in the second subchannel.
    Add the following test to verify UE support receive 48 HARQ processes per slot: “For verification of n48, the first 31 UEs transmit signal one by one circularly for every slot and in the first subchannel. The next 17 UEs transmit signal one by one circularly for every slot and in the second subchannel
    For verification of n64, first 31 UEs transmit signal one by one circularly for every slot and in the first subchannel, the next 31 UEs transmit signal one by one circularly for every slot and in the second subchannel, the last 2 UEs transmit signal in the same slot as the first two UEs but in the third subchannel.
  Propagation conditions: AWGN channel model
  PSCCH resource allocation: 2 symbols and 10 RBs
  2 DMRS symbols for PSSCH
  PSFCH configuration: PSFCH with periodicity 1
  Sub-channel size: 10 PRBs
  SCI stage 2 configuration: Payload = 35 Bits, = 2.5
  MCS 28
  Test metric: 5% of PSSCH BLER

## Slide 3: HARQ buffer soft combining test
      Agreements for RAN WG4 Meeting #98-bis-e
  Use MCS 27
  Rx assumptions for simulation alignment: No need any agreement on RX CFO and TO assumptions for requirements definition

## Slide 4: PSFCH decoding capability test
      Agreements from RAN WG4 Meeting #97-e and #98-e
  Test design
    N UEs transmit PSFCH one by one following procedure from Section 16.3 of TS 38.1213
    N is {5, 15, 25, 32, 35, 45, 50, 64} depending on UE capability
  PSFCH periodicity 1
  Feedback mode: ACK/NACK
  Propagation conditions
    Static propagation condition without external noise
  Test metric
    Pr(DTX to ACK)<1% and Pr(ACK miss)<1%
  CBW/SCS
    40 MHz, 30 kHz
  Number of sub-channels
    Multiple subchannels of size 10 PRBs (i.e. 10 for 40 MHz case)

## Slide 5: PSFCH decoding capability test
      Agreements for RAN WG4 Meeting #98-bis-e
  Assumptions on PSSCH transmission from tested UE
    Always let tested UE to transmit PSSCH to enable it to detect related PSFCHs. Meanwhile, it is not necessary for TE to decode the PSSCH to transmit ACK.
  Scenario for test
    Consider groupcast scenario
  Details of Test configuration
    PSSCH allocation: 10 subchannels.
    Sl-PSFCH-CandidateResourceType-r16: allocSubCH
    Sl-PSFCH-RB-Set-r16: 100.
    PSFCH periodicity: 1 slot
    Source ID for tested UE: 0
    Member ID for feedback UE: 0 for UE 0, 1 for UE 1,…,N-1 for UE N-1 and N equals to PSFCH-RX-Number.
    Sl-MinTimeGapPSFCH-r16: 2

## Slide 6: PSFCH decoding capability test
Agreements for RAN WG4 Meeting #98-bis-e
  Details of Test setup and test method
    Option 1 (Baseline solution, GTW #98-bis-e agreement)
      TE randomly transmit ACK or DTX on each PSFCH resource with equal probability
      AT command adopted for this test case based on current available solution.
    Option 2 (new option)
      In every slot, TE transmits one of the two following options (1) all ACK (2) one NACK and all the rests are ACK
      UE decodes all the PSFCH to decide PSSCH ReTx. For (1) no reTx; for (2) ReTx
      Test metric: TE can verify whether UE successfully detect all the PSFCH by reTx received or not. If UE reTx behavior is correct, this slot is a “successful slot”. The requirement can be defined by “successful slot” exceeding 90%/99% or higher.
    Make agreement between option 1 and 2 in RAN4#99e

## Slide 7: PSCCH/PSSCH decoding capability test
      Agreements from RAN WG4 Meeting #97-e and #98-e
  DMRS configuration: 2 DMRS symbols
  MCS 4
  Propagation conditions: Static propagation condition without external noise
  Test metric: Probability of missed PSCCH 1%
  Verification of 2*floor(NRB /10 RBs) capability
    Not to verify 2*floor(NRB /10 RBs) capability in Rel-16 V2X
      Agreements for RAN WG4 Meeting #98-bis-e
  Test title
    Rename the test from “PSCCH/PSSCH decoding capability requirements” to “PSCCH decoding capability requirements”.

## Slide 8: PSCCH/PSSCH decoding capability test
      Agreements for RAN WG4 Meeting #98-bis-e
  CBW and feedback configuration
    GTW #98-bis-e agreement: Option 1 (no PSFCH, AT command and 40 MHz) adopted with the consideration that AT command need to be used for some other test case(s).
    Option 2 (will be considered only if no AT command PSFCH capability test is agreed): 40 MHz CBW, PSFCH based feedback and following test methodology
      TE sets PSSCH priority (in PSCCH) when PSFCH Tx capability < 10, x PSSCH with higher priority, 10-x PSSCH with lower priority. Note that PSFCH is selected according to PSSCH priority, hence if PSFCH Tx capability = x, the x feedback corresponding to x high priority PSSCH is transmitted to TE.
      TE can verify UE PSCCH decoding success or failure by checking whether all the higher priority PSSCH feedback is received. In order to always feedback all the high priority SCHs, UE has to decode all CCH to know the priority.
      To avoid UE cheating, TE can randomize the location of higher priority PSSCHs