## Slide 1: WF on NR repeaters EMC core requirements
ZTE, [...]
3GPP TSG-RAN WG4 Meeting # 98-bis-e
Electronic Meeting, Apr. 12-20, 2021
R4-2106087
Agenda item: 8.11.4
Document for: Approval

## Slide 2: Background
A new TS (TS38.114) was agreed for NR Repeaters EMC according to the revised WID for NR repeaters (RP-210818).
Some the NR FDD/TDD repeaters EMC requirements are discussed in 1st round email discussion

## Slide 3: WF(1)
The following EMC requirements are referred to CISPR or IEC specifications and can be applied to NR FDD/TDD repeaters (subject to WF(3) on slide #5)
  Radiated emission(ancillary equipment), conducted emission (including DC power input/output port, AC mains power input/output port, Telecommunication port) , Harmonic current emissions(AC mains input port), Voltage fluctuations and flicker (AC mains input port)
  RF electromagnetic field (80 MHz to 6000 MHz), conducted immunity (0.15 MHz - 80 MHz), ESD, EFT, Voltage dips, surges
  For the time being, only focus core requirement for TDD and FDD NR repeater EMC.

## Slide 4: WF(2)
Other than the requirments in previous slide, other requirements (such as radiated emission requirement) for NR TDD repeaters are pending on the repeater RF discussion, more discussions are needed for TDD NR repeaters
Other than the requirments in previous slide, other requirements (such as radiated emission requirement) for NR FDD repeaters use TS 36.113 and TS 38.113 as a starting point

## Slide 5: WF(3)
  If there are any differences in core requirement for the NR TDD and FDD repeaters EMC?
  More time to check and decide this in May meeting.

## Slide 6: WF(4)
  Consideration of the TS 38.114 and its skeleton:
  In order to verify technical justification for the new TS 38.114, companies to provide analysis of the TS 36.113 and TS 38.113 with the aim to:
  1. Identify challenges in including NR repeaters in TS 38.113.

## Slide 7: References
R4-2105973, 1st round summary for [98-bis-e] [302] NR_EMC, ZTE Coporation
R4-2106514, Discussion on EMC requirements for NR Repeater. Ericsson
R4-2107252, Discussion on NR repeater EMC, Nokia