## Slide 1: Way Forward on general and PDSCH demodulation requirements for inter-cell interference MMSE-IRC
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #98-bis-e
E-meeting, 12 – 20 April 2021
Agenda Item: 8.14.2.1
R4-2106116

## Slide 2: Common test parameters
Network type
  Synchronized for FDD and TDD
  FFS asynchronized for FDD
Physical cell ID
  Physical cell ID of 0 for the serving cell, and cell ID i for interferer i (where i ≥ 1, maximum number of i is FFS)
SCS
  FDD 15kHz, TDD 30kHz (Same SCS is used for the target and the interference cells)
Channel bandwidth
  Use 10MHz for FDD 15kHz and 40MHz for TDD 30kHz for initial simulation purpose:
  Other options are not precluded
    Option 1: In addition, consider 50 MHz for FDD 15kHz and 100 MHz for TDD 30kHz
    Option 2: In addition, consider 40 MHz for FDD 15kHz and 100 MHz for TDD 30kHz
TDD DL/UL configuration for 30kHz SCS
  7D1S2U(S=6D+4G+4U)
Number of carriers
  In Rel-17, MMSE-IRC receiver performance requirements with interference cell condition is defined only for single carrier scenario

## Slide 3: Common test parameters
  PDCCH and PDSCH allocation in time domain
  Use symbols #0 and #1 of each slot for PDCCH
  PDSCH mapping type A, Start symbol 2, Duration 12
PDSCH allocation in frequency domain: Full PRB
SSB, TRS/CSI-RS configuration
  Configure SSB with different locations and no PDSCH scheduled in SSB slots considering limited number of SSB transmitted
    FFS for HeNet scenario if introduced
    SSB Position in burst is FFS
  Further evaluate the performance difference among following options for TRS/CSI-RS
    TRS/CSI-RS colliding with TRS/CSI-RS interference
    TRS/CSI-RS colliding with data interference
    TRS/CSI-RS with interference free
      Reuse same config for TRS/ CSI-RS as Table 5.2-1
DMRS configuration
  For both serving and interfering cells, DMRS Type 1 with single symbol front loaded and 1 additional DMRS, with FDM applied between DMRS and data (number of CDM groups without data is equal to 1), i.e., overlapped DMRS between target and interferer

## Slide 4: Common test parameters
Propagation condition
  Use TDLA30-10 and for initial simulation purpose
  Other options are not precluded
    Option 1: TDLC300-100
Antenna configuration
  2 Tx as baseline for serving cell and interfering cells
  UE with 2 and 4 RX
  ULA low correlation as baseline

## Slide 5: Target PDSCH parameters for scenario 1
Transmission rank
  Use rank 1 as baseline
MCS
  Use MCS 4 (QPSK, CR=0.3) and MCS 13 (16QAM, CR=0.5) for initial simulation purpose
  Further discuss MCS for requirements definition
  Consider MCS corresponding to QPSK and 16QAM modulation formats
Precoding model
  Use Single Panel Type I and Random precoder selection for initial simulation purpose
  Follow PMI is not precluded.
PRB bundle size
  Set PRB bundle size as 2 for target PDSCH
HARQ process number
  4 for FDD 15kHz SCS and 8 for TDD 30kHz SCS as baseline
Performance measurement point
  SINR at 70% TP for initial simulation purpose
  Using of SNR at 70% TP is not precluded

## Slide 6: Interference model for scenario 1
Interference profile
  Using DIP approach for interference profile definition for initial simulation purpose
    Interference profiles from LTE MMSE-IRC can be used for initial simulation
      Further decide the exact DIP value(s) and interference cell number based on simulation results.
    FFS whether HetNet scenario need to be considered
      The interference profile from LTE NAICS can be used for initial simulation purpose under this scenario
    Other interference profiles not precluded with the consideration of NR deployment scenario pending on further discussion
    Companies are encouraged to bring evaluation for the analysis of performance gain with MMSE-IRC receiver over MMSE receiver under the same inter-cell interference
Transmission rank of interfering PDSCH
  Use the following assumptions initial simulation purpose: random rank with 70% and 30% probability for rank 1 and rank 2 transmission in the interfering cell(s)
Precoding of interfering PDSCH
  Random precoding with single panel type I codebook per slot and per PRB bundling granularity, with PRB bundling size of 2.
Modulation order of interfering PDSCH
  Use 16QAM randomly modulated symbols for initial simulation assumption and other options not precluded.

## Slide 7: Reference receiver
Interference covariance estimation granularity
  Interference covariance estimation granularity is up to UE implementation
  Further check the results and if needed per PRB bundle size or per PRB and per slot basis can be considered as possible options for simulation

## Slide 8: Release independence
Further discuss whether the UE demodulation and CQI reporting requirements with inter-cell interference is release independent from Rel-15 or not