## Slide 1: Way Forward on MMSE-IRC for intra-cell inter-user interference
Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #99-e
Electronic Meeting, 19th – 27th May. 2021
Agenda item: 9.11.2.2
R4-2108666
Document for: Approval

## Slide 2: Inter-user interference modeling for phase I evaluation

## Slide 3: Inter-user interference modeling for phase I evaluation
Number of paired UEs
  2 and 4 Tx
    1 target UE + 1 interference UE
  8 and 16 Tx (if introduced)
    Option 1: 3 paired UEs
    Option 2: 1 target UE + 1 interference UE
    Option 3: Use 1 target UE + 1 interference UE as starting point for initial simulation, and interested companies can bring analysis on scenarios of interference UE more than 1
    Note: further discuss based on the outcome of issue Tx antenna configuration
Rank for target and interference PDSCH
  Consider [1+1], [2+1] and [2+2] for phase I evaluation and make further down selection based on the simulation results

## Slide 4: Inter-user interference modeling for phase I evaluation
Antenna configuration
  Keep previous meeting agreements
    Using 2Tx and 4Tx with random PMI for target UE as starting point for initial simulation
    Other options not excluded
    Interested companies can bring analysis with 8Tx and 16Tx cases with following PMI for target UE
Codebook Type
  For 2Tx and 4Tx with random precoding
    Consider Type I SP codebook
  For more than 4Tx or feedback based precoding (If introduced)
    Option 1: Type II codebook for 16Tx
    Option 2: Type I SP
    Other option not precluded

## Slide 5: Inter-user interference modeling for phase I evaluation
Precoder selection for target UE
  Random for 2 and 4Tx cases
  Further discuss for 8 and 16Tx in case such scenarios will be agreed

## Slide 6: Inter-user interference modeling for phase I evaluation
Precoder selection for interference UE
  2 and 4 Tx
    Prioritize option 1 and 2 for phase I evaluation
      Options:
        Option 1: Select the precoder to ensure orthogonality
        Option 2: Random ensuring the selected PMI matrix shall not be identical to the precoding matrix applied for the UE under test
        Option 3: Fixed
  8 and 16 Tx(If introduced)
    Option 1: Select the precoder to ensure orthogonality

## Slide 7: Inter-user interference modeling for phase I evaluation
Precoding granularity
  2 PRBs for 2 and 4Tx cases
  Further discuss for 8 and 16 Tx in case such scenarios will be agreed
PRB bundling size
  2 PRBs for 2 and 4Tx cases
  Further discuss for 8 and 16 Tx in case such scenarios will be agreed

## Slide 8: Inter-user interference modeling for phase I evaluation
DMRS ports for 1 target and 1 interfering UE scenario
  Consider Option 1A, 1B and 2A for phase I evaluation
    Options:
      Option 1A: DMRS port 0 for target UE, DMRS port 1 for the interference UE, i.e., same CDM group
      Option 1B: DMRS port 0 for target UE, DMRS port 2 for the interference UE, i.e., different CDM groups
      Option 2A: DMRS port 0 (and 1) for target UE, port 2 (and 3) for the interference UE, i.e., use different CDM groups for the target and interference UEs

## Slide 9: Inter-user interference modeling for phase I evaluation
DMRS ports for 1 target and more than 1 interfering UE scenario (if introduced)
  Keep previous meeting agreement

## Slide 10: Inter-user interference modeling for phase I evaluation
DMRS pattern and sequence for all co-scheduled UEs
  Prioritize on scenarios with following configurations for phase I evaluation
    Same DMRS type
    Same DMRS additional position
    Same scrambling ID
    Same cell ID
  Interested companies can evaluate the performance between configuring same or different scrambling ID
Number of front-loaded DMRS
  1 front-loaded DMRS

## Slide 11: Reference receiver for phase I evaluation

## Slide 12: Reference receiver for phase I evaluation
Candidate Receiver
  Prioritize MMSE-IRC processing with serving signal demodulation for Phase I evaluation
  Interested companies can check the benefits of MMSE-IRC processing with joint demodulation
Interference estimation for cases with 2 DMRS CDM group
  Keep it up to UE implementation
  Interested companies can bring analysis on different options
Interference estimation granularity
  Keep it up to UE implementation
  Interested companies can bring analysis on different options

## Slide 13: Reference receiver for phase I evaluation
Network assistance
  FFS on whether considering network assistance
  Companies are encouraged to investigate the pro’s and con’s in the next meeting in order to make decision
QCL assumptions
  Option 1: Assume different QCL information for different CDM groups for studying scenarios with target and interfering UEs on different CDM groups.
  Option 2: Same QCL assumption
  Option 3: No need to consider and specify the QCL assumptions if we agree on using baseline reference receiver.
  Apple request clarification, Intel need time to check

## Slide 14: PDSCH parameters for phase I evaluation

## Slide 15: PDSCH parameters for phase I evaluation
Channel bandwidth
  Option 1:
    For FDD 15kHz SCS: Cover 10MHz and 50MHz CBW
    For TDD 30kHz SCS: Cover 40MHz and 100MHz CBW
  Option 2:
    For FDD 15kHz SCS: Cover 10MHz
    For TDD 30kHz SCS: Cover 40MHz
  Option 3:
    For FDD 15kHz SCS: Cover 10MHz and 40MHz CBW
    For TDD 30kHz SCS: Cover 40MHz and 100MHz CBW
  Option 4: Different assumptions for evaluation phase and for requirements definition can be considered

## Slide 16: PDSCH parameters for phase I evaluation
MIMO correlation for each UE
  Consider ULA Low and XP Low for further phase I evaluation

## Slide 17: PDSCH parameters for phase I evaluation
Propagation condition
  Keep previous meeting agreement: Cover both TDLA30-10 and TDLC300-100 in phase I, and decide whether down-selection or adjustment is needed based on the simulation results
MCS for target UE
  Keep previous meeting agreement:
    Cover QPSK MCS 4, 16QAM MCS 13, and 64QAM MCS 19 for initial simulation
      Rank 1: QPSK, 16QAM
      Rank 2: 16QAM, 64QAM
    Other options are not precluded