## Slide 1: NB-IoT RF-RRM status before RAN5#71 CMCC 2016.05.12
3GPP TSG WG RAN5 meeting#71
Nanjing, China, 23 - 27 May 2016
R5-163023

## Slide 2: Introduction
  RAN5 NB-IoT WI starts from RAN#71 and is planned to be complete in November.
  This slides will give a general information about NB-IoT progress in 3GPP RAN4 which mainly relate to RF and RRM core and performance requirements.

## Slide 3: NB-IoT general information
  Duplex Mode
  HD-FDD
  Three operation modes
  Stand-alone operation
    making use of scattered spectrum and e.g. re-farming of GSM spectrum.
  In-band operation
    making use of resources that are within the system bandwidth of the MBB LTE cell.
  Guard-band operation
    making use of the currently unused resource blocks at the edges of the MBB LTE cell.
  UL Multiple Access
  Single tone: 3.75kHz carrier or 15kHz carrier
  Multi-tone: multiple 15kHz carriers, with SC-FDM
  DL Multiple Access
  15kHz carriers, with OFDM

## Slide 4: Overall progress after April adhoc meeting
Overall Core part: 95%
  RAN1 100%
  RAN2 92%
  RAN3 80%
  RAN4 85%
  Completion date: June 2016 RAN #72
RAN4 Performance part:
  Completion status: 0%
  Completion date: September 2016 RAN #73
  RAN5 Core part:
  Completion date: December 2016 RAN #74
  RAN5 Performance part:
  Completion date: March 2017 RAN #75

## Slide 5: RF progress in RAN4
  Use TS 36.101 for NB-IOT UE RF requirements
  Frequency bands and channel arrangement
  Operating bands
    Re-use existing E-UTRA band definition for NB-IOT.
  Channel bandwidth (R4-78AH-0177)
    for standalone: UL and DL channel BW is 200 kHz for both single tone and multitone
    for Guard band and In band: UL channel BW is 200 kHz, DL use LTE channel BW
  Channel raster
    for in, guard and standalone is 100 kHz
  EARFCN
    Channel numbering is defined

## Slide 6: RF TX/RX progress in RAN4
  Most of the test requirements are defined.
  Completed items:
  TX: Maximum output power, Minimum power, OFF power, ON/OFF time mask, EVM, Occupied bandwidth, SEM, ACLR, Transmitter Spurious emissions, Spurious emission band UE co-existence, Transmit intermodulation
  RX: Maximum input level, ACS, In-band Blocking, Spurious response, Narrow band blocking, Receiver spurious emissions
  Ongoing items:
  TX: MPR, Power control tolerance, Frequency error, In-band emissions
  RX: Reference sensitivity, Out-of-band blocking, Wide band Inter-modulation
  Not needed
  AMPR, Additional spurious emissions

## Slide 7: RF Performance progress in RAN4
  Demodulation of NPDSCH & NPDCCH
  Not yet discussed
  Demodulation of NPBCH
  Not needed
RF CSI report progress in RAN4
  CQI / PMI/ RI Reporting under AWGN conditions
  Not needed

## Slide 8: RRM progress in RAN4
  All items are still ongoing in RAN4:
  Cell reselection, RRC Re-establishment, Random access, UE transmit timing , UE Timing Advance, Radio link monitoring, Measurement
  Cell selection: No requirement will be defined.

## Slide 9: Conclusion
  The overall completion of RAN4 RF and RRM core requirements now is 85%, it is anticipated RAN4 will complete all core requirements on time. Besides RAN4 is considering adding adhoc meetings for performance requirements after June to complete it in September.
  For RAN5, the work plan need to be discussed and optimized during this meeting to make sure test case definition work could be carried out afterwards.