## Slide 1: 3GPP RAN5 #82 Athens, Greece 25 Feb to 01 Mar 2019 R5-192615 Test Tolerance review process for NR

## Slide 2: Current status
RAN5 focus is now on NR, with many new challenges for MU/TT
  NR schedules require significant TT effort to complete Test cases
  NR has new features to be handled and needs new templates
  Many NR Test cases will be developed in parallel
First NR FR1 TT analyses have started to appear
  FR1 PRACH TT template R5-190449 endorsed at RAN5 AdHoc in Singapore
  Complete FR1 PRACH TT analysis provided at RAN5#82, R5-191342
  Non-template-compliant FR1 TT analysis R5-190872 agreed at RAN5 AdHoc in Singapore
Clear need to set up process to formally review NR TT analyses
  Early agreement of templates will help RAN5 efficiency

## Slide 3: Proposed Way Forward
Proposed NR Test Tolerance review process:
  “Declaration” date: normally (meeting upload deadline – 4 weeks)
  “Drafts available” date: normally (meeting upload deadline – 2 weeks)
  Share review workload between NR-reviewing companies
  NR TT analyses are given meeting time (no block approval yet)
  NR TT review process runs at main meetings only (4 times per year)
  Test case sign-up companies resolve any associated RAN4 issues
NR-reviewing companies so far for FR1 (thanks):
  Qualcomm, Rohde & Schwarz, Ericsson, Anritsu, Keysight
  Other companies welcome to join
  Anritsu is willing to do assignment to each NR-reviewing company

## Slide 4: Scope and Technical basis
Scope of NR Test Tolerance review process:
  RRM and Demodulation/CSI (most RF already done)
Technical basis:
  Principle of Superposition, as defined in TR 38.903
  Uncertainties are orthogonal (required for superposition to be valid)
  Base on common uncertainties, such as TS 38.533 Table F.1.1.2-1
  Measurement uncertainty tolerance interval 95%, as in TR 38.903
  All core requirement side conditions met, based on tolerance interval
  The technical basis above aligns with TT = MU
RAN5 will work to identify test cases where special handling of TT is required to avoid significant adverse effects on network operation

## Slide 5: Deliverables
At the “Declaration” date:
  Which test cases the contributing company intends to work on
At the “Drafts available” date:
  Draft TT analysis, .xls and .doc as required
  TR 38.903 CR to include the TT analysis as .zip files
  Conformance test spec CRs to include TT in the test cases, together with Annex F updates (Uncertainties and Test requirement derivation)
  Identify issues and proposals to solve, for example RAN4 updates
At the Tdoc upload date and at the meeting:
  TR 38.903 and Conformance test spec CRs
  Known status of any associated issues such as RAN4 dependency

## Slide 6: Open issues
FR2 Uncertainties
  For RRM and Demodulation/CSI, would like to avoid the need for multiple per-test-case detailed analysis of uncertainties
RAN4 Core requirement side conditions in TS 38.133
  A few NR FR1 side conditions are not yet finalised in RAN4
  Many NR FR2 side conditions are absent in RAN4
RAN4 Spatial aspects of RRM test cases in TS 38.133 Annex A
  Test cases with 2 angles of arrival are not yet agreed in RAN4
  Aspects related to UE Spherical coverage are not yet defined
  UE Spherical coverage is also dependent on Power class

## Slide 7: Proposed Way Forward for FR1
RAN5 is asked to endorse key points for NR TT review process:
  “Declaration” date: normally (meeting upload deadline – 4 weeks)
  “Drafts available” date: normally (meeting upload deadline – 2 weeks)
  Share review workload between NR-reviewing companies
  NR TT analyses are given meeting time (no block approval yet)
  NR TT review process runs at main meetings only (4 times per year)
  Test case sign-up companies resolve any associated RAN4 issues
RAN5 is asked to endorse the principles on slide 4:
  Scope is RRM and Demodulation/CSI
  Technical basis as given on slide 4
  Identify test cases where special handling of TT is required

## Slide 8: Offline discussion, 1 of 3 (for information only)
An FR1 RF Test case where TT < MU
  One (RF) example where there was an obvious problem for network operation is UE max output power, where the FR1 core requirement in TS 38.101-2 is +/-2dB. For 3GHz to 6GHz, BW 40MHz to 100MHz, the MU in 38.521-1 Table F.1.2-1 is +/-1.6dB.
  If we applied TT=MU, then the max power test requirement would be relaxed to +/-(2 +1.6) = +/-3.6dB. This is too big (large adverse effect on cell coverage). So the RAN5 agreement was TT=1dB, and the test requirement is +/-3dB, which is more reasonable.

## Slide 9: Offline discussion, 2 of 3 (for information only)
Possible criteria for deciding special handling for RRM/demod TT:
  MU is too big compared to the core requirement tolerance (for example MU +/-1.6dB and Core requirement +/-2dB above).
  The parameter where MU is too big compared to the core requirement tolerance is critical to the test purpose (in example above, UE max power is test purpose, not just a side condition)
  The parameter value is critical to network operation (for example, UE power affects cell coverage)
  To identify a test case for special handling with TT < MU, all 3 criteria should be met (which they are for FR1 UE max output power).

## Slide 10: Offline discussion, 3 of 3 (for information only)
Test Purpose:
  When indentifying exceptions, consider the test purpose. For example, an RRM test case might have test purpose to measure the time to report an Event. The important thing for the network is whether the test requirement for reporting time is relaxed or not. Correct operation of the test also depends on RSRP measurement which in turn has side conditions, but the test purpose is not usually to stress all the side conditions (dB values) at the same time.
  A different example would be UE RSRP reporting accuracy, where the test purpose is (obviously..) to measure the UE RSRP reporting accuracy, which is the important thing for network operation. The test case may be designed with chosen side conditions to stress the UE. Here the effect of test system uncertainty on side condition dB values and reported RSRP dB values needs to be carefully considered.