## Slide 1: FR2 NR TT Way Forward update
3GPP TSG-RAN WG5 Meeting #583
Reno, USA, 13th – 17th May 2019
R5-194291
Telecom Italia

## Slide 2: Background
At RAN5 5G-AH#3 New FR2 MU values for IFF method introduced in R5-186344
At RAN5#81 several contributions regarding TT are presented:
  R5-186888: proposing TT = 0 and highlight Network coverage impact
  R5-187576: defining upper bound for TTs (TT = 2.1 dB)
  R5-187568: proposing TT = 0.65xMU
  R5-187235: proposing basically TT = 0.82xMU
At RAN5 RAN5#81 a WF for FR2 in TS 38.521-2 is agreed in R5-188058 and a MU update in R5-188224 and R5-188225
At RAN RAN5 5G-AH#4 MU values are updated in TS 38.903 and Spherical Coverage MU values are introduced in R5-190576
At RAN5#82 contributions regarding TT spherical coverage test cases are presented (still under discussion):
  R5-191727 and R5-191836: proposing TT = 0.65xMU
  R5-192657: proposing TT = 2 dB Upper bound

## Slide 3: Agreed FR2 WF TS 38.521-2
Except the FFS and empty items, the proposed FR2 TT Values are included in the spreadsheet file, based on the following assumption:
TTs shall be defined case by case
TT = 0.65 * MU (the upper bound of MU value used for TT calculation is 5.5 dB, 0.65 upper bound TT/MU ratio). Applies to following Test Cases:
    Min Peak EIRP
    Max TRP
    Reference Sensitivity
    ACLR and SEM (no MU Upper Bound Applied)
Min EIRP at 50t%-tile CDF and EIS spherical coverage still under discussion.
TT = 0.50 * MU (the upper bound of MU value used for TT calculation is 0.01ppm , 0.5 upper bound TT/MU ratio) Applies to following Test Cases:
    Frequency error
Since TT have dependency from MU, no TT value can be defined if the corresponding MU is not finalized (business as usual).
TT values may decrease based on the experience on the field and when all parties will have more confidence in device performance
The TT values and the method to derive the TT defined until RAN5#85 (November 2019) for execution in any possible certification. At RAN5#85 the TT values shall be re-evaluated
  Required actions are specified in editor’s note in Annex F

## Slide 4: Attached Spreadsheets update
TS 38.521-2 SA FR2 TT after RAN5#82
  Removed Test methods
  DUT size separation
  MU values updates R5-192845
    EIRP Expanded uncertainty
    TRP Expanded uncertainty
    EIS Expanded uncertainty
    Spherical coverage Expanded uncertainty (TBD)
    EIS Spherical coverage Expanded uncertainty
TS 38.521-2 SA FR2 TT after RAN5 5GAH#5
  MU values updates R5-193465
    Spectrum Emission Mask
    Reference sensitivity
    EIS Spherical coverage
  Corresponding TT re-calculated except Spherical Coverage which is TBD pending multiple measurement analysis and TT ratio