## Slide 1: Discussion on handling of MDT IDC problem
China Mobile, CATT, Qualcomm
3GPP TSG-RAN5 Meeting #103 R5-243486
Fukuoka, Japan, May 20 - 24, 2024

## Slide 2: Background
Observation 0: To complete TC 8.1.6.1.2.14, it is still need to confirm UE will detect IDC problem with “T1” configuration.
TS 38.523-1
Notes: Comparing to the idle “Victim” DL, there is no changes happened to the connected “Victim”DL

## Slide 3: How to set up the Pre-test conditions to detect IDC problem?
Observation 1.2: Comparing to the idle “Victim(DL)”, there is no changes happened to the connected “Victim(DL)” considering they suffer the same interference from the unchanged “Aggressor”(the same working frequency and the same power level). If the connected “Victim(DL)” suffers the IDC problem, the idle “Victim(DL)” will also suffer the same IDC problem under the same pre-test conditions.
Proposal 1: When checking whether UE will suspends measurement logging when IDC problem is detected, if UE detects IDC problem in RRC_CONNECTED with some pre-test condition, to configure the IDLE UE with the same pre-test condition as in RRC_CONNECTED to enable the UE detect IDC problem in RRC_IDLE also.
Observation 1.1: By the agreed CR R5-241635 for TS 38.523-1, the pre-test condition of TC 8.1.6.1.2.14 was set as shown in the picture above. “Victim(DL)” B40 and “Aggressor(UL)” 2.4GHz WiFi have been set as close to each other as possible. Only 1MHz of isolation will lead to inevitable interference from “Aggressor: Channel 1” to “Victim: NR Cell 14/NRf4”.
Notes: Comparing to the idle “Victim” DL, there is no changes happened to the connected “Victim”DL

## Slide 4: How to confirm UE detects IDC problem? (1/2)
5.7.4.2 Initiation
[…]
A UE capable of providing IDC assistance information in RRC_CONNECTED may initiate the procedure if it was configured to do so, upon detecting IDC problem if the UE did not transmit an IDC assistance information since it was configured to provide IDC indications, or upon change of IDC problem information.
[…]
Upon initiating the procedure, the UE shall:
[…]
1> if configured to provide IDC assistance information:
  2> if the UE did not transmit a UEAssistanceInformation message with idc-Assistance since it was configured to provide IDC assistance information:
    3> if on one or more frequencies included in candidateServingFreqListNR, the UE is experiencing IDC problems that it cannot solve by itself; or
    3> if on one or more supported UL CA combination comprising of carrier frequencies included in candidateServingFreqListNR, the UE is experiencing IDC problems that it cannot solve by itself:
      4> initiate transmission of the UEAssistanceInformation message in accordance with 5.7.4.3 to provide IDC assistance information;
  2> else if the current IDC assistance information is different from the one indicated in the last transmission of the UEAssistanceInformation message:
    3> initiate transmission of the UEAssistanceInformation message in accordance with 5.7.4.3 to provide IDC assistance information;
Observation 2.1: A UE capable of providing IDC assistance information in RRC_CONNECTED may NOT initiate the procedure even if it was configured to do so. However, upon initiating the procedure, the UE shall initiate transmission of the UEAssistanceInformation message in accordance with 5.7.4.3 to provide IDC assistance information.
TS 38.331

## Slide 5: How to confirm UE detects IDC problem? (2/2)
Observation 2.3: “UE to initiate the UAI procedure” is the pre-condition to check whether UE detects IDC problem. Once UE initiates the UAI procedure, we can confirm that UE detects IDC problem if UE initiates transmission of the UAI message. Similarly, we can also confirm that UE does NOT detect IDC problem if UE does NOT initiate transmission of the UAI message.
TS 38.523-1
Observation 2.2: Whether UE will initiate the UAI procedure is out of the scope of the TP(Test Purpose) of TC 8.1.6.1.2.14.
Proposal 3: Instead of Propsal 2 above, RAN5 to define a new PICS “PC_IDC_Report” as “Support providing UEAssistanceInformation message with IDC-Assistance-r16 in RRC_CONNECTED when an IDC problem is detected in RRC_IDLE” if it was configured to do so.
Proposal 2: RAN5 to define a new test mode as “A UE capable of providing IDC assistance information in RRC_CONNECTED will initiate the procedure” if it was configured to do so.

## Slide 6: Thank you!