## Slide 1: Discussion Slice based PLMN selection
Ericsson

## Slide 2: General
From the Rel 18 study EASNS we have the TR 22.835 and the accompanying CR to 22.261(CR 505)
The requirement for roaming is
“For a roaming UE activating a service/application requiring a network slice not offered by the serving network but available in the area from other network(s), the HPLMN shall be able to provide the UE with prioritization information of the VPLMNs with which the UE may register for the network slice.”
This requirement is for one slice only but in a general case it implies that the HPLMN needs to provide a prioritization list of VPLMN. This list needs to include the supported slices per VPLMN. This would enable the UE to make choices based on which application it uses.

## Slide 3: Question 1
Question 1: Would SA1 be able to provide any additional guidance regarding Scenario 1? In particular:
Whether the "prioritization information" defines priorities between the PLMNs or between the slices?
If the answer to a) is “between the slices”, should the prioritization of slices be determined by the network or by the UE?
Our suggestion is to interpret the SA1 requirement on previous page “HPLMN shall be able to provide the UE with prioritization information of the VPLMNs “ to be interpreted as HPLMN sends a prioritized list of VPLMN’s with additional information (supported slices)
Answer 1:
a) The prioritization information is given from HPLMN and is a list of VPLMNs in priority order and each VPLMN with information of supported HPLMN network slices
b) n/a

## Slide 4: Question 2
Question 2: Should a slice determined according to Scenario 2 be considered as being offered by the serving network or not? If yes, then is the slice determined from the non-default URSP rule to be considered as higher priority than the slice determined from the default URSP rule?
There is no service requirement for the default URSP “match all” slice. It is however understood from the roaming UE requirement that if a different slice should be chosen it needs to be based on that there is no support in current VPLMN. If the current VPLMN do not have any limitations, there should be no need to choose a different VPLMN
Answer 2:
There is no requirement that explicitly cover “match all” slice scenario in SA1, CT1 should progress in suitable way.

## Slide 5: Question 3
Question 3: Would SA1 be able to provide any additional guidance regarding the interaction between legacy PLMN selection prioritization and new prioritization information for slice based PLMN selection? In particular:
which list has a higher priority while performing PLMN selection?;
does the trigger to perform SOR apply when the UE uses slice-based PLMN selection?
Answer 3:
A slice based VPLMN selection while enabled by the HPLMN has higher priority.
No, if slice-based selection is used it is triggered from the fact that an application needs the specific slice