## Slide 1: Without Spanning Tree Protocol
Ethernet broadcast from Ethernet Device E
This is unexpected behaviour for Ethernet Device C!
  Causes lots of issues at Ethernet Device C
/N6

## Slide 2: What if this were wired Ethernet?
How would Spanning Tree Protocol help?
Ethernet cable
Ethernet cable
Spanning Tree Protocol blocks certain links in a network
  One node in a network is designated Root and has the responsibility to assess the topology and issue commands to block damaging links
  In this example, Ethernet Switch T has been instructed to route to Device C only via Ethernet Switch S and to block the direct link

## Slide 3: How might this look in 3GPP?
In Ethernet, ports are blocked by STP in order to prevent loops
In the 5G example, we would want to prevent packets flowing to one particular UE
If the 5G system (perhaps at the UPF, perhaps on the N6 interface somewhere) can interpret STP Bridge Protocol Data Units and associate each UE with an Ethernet port, then the 5G system can route Ethernet frames based on destination UEs mapped to Ethernet ports
Ports blocked by STP would equate to removing a particular UE from a broadcast group
  Note that in Rapid Spanning Tree Protocol (RSTP) a blocked port state is known as Discarding state
Analogise UEs to Ethernet ports

## Slide 4: How might this look in 3GPP?
This is a stage 2 decision, however, and 3GPP may chose not to exactly specify this role in a 3GPP function like the UPF, but to expect that STP would be supported by something on the N6 interface (like SGi-LAN in LTE)
From a service requirement point of view, we should care that the Ethernet devices beyond the 5G network receive frames as expected and that the 5G network responds predictably like Ethernet transport
Analogise UEs to Ethernet ports

## Slide 5: With Spanning Tree Protocol
Ethernet broadcast from Ethernet Device E
Great news, everyone!
/N6