## Slide 1: 5G-Advanced Harmonized Communication and Sensing
Huawei
SA1 97e 14-24 February 2022 , S1-220140

## Slide 2: Motivation
Harmonized Sensing and Communication in 3GPP means that the sensing capability is integrated with cellular wireless communication system to share the same spectrum and infrastructure especially on the industry with both communication and sensing demand, which will optimize both communication and sensing performance.
Considering the following advantages of cellular network, the cellular network will bring large-scale wireless sensing capability and huge market opportunity:
  Native network-wide sensing
  Feasible resource cooperation
  Spectrum interference avoidance
  No privacy issues, which can be equipped even in bedroom
Sensing
Communication
Base station
Base station
Core
network
UE
S1-220140

## Slide 3: Technical Principles
Sensing based on the 5G signals is a technology using the difference between wireless signals and its reflective signals including the Doppler frequency shift, time of flight (ToF), amplitude variation and so on, to sense the surroundings
Distance: identified based on the ToF related information.
Angle: identified based on the phase related information from multiple antennas.
Velocity: identified based on the Doppler frequency related information
Material: identified based on the amplitude related information
…
S1-220140

## Slide 4: Existing 3GPP Design Supports RAN-based Sensing
D
D
S
U
D
D
D
S
U
D
Sensing period：scan120 horizontal degrees every 100ms
Time slot
D
D
S
U
D
……
Transmit a sensing beam direction every 10ms
beam#1
beam#2
beam#10
communication
sensing
sensing
communication
Time division multiplexing for sensing symbol and communication symbol
Existing NR Uu design capability
NR supports Type B PDSCH allocation from 3GPP Rel-15，and the number and position of DL communication symbols can be flexibly configured.
NR supports the configuration of reserved DL time-frequency resources from 3GPP Rel-15. The sensing symbols can be transmitted in the reserved resources.
Existing NR PC5 design capability
Existing PC5 structure can be used as baseline for UE centric Sensing
OFDM wave can be used to sensing
Source：”OFDM Radar Algorithms in Mobile Communication Networks” Martin Braun
CP
Sense
Transmit
CP
Sense
Receive echo signal
The farthest echo signal can be correctly detected within the CP rang.
OFDM sensing process
Sensing
Communication
Transmission
Reflection
Co-Base Station Hardware/Co-Device Hardware
Co-Spectrum, <10% resources for sensing
Co-site/Co-device deployment for HCS
Feasibility for support of 5GS sensing capability
S1-220140

## Slide 5: Objectives
Scope for Rel-17*
The objective of this study item is to study 5G system support of Integrated Sensing and Communication (e.g. sensing the target object based on the NR radio signal):
- Study use cases and potential requirements for enhancement of the 5G system to provide sensing services, specifically addressing the following scenarios:
- 5G system to provide sensing service to V2X, including improving perception of surroundings and 3D map reconstruction for road/pedestrian safety, autonomous vehicles and/or assisted driving.
- 5G system to provide sensing service to low-altitude UAV applications, such as using sensing to detect obstacles for drones.
- 5G system to provide new sensing services for other target use cases and verticals/applications, e.g. in the area of smart home, in-car sensing, healthcare, crowd management, environmental monitoring, infrastructure monitoring, etc. having in mind indoor and outdoor scenarios.
- Sensing service performance requirements pertaining to each of the identified use cases, such as: sensing range, sensing velocity (influential factors such as incident angle, Doppler effect, etc.), sensing resolution, sensing service response time, etc.
- Study to support different dimensions of sensing services (e.g., per UE/per object/per area).
- Study sensing service-related network management including: discovery, authorization and provisioning of the sensing service, as well as network control aspects, such as activate/deactivate/update the sensing service;
- Study sensing information exposure to UE or 3rd party by network;
- Study description of sensing information that is used to reconstruct the sensed target region for the sensing services, e.g. object presence in the area of interest.
- Study use cases and potential requirements for improving communication performance, e.g. by assisting beam alignment or channel estimation.
- Aspects related to security, privacy, regulatory requirements and charging.
- Gap analysis between the identified requirements and existing 5GS requirements or functionalities.
NOTE 1: For UE-centric scenarios, both in coverage and out of coverage will be studied.
NOTE 2: Application enablement layer is considered as out of scope of 3GPP for this study.
S1-220140

## Slide 6: Annex

## Slide 7: Use Cases ---NW centric Sensing-UAV
1. Industrial UAVs Boosting Brings Urgent Safety Concern
Industrial Drones forecast [K Units]: More usage on Utility & power/oil & gas/Emergency
Industrial UAVs To Be Boosting in Next Few Years
Source: Morgan Stanley Research
Urban Air Mobility Global Market(Billions)
UAVs values accepted in many industries, will boost in next 5 years, expected to reach 1500 billions value
INCIDENT | INDUSTRY | LOCATION | DATE
Van struck by low-flying drone | Law Enforcement | Queensferry, UK | 15-Nov
Police and air traffic control intervene after drone spotted at Newcastle | Stadiums | Newcastle, UK | 8-Oct
Criminals Use Drones to Drop 5 Litres of Flammable Liquit | Law Enforcement |  | 1-Oct
Drone crashes into Leaning Tower of Pisa | Private/Non-Coporate | Pisa, Italy | 28-Sep
Student got fined with 4,000€ for filming Mont-Saint-Michel | Private/Non-Coporate | Le Mont-Sain-Michel, France | 22-Sep
Drone attack on vaccination opponents in Hanau | Law Enforcement | Hanau, Germany | 18-Sep
drone strike leads to explosion at oil depot | Energy/Utilities | Donetsk, Ukraine | 11-Sep
Drone incursion during world championship qualifiers between Austria and Republic of Moldova | Stadiums | Chisinau, Republic of Moldova | 1-Sep
Drug-carrying drone bound for prison lands outside Virginia school | Prisons | Lawrenceville, USA | 13-Sep
Drone Passes Below JetBlue Flight Landing At Logan Airport; FAA Investigating | Airports | Boston, MA, USA | 15-Aug
Drone Slams into Building in World Trade Center | Law Enforcement | Manhattan, NY, USA | 2-Aug
Typical UAV incidents of EU and NA, from https://www.dedrone.com
More and More UAV Incidents, Safety Concern Becomes Urgent Issue
S1-220140

## Slide 8: Use Cases ---NW centric Sensing-UAV
1. 5G-A HCS enables UAV Invading Detection
Detailed Requirements for UAV Invading Detection
Without safety guarantee, UAV can’t develop massively
Events Assurance
Important Areas Protection
Airports
Stadiums
Important Buildings
Celebrations
Commercial: Prevent UAVs Invading from:
Stealing Confidential Info.
Affecting Public Safety
Chemistry/Energy…
Big Enterprises
UAV Detection Market Will Increase to 12 Billion/Year by 2030
DRONE INDUSTRY INSIGHTS(Germany): Anti-Drone market $6.6 billion by 2024, CAGR 41.4%, will reach $50 billion by 2030
Commercial
26%
Government
24%
Others
50%
Detection
48%
Detection & Disruption 52%
touchable UAV detection market will reach 12 billion by 2030, According to distribution by end-user and defense type
Source: Verified Market Research
S1-220140

## Slide 9: Use Cases ---NW centric Sensing-ITS
2. Intelligent transportation has strong sensing demand
10 thousands sets
Strong sensing demand for ITS
Various sensing cases for ITS
Radar market in China (200K sets/year)
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
 | 3.95 | 6.38 | 11.02 | 13.05 | 15 | 17.03 | 19.3347 | 21.6549 | 24.0369 | 26.4406 | 29.0847
Automotive Vehicle-to-Everything (V2X) market by region, 2014-2025
Source: Grand View Research, Feb, 2017
USD Million
Radar market in US
All-day traffic monitoring and management
Traffic hazard detection and handling
Track restoration for determination of accident responsibility
Illegal driving
supervision
Smart car: RAN-based sensing for autonomous driving
Smart road: RAN-based sensing for road supervision
Sensing for ITS(Detail in S1-22XXXX）
S1-220140

## Slide 10: Use Cases ---NW centric Sensing-Railway
3. Potential Use Cases: Railway Intrusion Detection
https://ec.europa.eu/eurostat/statistics-explained/index.php?title=Railway_safety_statistics_in_the_EU
EU 2019: 520 people died in accidents and 2313 suicides on railway
Vehicles Intrusion
Pedestrians Intrusion
Natural Disasters
Thousands of people died due to intrusion into railway
HCS Is A Good Option of Railway Intrusion Detection System
“Construct an intelligent monitoring and warning system for natural disasters, foreign object intrusion.”
Candidate Technologies: Camera + mmW Radar / Vibrating fiber…
China 2019: 788 people died, pedestrian intrusion as main reason
HCS is a better option, because railway companies has strong communication requirements simultaneously
Notice of China Advanced Railway Planning
Published in 2020
Services |  | Requirement
CCTV upload | 40~60 cameras per train | 100Mbps
Train info upload | Mechanical and electrical data | 50GB/day
trackside Info upload | Trackside monitoring camera and Worker Portable camera | 10Mbps+
Safety Mgmt | natural disasters, foreign object intrusion | Sensing
5GS provides communication + sensing services for railway.
China is Planning Railway Intrusion Detection System
S1-220140

## Slide 11: Use Cases ---UE centric Sensing
Home Intelligence
(Detail in S1-22XXXX）
In-vehicle sensing
Intelligent home management and control based on sensing
Safe driving in a sensory assisted vehicle
…
…
Fall Detection
Home control
Children Custody
Infant testing
Sleep Alert
Coordinated Sensing between multiple UEs
Improve sensing accuracy by multiple sensing device coordination in home scenarios.
Sensing and enabling smart applications
Smart application
Interaction Identification
Gesture Reconfiguration
…
S1-220140

## Slide 12: Thank you