## Slide 1: 5G System and CN Operator Perspective
AT&T
S2-153079

## Slide 2: Background
NGMN and 4G Americas have both advocated certain principles for the design of the 5G core network and for interfacing of access technologies to the 5G Core Network
Many of these principles and requirements are derived from operator’s operational experience and not from specific 5G service related use cases
Such operational needs should be included by SA2 as architectural requirements and assumptions while developing a new 5G system architecture and 5G CN
  In the past backward compatibility and ease of migration to the next “G” was considered the key operational requirement that largely dictated the level of innovation and improvement that could be allowed in the next generation of packet core
  While migration/backward compatibility can still be part of operational considerations but neglecting other operational aspects will result in a network with increased complexity, reduced flexibility and a system where innovation is stifled

## Slide 3: NGMN Architectural Requirements
NGMN whitepaper lists several key requirements relevant to 5G System and Packet Core including the following:
  A functional decoupling of Core and RAN network domains
  A RAN technology agnostic architecture where introduction and connection of new radio technology will be possible in a plug and play manner
  Independent evolution of core and RAN network domains should be possible.
  C- and U-plane functions should be clearly separated, with open interfaces defined between them, in accordance with SDN principles.
  A decoupling of Hardware and Software functions of network elements in all network domains.
  Cost and effort efficient upgrade path so that Operators can leverage significant investments into existing operational infrastructure and maximize its utilization.
  Real-time and on demand network configuration and automated optimization.
  Flexible and cost efficient network operation.
  Maximize utilization efficiency of available network resources.
  Dynamic relocation of network resources, fully controlled by operator.

## Slide 4: 4GA Architectural Requirements
4G Americas also lists several 5G requirements that are relevant to development of a next generation of packet core:
  The 5G network architecture should be such that the air interface and the core network can evolve and scale independently of each other.
    Changes/enhancements to one domain should not mandate changes/enhancements to the other.
  5G networks must also support multi-RAT connectivity efficiently and effectively.
    Provide access agnostic packet core across multiple Radio Technologies (e.g. cellular, Wi-Fi, etc.) to support uniform Authentication, Session Continuity, and Security across radio technologies.
    Provide Plug and Play capability where a new access technology may be attached to the packet core without any modifications.

## Slide 5: EPC and its Limitations
During development of LTE in 3GPP, for its coexistence with legacy 3GPP technologies a tight coupling approach was adopted that allowed seamless service continuity for legacy services. While the differences between the GPRS (2G/3G packet core) and EPC were not as significant, a tight coupling resulted in an increased packet core complexity involving interworking between 2G/3G and EPC packet core entities.
  A tight coupling of new 5G packet core with legacy RANs would result in introduction of similar complexity as was seen in LTE and 2G/3G interworking.
  In the context of 5G perhaps 2G/3G can be considered legacy that do not require tight coupling
  To have tight integration of LTE Advanced with 5G while avoiding CN complexity, LTE Advanced should support a new control plane to connect natively to 5G CN
Like 2G/3G packet core, EPC is also not access agnostic and has dependencies on the LTE RAN. For example EPS bearers and QoS principles are access specific QoS concepts that would need to be made access agnostic in 5G architecture. AAA is another area that should be looked at for making it access agnostic in a 5G CN.
  This is to ensure that the new packet core can easily be upgraded independent of the access technology and also natively support a variety of access technologies without a need for complex interworking

## Slide 6: 5G System Architecture and CN Features
The design principles from NGMN and 4GA and limitations of EPC can lead to a new architecture with a CN that:
  Minimizes access specific nodes
  Has separation of user and control plane
  Uses SDN based policy framework for operator policies
  Provides mobility support when its needed
  Implements QoS in an access agnostic manner
  Implements AAA in an access agnostic manner
  Supports use of service specific core via network virtualization and service specific network slicing
5G CN should avoid carrying legacy baggage from EPC. It should be based on access independent features like access neutral QoS model, AAA, mobility and policy framework
Developing a new 5G CN will have impact on RAN-CN interface and hence for providing a deployable 5G system work on this interface needs to be prioritized
*Note: While some of the features like NFV are independent of network architecture and hence can and will be implemented for existing EPC, other aspects like access agnostic QoS and AAA, mobility on demand, access agnostic mobility tunnels, use of SDNs for policies would result in a significant change to the current packet core. Thus, the 5G packet core may not be an evolution of EPC but rather a brand new solution

## Slide 7: 5G RAN-CN interface - NGMN preferred Option 3 should be the way forward

## Slide 8: 5G CN and it Co-existence with Legacy Technologies
5G RATs
Evolved LTE
Legacy Cellular RATs
Wireline / Others
LTE Core with
LTE Capabilities
Legacy Core with
Legacy Capabilities
Wireline / Other Core
with their Capabilities
Services
(e.g. IMS)
Services
(e.g. IMS)
Services
(e.g. IMS)
Access Agnostic Interface
Access Agnostic Interface
Access Agnostic Interface
Legacy
Interface
Legacy
Interface
Legacy
Interface
Network Capabilities
Exposed to the Outside
World via APIs
Databases
5G, LTE, Legacy, Wireline/Others
Access Agnostic Functions
Authentication
Authorization
Accounting/Charging
Quality of Service
Security
Mobility on Demand
Data Analytics
Policy Enforcement
Content Optimization
Others…
SGi
SGi
SGi

## Slide 9: Timeline for 5G System Architecture and CN
Any phased 5G approach needs to address 5G system architecture and 5G CN in the initial phase
  Work on 5G System Architecture and 5G CN needs to be aligned with 5G radio work for timing and content
  We believe a baseline 5G System Architecture and CN work can be completed in Release 15 and in synch with first phase of normative work for 5G RAN. Its features can further be enhanced in Release 16
  Launching of a 5G RAT without a 5G CN we believe impacts target timelines for a deployment of a 5G CN by 2020 for operators, increases dependency of 5G on legacy EPC and creates complex roaming scenarios for 5G
Any phased approach that results in fragmentation of 5G ecosystem should be avoided
  A phased approach towards 5G work should not result in non-compatible* 5G UEs and base stations for different phases of 5G
  Operators should not be required to launch 5G networks
    with non-compatible UEs and 5G RAN for different 5G phases or
    requiring support for multiple 5G stacks or
    with a CN that can not be evolved independently of 5G radio
*Note: the incompatibility is from differences in higher layer functionality associated with RAN-CN interface