## Slide 1: Analysis and way forward in 5G support for emergency session
Shabnam Sultana

## Slide 2: Emergency type background
Basic Emergency (UE detected & verifiable, not Limited Service)
Limited Service emergency support (including failed or not performed auth, without USIM)
UE undetected emergency (IMS level detection and reroute)
  If the UE initiates a non UE detectable emergency session, and the session initiation request is rejected by the P-CSCF with an indication that this is an emergency session, the UE shall select a domain according to the requirements for domain priority and selection. In EPS the IMS can indicate to use CS for emergency.
Domain and Priority Selection as per 23.167 in the context of 5G needs to be developed.

## Slide 3: Deployment scenarios
Case 1: 5GC supports two 3GPP RATs: LTE and NR
Operator deploys Emergency over:
  LTE RAT connected to 5GC or
  NR and LTE Connected to 5GC or
  Fallback/Redirect to other System
    LTE connected to EPC or
    CS domain (2G/3G)
  Seems unlikely that NR supports emergency but LTE does not, so assume this case not supported/needed.
Case 2: 5GS supports LTE only connected to 5GC
  & supports emergency or
  Supports emergency using Fallback/redirect to other System
    LTE via EPC or
    CS domain (2G/3G)
Case 3: 5GS supports NR only
  & supports emergency on NR or
  Supports emergency using Fallback/redirect to other System (LTE via EPC, CS domain (2G/3G)

## Slide 4: UE normal emergency operation
UE has registered in the 5GS and has information provided by 5GC (i.e. AMF) about the type of emergency the system supports (according to the operator setup as described in Deployment scenarios) at Initial Registration and Mobility Registration Update so the UE has most up to date information always.
5GC shall inform UE about emergency support information regardless of whether system supports emergency itself or not (e.g. via fallback). This ensures consistent behavior for 5GS from the beginning.
This allows the UE (depending on the combination of system provided information and what UE supports) either
  Selects (with or without further assistance such as RAN provided configuration info in broadcast info or RRC, it is up to RAN to develop) to directly set up emergency session (or CS emergency call) by (re)selecting the appropriate system/access. OR
  Selects to set up emergency session via 5GC over the RAT it is connected to or moves to a system that supports emergency sessions (calls) via an Inter-RAT change/reselection (with or without support from 5GS)
AMF provides the emergency support information regardless of whether 5GS supports Voice over IMS or not.

## Slide 5: LIMITED Service State & UE undetected emergency
Limited Service state over 5GS work as today, i.e. 5G RAN must broadcast via System Broadcast information per RAT if supported.
  UE then directly connects to 5GC via that RAT.
No additional special support needed since the broadcast information indicates system wide support of emergency as configured by the operator.
IF UE undetected emergency, then similar to the table for EPC (as defined in 23.167) need to be developed for redirecting the emergency after UE is informed of the call being emergency. Since the UE receives information that the session is emergency via IMS, then the UE has already connected to the 5GS and as such have AMF provided information to determine how to proceed.

## Slide 6: Additional requirements
Dual Connectivity: Assume that Master node B status on emergency is applicable for secondary node B.
Like EPS, AMF provides any Local Emergency numbers which is not part of the existing emergency numbers defined in stage 1.
SSC mode 1 is assumed and as in EPC local breakout (VPLMN) for emergency.
For Slice support:
  In cases 1 and 3 (slide 2), UE should (Shall?) use the same slice as for IMS (Voice over IMS), unless otherwise configured.
  In case of Limited Service state, UE may not be able to provide any information (e.g. No UICC, no subscription etc.). As such UE need not provide any slice info and RAN uses default AMF selection.
Other than Emergency PDU Session, other sessions are not preserved (i.e. no special action taken, if it survives it survives, if user decides to drop them they are dropped).
UE needs to autonomously select/attempt emergency session based on available information. This applies to all 3 types of emergency cases.

## Slide 7: Additional requirements
Session continuity between EPC and 5GC for emergency : TBD
  May keep the session in the current system as long as possible by indicating to RAN to not do Inter RAT/Inter System HO?
  Allow to initiate handover between EPC and 5GC if configured to know that emergency service is supported on target