## Slide 1: 3GPP TSG-SA WG2 Meeting #131 S2- 1901577 Santa Cruz - Tenerife, Spain, 25 Feb - 1 March (revision of S2-19xxxx) Source: Ericsson, … Title: Secured Packet Service Document for: Discussion Agenda Item: 7.1 Work Item / Release: TEI16
Abstract of the contribution: This contribution proposes the principles for a mechanism for UDM to get any parameter to be provided to the USIM in Secured Packet format.

## Slide 2: Background
3GPP Rel 15 enables the delivery of information from the HPLMN/UDM to the UE via a CP procedure.
  Steering of Roaming (SoR)
  Delivery of Network Slicing Subscription Change Indication to UE.
  UE Parameter Update procedure including possibility to …
    Update Default Configured S-NSSAI in UE.
    Routing Indicator in USIM.
This includes a security procedure so that information in transit is integrity protected (using Nausf service) and HPLMN can get prove from UE that the information was successfully delivered.
Some of the updated params in these UCs are targeted for the USIM rather than for the ME.
  SoR and Routing Indicator within UE Param Update.
  Concerns exist that VPLMN AMF may read updated parameters (SoR specially) and that ME’s shall be allowed to manipulate info within USIM.
Therefore the possibility for UDM to provide this information using Secured Packet format as defined in TS 31.115 has been specified. The structure and security of Secured Packets shall comply with ETSI TS 102 225.
It is unclear however how relevant UE parameters composed and secured using Secured Packet as defined in TS 31.115 and ETSI TS 102 225 are made available to UDM.

## Slide 3: Background Gemalto/Orange Proposal
Gemalto/Orange presented a solution proposing a NEW service for SoR protection in SA2 and CT1.
  S2-1812454/S2-1812491 and C1-190340
This proposal is though only proposed in the context of SoR while a more general mechanism will enable that other UE parameters targeted for the USIM (e.g. Routing Indicator) could be covered too.
Additionally, this proposal does not make a proper use of the relevant parameters from a subscription management point of view.
  During registration: The UDM will retrieve in real time the PLMNList (as secure packet) from SoRNF.
    Suggests UDM to fetch SoR info from SoRNF (rather than from UDR) in secure packet already.
  After registration: The SoRNF can push asynchronously a new VPLMN list (secure packet) to UDM. If UE is already registered, the UDM may generate SDM_Update_Notification
    SoRNF pushes SoR info to UDM in secure packet already.
    Understood UDM does not even need to store it in UDR.
This is NOT according how e.g. SoR is defined in Rel 15 TSs; i.e. already part of Data Model UDM fetches from UDR (only in clear text though).

## Slide 4: UDM Parameters in Secured Packet Format Solution Principles
This Discussion Paper proposes a mechanism for UDM to get any SoR info and any other parameter (from now on UE parameters) to be provided to the USIM in Secured Packet format based on the following principles:
  Corresponding UE parameters are stored/updated in clear text format in UDR via provisioning interfaces.
  UDM fetches UE Parameters from UDR via Nudr.
  When UDM determines that UE parameters need to be delivered using Secured Packet format, UDM fetches UE Parameters from UDR and requests its encoding in Secured Packet format to another entity within the HN operator domain.
    The encoding and security of information in Secured Packet format according to TS 31.115 and ETSI TS 102 225 is enabled via a new service used by UDM.
    It shall be possible to use the same service for SoR, RID and other future params requiring it.
  Otherwise (Secured Packet not required) UE parameters can be delivered to the UE via the AMF as fetched from UDR (i.e. in clear text).
  UE parameters are delivered to AMF via Nudm_SDM service within Access and Mobility Data Type.
    UE Parameter Update defined within Access and Mobility Data Type as agreed in S2-1901137.
    The information is integrity protected and proof of reception can be achieved using the corresponding Nausf service (Nausf_SORProtection/UPUProtection_Protect).

## Slide 5: UDM Parameters in Secured Packet Format Solution Overview
ME/USIM
Secured Packet Service
HPLMN AUSF
VPLMN AMF
8. DL NAS TRANSPORT
9. UL NAS TRANSPORT
2. Nudm_SDM_Get Req (SUPI, Access&Mob)
HPLMN UDM
HPLMN UDR
BSS/ CAS
Parameters are stored/updated as subscription data in UDM/UDR
5. SecuredPacket_Get
(SUPI, VPLMN, SoR/RID/…)
1. Registration Initiation and Authentication
3. Decision to Update SoR/RID (using Secured Packet)
4. Nudr_DM_Get
(SUPI, SoR/RID/…)
6. Nausf_SoR/UPUProtection_Protect
(SUPI, SoR/RID/…)
7. Nudm_SDM_Get_Resp/Notification
(SUPI, [SoR/RID/…])
10. Nudm_SDM_Info
11. Registration Completion
ME provides secured packet to USIM

## Slide 6: UDM Parameters in Secured Packet Format Secured Packet Service
This solution proposes a NEW service to enable UDM to encapsulate UE parameters (e.g. SoR, RID, …) in Secured Packet Format.
  It is proposed to define a new optional NF within the 5GC SBA architecture, e.g. Secured Packet Service NF supporting TS 31.115.
    This solution ensures that the key(s) specified in ETSI TS 102 22, needed for securing the Secured Packet, and used in securing Secure Packet sent to the UE using SMS, can be stored in one network entity only.
  The secured packet service is proposed to be defined in a generic way to be able to encapsulate not only SoR but also any other UE parameter (e.g. RID) in Secured Packet format.
  Additionally, this service may be used to enable encapsulation of UE parameters using additional formats beyond Secured Packet.

## Slide 7: UDM Parameters in Secured Packet Format Proposal
It is proposed to agree on the principles for the solution to enable UDM to encapsulate UE Parameters (e.g. SoR, RID, …) in Secured Packet Format.
  Corresponding CRs will be provided in subsequent SA2 meetings.
Inform other 3GPP WGs in due time.
  SA3 to consider any security aspect of the new secured packet service.
  CT1 to rely on this generic secured packet service to encapsulate SoR info in Secured Packet format.