## Slide 1
Hannu Hietalahti
Nokia
NAS PDU delivery failure in RRC Inactive
Proposed way forward in SA2 #138E

## Slide 2: Key Questions
Why SA2 needs to specify error handling requirements
NAS error handling is based on indication received from the NG-RAN over N2
RAN3 asks for clarification of already existing requirements for handling error case that is specified in TS 23.501
Key questions:
Agreed baseline: failure to deliver DL NAS PDU included in PDU Session Release Command will lead to NG-RAN indication of failure back to CN
Question to be answered: Does the NG-RAN in addition run so called “Downlink NAS Non Delivery Indication procedure” which means echoing back to sender the NAS PDU whose delivery to the UE has failed?

## Slide 3: Task for SA2 #138E
Both Reply LS and CR(s) are needed in SA2 #138E
Reply LS is needed to give RAN3 the error handling requirement they asked us to clarify (LS in S2-2002658)
CRs are needed to clarify whether TS 23.501 expression “NAS non-delivery” means failure to deliver the NAS PDU in general or refers to “Downlink NAS Non Delivery Indication procedure” as specified by RAN3 in TS 36.300
  The answer depends on how the NAS PDU was received and these different cases should be identified in 23.501
  “Downlink NAS Non Delivery Indication procedure” applies on DL NAS TRANSPORT
  Otherwise, “Downlink NAS Non Delivery Indication procedure” does not apply

## Slide 4: Proposed way forward
Liaison statement
Take Qualcomm LS S2-2002938 as the basis (because it’s the shortest)
Option 1 in RAN3 LS is the right answer to Q1
  NAS PDU error handling is based on failure indication and it does not need the failed PDU to be returned
If further explanation is needed, the different scenarios from Ericsson LS in 2938 can be added (but “CN” and “implicit vs. explicit” need to be replaced by specific NFs)
Even if something more needs to be added to identify the target NF, echoing back the failed NAS PDU included in PDU Session Release Command is still not needed (except when explicitly stated already)
CRs:
23.501: Revise Qualcomm tdoc 2935 that addresses the minimum change required by the incoming LS by adding the correct RAN3 procedure name “Downlink NAS Non Delivery Indication”
Merge Nokia CR change indicating the cause value in the other case (i.e. when Downlink NAS Non Delivery Indication procedure is not used)
23.502: Align Ericsson tdoc 2777 to address the same decisions in 23.502

## Slide 5: Related documents, AI 6.1
S2-2002658 | LS from RAN WG3: LS on NAS Non delivery for RRC Inactive state | RAN WG3 (R3-201362) | Rel-15 | Responses in S2-2002774, S2-2002867 and S2-2002938
S2-2002774 | [DRAFT] Reply LS on NAS Non delivery for RRC Inactive state | Ericsson | Rel-15 | Response to S2-2002658
S2-2002867 | [DRAFT] Reply LS on NAS non-delivery in RRC Inactive state | Nokia, Nokia Shanghai Bell | Rel-16 | Response to S2-2002658
S2-2002938 | [DRAFT] Reply LS on NAS Non delivery for RRC Inactive state | QUALCOMM Europe Inc. - Italy | Rel-15 | Response to S2-2002658
S2-2002775 | 23.501 CR2244 (Rel-15, 'F'): Clarification on NAS non delivery | Ericsson | Rel-15 | 
S2-2002776 | 23.501 CR2245 (Rel-16, 'A'): Clarification on NAS non delivery | Ericsson | Rel-16 | 
S2-2002777 | 23.502 CR2191 (Rel-15, 'F'): Clarification on NAS non delivery | Ericsson | Rel-15 | 
S2-2002778 | 23.502 CR2192 (Rel-16, 'A'): Clarification on NAS non delivery | Ericsson | Rel-16 | 
S2-2002779 | 23.502 CR2193 (Rel-16, 'F'): Transfer Failure Notification Address handling | Ericsson | Rel-16 | 
S2-2002868 | 23.501 CR2272 (Rel-15, 'F'): NAS PDU delivery failure in RRC Inactive | Nokia, Nokia Shanghai Bell | Rel-15 | 
S2-2002869 | 23.501 CR2273 (Rel-16, 'A'): NAS PDU delivery failure in RRC Inactive | Nokia, Nokia Shanghai Bell | Rel-16 | 
S2-2003011 | [DRAFT] LS Response on NAS Non delivery for RRC Inactive state | Huawei, HiSilicon | Rel-16 | Response to S2-2002658
S2-2002935 | 23.501 CR2290 (Rel-15, 'F'): NAS Non Delivery during AN Release procedure | QUALCOMM Europe Inc. - Italy | Rel-15 | 
S2-2002936 | 23.501 CR2291 (Rel-16, 'A'): NAS Non Delivery during AN Release procedure | QUALCOMM Europe Inc. - Italy | Rel-16 | 
S2-2003012 | 23.501 CR2312 (Rel-16, 'F'): NAS non delivery in case of RRC inactivated state | Huawei,HiSilicon | Rel-16 |