## Slide 1
Proposal to send LS to SA6/SA4 to get feedback on new multicast MBS Session state “inactive”
Source: Ericsson

## Slide 2
Implications to AF/AS to support inactive state (new) for multicast MBS Session
Input from TR 23.757 v1.3.0 and S2-2102945:
  Introduce Inactive state (new) for MBS session (in addition to Active state);
  Propose “Established multicast session in inactive state” (by AF) (in addition to MBS Session in active state);
  UE join rejected if TMGI is allocated but MBS Session is not started/established by AF.
Implications to AF/AS
  AF needs to support new procedures for “inactive state”, including
    AF starts MBS Session (with service requirement e.g., QoS) in inactive state, and then activate the MBS Session;
    AF needs to be able to deactivate an MBS Session (i.e. to change the state from “active” to “inactive”, service requirement still available in 5GC), and then re-activate the MBS Session;
  To avoid UE join rejected by 5GC when TMGI is allocated but MBS Session is not started/established, the existing behavior of AF performing Service Announcement as soon as TMGI is available may need to be changed.
[Proposal-1] Send LS to SA4 and SA6 to get feedback

## Slide 3
Thank You!