## Slide 1: XRM ENs and Issues To be resolved in SA2#157 meeting
Dan Wang(China Mobile), Yixue Lei (Tencent)

## Slide 2: Agenda
Review of ENs for KI#3,4&5
Open Issues
AOB

## Slide 3: ENs for KI#3 – to be resolved
501 CR
  General API exposure
    Editor’s Note1: It is for RAN WGs to confirm whether providing QoS Notification Control for GBR QoS Flow and data rate information can be included in Release 18.
  L4S
    Editor’s Note3: During UE mobility, e.g., NG-RAN handover or local PSA UPF relocation, whether there are other impacts for ECN marking for L4S is FFS.
  QoS monitoring
    Editor’s Note4: It is pending for RAN WG to confirm whether providing measured data rate information for QoS Flow to the CN can be included or not in Release-18.
    Editor’s Note5: It is for pending to RAN WG to confirm whether providing QoS Notification for GBR QoS Flow to the CN via User Plane can be included or not in Release-18.
    Editor’s Note6: It is FFS whether Direct exposure of QoS Notification does need to be part of QoS Monitoring of rather more as an extension to 5.7.2.4 and a new UPF Event.
    Editor’s Note7: It is pending for RAN WG to confirm whether providing QoS Notification Control for GBR QoS Flow via the tunnel between the NG-RAN and PSA UPF can be included in Release-18.

## Slide 4: ENs for KI#4&5 to be resolved
501 CR
  UL PDU set
    Editor’s Note2 : The applicability and details of PDU Set handling in uplink direction is pending RAN WG’s progress.
  AN PSDB
    Editor's Note3: The need for AN PSDB and definition of AN PSDB is FFS.
  New SST
    Editor’s Note6: Whether a standardized S-NSSAI (SST) is defined for XRM or whether non-standardized S-NSSAI is used is FFS
  Scenario for PDU without PDU set information
    Editor’s note: How PDU Set Importance is applied to the PDU(s) that does not belong to a PDU Set based on Protocol Description is FFS.

## Slide 5: Issues to be discussed
Whether and how to process the unmarked PDUs.
Non-homogenous support of PDU set based QoS handling in NG-RAN.(paper)
Whether to support UP based QNC.(paper) related with RAN3 LS
Discussion for L4S mobility issue.(paper)
The New incoming LS from SA4

## Slide 6: Whether and how to process the unmarked PDUs
Paper endorsed(S2-2306239) in last meeting, related with SA4 LS(S2-2303974), about whether and how to process the unmarked PDUs.
    There is an Editor’s note: How PDU Set Importance is applied to the PDU(s) that does not belong to a PDU Set based on Protocol Description is FFS.
The following papers submitted in this meeting:
  S2-2307399(Nokia): UPF still maps PDUs that do not belong to a PDU Set, into a PDU set (e.g. it could be a PDU Set with just that PDU). Do not mention the PDU set importance only remove the EN.
  S2-2307172(Lenovo): Default PDU Set Importance.
  S2-2307293(Xiaomi) UPF maps one or more PDU(s) to a PDU set is up to the implementation. Not resolve the EN for PDU set importance.
  S2-2307314(Meta): UPF applies local policy on setting PDU Set Importance to a PDU Set based not based on Protocol Description
  S2-2307370(Interdigital): Default PDU Set Importance for the PDU.

## Slide 7: Non-homogenous
Doc | Main content
S2-2307178(Lenovo, Meta USA, CATT, Xiaomi,Tencent) | 1.SMF decides whether the NG-RAN supports the PDU set based QoS handling based on N2 SM information from NG-RAN 2.NG-RAN provides the capability information during QoS establishment and handover to SMF.
S2-2307203(ZTE) | Establishment SMF provides the PDU Set QoS parameters in the QoS profile to NG-RAN NG-RAN supports the PDU Set based QoS handling, it replies to the SMF in the N2 SM information indicating that the PDU Set based QoS handling is enabled for the QoS flow. Handover During the Xn based handover if the target NG-RAN receives PDU Set QoS parameters from the source NG-RAN it provides an indication to the SMF in the N2 SM information in the Path Switch request message indicating whether the PDU Set based QoS handling is enabled for the QoS flow. If the SMF does not receive such indication, it may initiate step 2a to 8b of the PDU Session modification procedure (see TS 23.502 [3] clause 4.3.3.2) without including the PDU Session Modification Command message to provide the PDU Set QoS parameters to NG-RAN. If the target NG-RAN supports the PDU Set based QoS handling, it replies to the SMF in the N2 SM information indicating that the PDU Set based QoS handling is enabled for the QoS flow.
S2-2306687(Qualcomm) | If the receiving NG-RAN node does not support the PDU set based QoS handling then the NG-RAN node ignores the PDU Set QoS parameters In case of handover from a non-supporting NG-RAN node to a supporting NG-RAN node, the target NG-RAN node can be configured (e.g., based on the 5QI values associated to the QoS Flow) to provide a positive response to the source NG-RAN node in the handover preparation
S2-2306688(Qualcomm) | Mainly content same as 7203 with more detailed description e.g. AMF SMF interaction,

## Slide 8: Support of UP-based QNC related with RAN3 LS
  Option 1: Support UP-based QNC in SA2 specification
    S2-2306479(CMCC, Verizon): DP and proposal that SA2 can support the UP based QNC mechanism in Rel-18
    S2-2306521 (Tencent, vivo)CR on API-based exposure
    S2-2306522 (vivo)CR on QoS monitoring
  Option 2: Remove UP-based QNC in SA2 specification
    S2-2306607 (Ericsson)
Way forward discussion

## Slide 9: L4S mobility issue
EN content
  Editor’s Note: During UE mobility, e.g., NG-RAN handover or local PSA UPF relocation, whether there are other impacts for ECN marking for L4S is FFS.
Related papers
  6604(Ericsson)
    Target NG-RAN and PSA UPF keep contributing to ECN marking for L4S as the current method
  6991(Huawei)
    Target NG-RAN reports congestion information immediately once the handover occur, which can be used both for API based exposure and UPF-L4S
  6418: (CMCC)
    same idea as 6991 with adding one scenario i.e. source NG-RAN support to report the congestion information while target NG-RAN does not support.
  6525(vivo)
    Option1: same as 6991
    Option2: the SMF provides to the UPF the transferred QoS Flows received from the AMF and the UPF understands no congestion anymore for those QoS flows.
  7397(Nokia)
    SMF may then indicates target NG-RAN to send congestion information (i.e. a percentage of packets that UPF uses for ECN marking for L4S) to the PSA UPF.

## Slide 10: New Incoming LS from SA4(1/2)
LS from SA4(6280)
  Q1 SA4 would like to ask if it is possible for a single QoS flow to include both PDUs marked with PDU set header extension and unmarked PDUs?
Analysis of related papers
  7017(Huawei): (revision of S2-2304717r24 )
    SA2 agreed that a single QoS Flow includes either PDUs with GTP-U header extensions for PDU Sets or PDUs without such extension, but not both.
    If the UPF receives a PDU that do not belong to a PDU Set based on Protocol Description for PDU Set identification, then the UPF still maps it to a PDU Set (e.g. it could be a PDU Set with just that PDU). Aligned with endorsed S2-2306239.
  7035(CATT): the same answer as the first part of 7017.
  7125(Intel): Clarify the first question from SA4. With this understanding the SA2’s answer is as follows: Mixing of PDUs that are marked with the new RTP header extension with PDUs that are not marked with the new RTP header extension in the same QoS Flow can happen as long as the information for QoS Flow matching (refer to the Packet Detection Information in the Packet Detection Rule in TS 23.501 Table 5.8.5.3-1) is the same for both.
  7215(vivo): Answer to Q1 and Q2 are aligned with 7017 but propose to ask two more questions
    Q1: if it is possible for a single RTP stream to include both PDUs marked with PDU set header extension and unmarked PDUs?
    Q2: if the answer to Q1 is yes, please further clarify the motivation that marking packets with PDU Set Header but leaving some other packets unmarked in an RTP stream.

## Slide 11: New Incoming LS from SA4(2/2)
LS from SA4(6309)
  SA2 is kindly requested to provide feedback on the feasibility and value of introducing additional signaling bits related to the End of Burst within the Rel-18 timeframe.
  Rapportuer : The understanding of additional signaling bits is about inter-burst time
Analysis of related papers
  6466(OPPO): no need to introduce such additional bits to indicate inter-burst time
  7125(Nokia): see the potential value of expanding the EoDB, but also tell SA4 that periodicity is introduced.
  7037(CATT): Question for the 3 bit EoDB. Analysis the inter-burst time and no benefit.
  6613(Ericsson): not part of the study conclusions , so not support of the inter-burst time.
  7155(CMCC)not support of inter-burst time.
  6390(vivo) not support of inter-burst time.