## Slide 1: R19 Energysys-Solutions proposed in TR and in August meeting
China Mobile
2024 August

## Slide 2: Summary of solutions- 5GC functionality-determined by SA2
Per UE EC= ECRAN,UE +∑ECupf,UE
EECF do the calculation.
Approach 1: data volume and NF EC information ECupf,ue=*Ecupf， ECran,ue= *ECran
  ECupf , DVran, ECran are from OAM, and the NF ID is provided from UDM to EECF. RAN ID is provided from AMF to EECF.
  DVupf, ue=DVran,ue are from UPF(I-UPF and PSA UPF)
  Approach 2:data volume, UPF EC information, and RAN reporting
  ECupf,ue=*ECupf, ECran,ue=RAN reporting
  ECupf is from OAM, and the NF ID is provided from UDM to EECF. RAN ID is provided from AMF to EECF.
  DVupf, ueare from UPF(I-UPF and PSA UPF)
  For roaming, the V-EECF may report the per UE EC of VPLMN to H-EECF.
UE
UE
UE
RAN
UE
I-UPF
UE
PSA-UPF
UE
SMF
UE
AMF
UE
EECF
UE
NEF
UE
AF
UE
OAM
UE
UDM
UE
5GCNF
Architecture of 5GC supporting EnergySys

## Slide 3: Summary of solutions- OAM based solution-determined by SA5
Per UE EC= ECRAN,UE +∑ECupf,UE
OAM do the calculation.
Formula the same as the slide 2 approach 1, except the CHF provides the DVupf,UE=DVran,ue
SBMA to support per UE EC information exposure to NEF/5GC NF.
Observation:
One problem: CHF does not have I-UPF information. Therefore the OAM cannot generate the I-UPF EC of the UE.
How to support roaming is not clear.
Currently, the OAM manage object focus on NF or NS, not per UE.
UE
UE
UE
RAN
UE
I-UPF
UE
PSA-UPF
UE
SMF
UE
AMF
UE
NEF
UE
AF
UE
CHF
UE
OAM
UE
5GCNF
How to calculate the I-UPF EC of UE is FFS

## Slide 4: Summary of solutions- CHF based solution-determined by SA5
Per UE EC= ECRAN,UE +∑ECupf,UE
Formula the same as the slide 2 approach 1, except the CHF provides the DVupf,UE=DVran,ue
CHF needs to get the ECupf, ECran, DVupf, DVran from OAM
Observation:
Functionality enhancement for CHF to calculate the EC information per UE.
Problem: CHF does not have I-UPF information. Therefore the CHF cannot generate the I-UPF EC of the UE.
How to support roaming is not clear.
How the CHF support to expose EC information to NEF/5GC NF is not clear.
UE
UE
UE
RAN
UE
I-UPF
UE
PSA-UPF
UE
SMF
UE
AMF
UE
NEF
UE
AF
UE
CHF
UE
5GCNF
How to calculate the I-UPF EC of UE is FFS
How to expose the EC of UE is FFS
UE
OAM
Node level EC, DV of RAN and UPF, provided from OAM to CHF

## Slide 5: Summary
Solution# | Per UE EC calculation | Evaluation
5GC New functionality | Approach 1 RAN, I-UPF, PSA-UPF Node level EC from OAM; RAN node level DV from OAM DVupf,ue=DVran,ue Approach 2 ECran,ue reporting from RAN | Node level EC, DVran from OAM Decided by SA2.
OAM | Formula the same as the Sol#1 approach 1, except the CHF provides the DVupf,UE=DVran,ue SBMA to support per UE EC information exposure to NEF/5GC NF. DV from CHF but without I-UPF related information | Specification enhancement in SA5 is needed to support the I-UPF EC information calculation. How to support roaming is not clear, and OAM do not support roaming. Currently, the OAM manage object focus on NF or NS, not per UE. Decided by SA5.
CHF | Formula the same as the Sol#1 approach 1, except the CHF provides the DVupf,UE=DVran,ue CHF needs to get the ECupf, ECran, DVupf, DVran from OAM DV from CHF but without I-UPF related information How to expose is not clear | Specification enhancement in SA5 to support the I-UPF EC information calculation, and the CHF information exposure Interface between CHF and OAM to support CHF getting the ECupf, ECran, DVupf, DVran from OAM Decided by SA5.