## Slide 1
KI#2: Support of a list of satellite IDs and/or S&F monitoring list
We have four options to support of a list of satellite IDs and/or S&F monitoring list sent to the UE:
Option A: Two separate list “List of Satellite IDs” and “S&F Monitored List”, the “List of Satellite IDs” aims to mandate UE not to initiate NAS procedures via a satellite in S&F mode not in the list (i.e. not holding UE context), and “S&F Monitored List” is just an assistance information for the UE with regard to MT traffic delivery; (baseline CR: S2-2500972, Sateliot)
Option B-1 : A single list, e.g., S&F monitoring list, is sent to UE as an assistance information (may) for the UE; (baseline CR: S2-2500782, HW)
Option B-2: A single list, e.g., S&F monitoring list, is sent to UE as a strong recommendation (should) for the UE; (baseline CR: S2-2500782, HW)
Option C: A single list, e.g., S&F monitoring list, is sent to UE as a requirement (shall) to not initiate NAS procedures via a satellite not in the list; (baseline CR: S2-2501026, SAMSUNG)
Option D: A single list, e.g., S&F monitoring list, is sent to UE together with an indication on whether this list is a strong recommendation or just an assistance information for the UE. (baseline CR: S2-2500137, QC)

## Slide 2
Question: Which option can be selected as the way forward:
1. Option A: Two separate list “List of Satellite IDs” and “S&F Monitored List”
Supporting companies: 5
Objections:
2. Option B-1: A single list is sent to UE as an assistance information (may) for the UE
Supporting companies: 16
Objections: 0
3. Option B-2: A single list is sent to UE as a strong recommendation (should) for the UE
Supporting companies: 12
Objections:
4. Option C: A single list is sent to UE as a requirement (shall) to not initiate NAS procedures via a satellite not in the list
Supporting companies: 4
Objections:
5. Option D: A single list is sent to UE together with an indication on whether this list is a strong recommendation or just an assistance information for the UE
Supporting companies: 5
Objections:
Way forward: work on option B-1.
KI#2: Support of a list of satellite IDs and/or S&F monitoring list

## Slide 3
KI#3: how to send SIP re-INVITE during the IMS AGW relocation
We have two options to send SIP re-invite during the AGW relocation:
Option A: IMS-AS initiate SIP re-INVITE during the IMS AGW relocation
Option B: P-CSCF initiate SIP re-INVITE during the IMS AGW relocation
Question: Shall only option A, only option B or both option A and B be supported:
1. Only option A (baseline: S2-2500716 and S2-2500717, NTT DCM)
Supporting companies: 9
Objections: 0
2. Only option B (no baseline CR)
Supporting companies: 4
Objections: 2
3. Both option A and B (baseline: S2-2500627 and S2-2500628, China Mobile)
Supporting companies: 6
Objections: 5
Way forward: standardize only option A.