## Slide 1: Intel views on SA2 6G Study Scope and Organization
Intel

## Slide 2: Introduction
Intel priority is listed on slide #3 - #5 (no specific priority order)
Beside these we also expect general aspects such as 6G architectural assumption/principle, architectural options, 5G to 6G Migration, Interworking aspects, 6G Day-1 services (voice, SMS, etc.) will be part of 6G Study.
We propose 6G SID organization in Slide#6

## Slide 3: Areas for SA2 6G SID Scope/Objectives
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | SBI Enhancements related | Evolve 6G RAN CP to core network interface (“N2”) to SBI Evolve 6G UPF to the core network control plane for session management (“N4”) to SBI | In 5G, the N2 and N4 interfaces remain legacy protocols, specifically NGAP and PFCP, which limit flexibility and efficient service expansion. Evolving N2 and N4 into SBI-based interfaces will enable: More efficient, direct communication (e.g., RAN ↔ NWDAF, LMF) without routing through AMF or SMF. Service exposure for select RAN or UPF functions (e.g., capability exchange, RIM info, configuration transfer). Better support for modular, cloud-native 6G deployments and improved analytics integration (e.g., NWDAF access to UPF or RAN data). | RAN
2 | Compute and communication convergence in 6G network | UE to Network Compute offload Define unified SBI-based interfaces for compute resource advertisement, discovery, orchestration, and service invocation across UE, RAN, CN, edge, and AFs. Enable compute-aware session management and routing (e.g., mobility and handover with compute affinity, session continuity with compute location awareness). Enable AI-driven compute workload distribution across UE, edge, and cloud Enable API exposure and authorize 3rd parties to the computation network. | 5G-Advanced lacks integrated compute-control mechanisms across the network stack. It does not natively support in-network processing, dynamic workload migration, or compute-QoS coordination. Stage 1 (TR 22.870) identifies a need for cyber-physical integration, immersive XR, and real-time AI/ML applications, all requiring joint optimization of compute and connectivity. | RAN – Compute-aware RAN coordination, support for low-latency compute routing SA3: Security related aspects SA5: M&O aspects

## Slide 4: Areas for SA2 6G SID Scope/Objectives
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
4 | AI Support | Enabling AI agent communication How to identify an AI Agent, how to authorise access to a different AI Agent and how to establish and maintain secure association between AI Agents. Interoperability between the AI Agents needs to be provided when the collaborating AI Agents are implemented in different networks. Communication domain dynamically created for users and AI agents from multiple groups to communicate with each other for a specific task during a specific time. 6G network support for AI applications (AI-as-a-Service) The 6G network should be able to securely provide the trained AI/ML model between the operator managed data network (e.g. edge compute domain) and the authorized 3rd party. Supporting AI model training, inference, and management Subject to operator’s policy, the 6G network should be able to provide AI service (e.g., AI model inference) to a UE. | 6G networks is expected to natively support and facilitate AI-driven applications, services, and use cases. It involves creating a network architecture that can efficiently handle the unique requirements of AI workloads, such as large data volumes, low latency, and high computing. Using AI technologies to enhance and optimize 6G network operations, performance, and management - to enable intelligent automation, efficient resource allocation, enhanced security, and improved service delivery Support new service requirements as listed in stage-1 TR 22.870, clause 6. | RAN
3 | Unified data framework | A unified data framework which is use case agnostic : Standardized unified data service interface for data collection/exposure across diverse providers and consumers (UE, RAN, OAM, AF) Unified logical storage functionality centralized or distributed modes to cater for scalability and resilience. Unified security and privacy protection mechanisms, addressing varying sensitivity levels (e.g., anonymization for user data, encryption for ML models). Standardized data formats, ensuring compatibility and seamless integration across heterogeneous data sources. The data life cycle management includes handling data from its creation to its destruction, encompassing the following stages: data creation (e.g. collection, produce), storage, exposure, and deletion. | Current approaches, including MDT-based, LPP-based, NWDAF-driven, DCAF-based methods introduce significant complexity in data gathering across Control Plane and User Plane. The fragmented solutions based on individual use cases have standards overhead as well as duplicate data collection. | RAN, SA3, SA5

## Slide 5: Areas for SA2 6G SID Scope/Objectives
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
5 | Integrated Sensing and communication | Architecture and function enhancements to support sensing. Sensing data and the associated information collection and transport mechanisms for result calculation. Discovery and selection of sensing entities based on service requirements triggered by the service request and capability of the sensing entities. | ISAC working ongoing for 5GA. ISAC Architecture should be G agnostic and should apply to 6G. | RAN, SA3
6 | Ubiquitous Connectivity | Standardized service and control interface for dynamic coordination across heterogeneous access types, including terrestrial (macro/small cell), non-terrestrial (LEO/MEO satellites, HAPS, UAV), and non-3GPP networks (e.g., Wi-Fi, fixed). Unified mobility management architecture supporting seamless inter-access mobility and service Unified data and session management for multi-access devices with simultaneous connectivity (multi-link), enabling predictive handover and session persistence across coverage domains. Support for NTN-specific QoS mechanisms, slicing extensions, and session/policy retention across TN-NTN transitions. Network-aware resiliency framework for fallback, coverage recovery, and service assurance under limited or degraded connectivity (e.g., in disaster scenarios, rural zones, or edge-of-coverage zones). | Stage 1 (TR 22.870) outlines service continuity and ubiquitous coverage expectations across land, sea, air, and space domains. To deliver seamless experience and reliable service across vastly different environments and speeds (e.g., LEO satellite, bullet trains, UAVs), a converged and intelligent 6G networking framework is needed. | RAN: mobility procedure enhancements and multi-link support.

## Slide 6: Consideration for SA2 6G Study Organization
Single Technical Report (TR):
  A single TR should be used, enabling a structured and consistent architectural study.
  Single TR will serve as a reference document for external organizations, ensuring alignment across the industry.
  SA2 SID should list key Work Tasks (WTs) under the objective clause of the SID along with the rough TU estimates.
Study may be organized into two phases
  Phase 1:
    General aspects: Focus on architectural assumption/principle, architectural options, 5G to 6G Migration, Interworking aspects, 6G Day-1 services (voice, SMS, etc.), etc. Phase 1 should be under single stream.
    Additional WTs can be introduced (during Phase 1) if new study areas emerge during the early phase of the study in SA2, i.e. after SID approval in June plenary, or based on the SA1 6G SID progress.
    Timeline: June 2025 – Dec 2025. Checkpoint is Sep/Dec 2025 with possible SID revision with additional WTs.
  Phase 2:
    Additional aspects: New 6G features/services support, solutions evaluation, and conclusion (including for phase 1 topics). Parallel stream may be organized if needed.
    Timeline: Jan 2026 – Dec 2026/Mar 2027.