## Slide 1: Views on Priority Topics for 6G System Architecture SID
Deutsche Telekom

## Slide 2: Outline
Increase network efficiency and sustainability
  For eMBB use case as main goal
  Minimize the adoption of multiple options for the same functionality, avoid excessive configurations
  Clearly highlight benefits vs. added complexity. No complexity for the sake of “making something new”
  More efficient, flexible and stateless User Plane
5G SBA as basis for 6G system architecture
Prepare change from Word to Markdown and use of Git

## Slide 3: View on 6G SID Scope Content for Architecture requirements
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
1 | SBA as basis for 6G System Architecture | Consider 5G-SBA as starting point for 6G Study more cloud-friendly architecture and protocols within CN and between CN/RAN functions, including benefits of a full SBA and full SBI Replacement of remaining P2P interfaces by SBI (N2, N4) | Mix of P2P & SBI not cloud-friendly. Difficulties with cloud automation Full SBI = easier to manage in cloud | RAN
2 | Migration, co-existence and Interworking | Voice, IMS and roaming from Day 1 Migration, co-existence and interworking from/with 5G. No 2G/3G/4G IWK Fallback solutions should be avoided | Not repeating 5G’s failure. Voice in 5G took long Expected very strong 5G-SA position when 6G is introduced | 
3 | User Plane Improvements | Study more flexible, efficient and stateless UP communication Include both N3 and N9 | Allow more stateless UP processing Allow better coupling between TN and UP | RAN, potentially SA3
4 | Reshaping of NFs | Improve procedure flows Improvement of NFs / NF Services Re-use 5G NFs where possible, enhance where needed | Current procedures are immensely long, complex and chatty Increase efficiency | 
5 | Consistent AI/ML framework | Cross-domain AI/ML model life cycle management (led by SA5) Multi-vendor-interoperability | No framework for interoperability of AI/ML within 3GPP | RAN, SA5
6 | Integration of Non-3GPP accesses | Converged control plane for non-3GPP accesses (Wifi, Fixed, Cable) N3IWF as basis | Increase efficiency | RAN
7 | NAS evolution | Direct NAS communication between UE and NFs including msg. distribution | AMF as single entry point limits topology Hop-by-hop NAS security | Potentially RAN SA3

## Slide 4: 6G Study organization
Start with a single TR
Additional TRs for specific topics for easier document handling
Preparation for usage of developer friendly tools for specification (e.g. Git) development during the study
  Prepare change from Word to Markdown and usage of Git in SA2
Review and update of “Best Practices for SA2 studies” during the study