## Slide 1
Discussion for 6G Study on Service Plane
Agenda item: 30.7
Source: Samsung
Document for: Discussion
3GPP SA WG2 Meeting #168
07 – 11 April, 2025, Goteburg, Sweden
S2-2503669

## Slide 2
“Service Plane” for 6G Services
Operator services in 6G (e.g., AI/ML, sensing) require large data transmission which may cause negative impact on essential control plane signaling (e.g., for mobility/session management)
Operator services integrated with the control plane functionalities does not allow the independent scalability, evolution, deployment of 6G services
User plane is mainly for data services and not suitable for operator services
Proposal
6G architecture should be designed to support new characteristics of 6G Services (e.g. sensing, AI/ML) which are different than traditional telecommunication services
UE
RAN
Service
Plane
Sensing
AIML
User Consent
Location
IoT
Control
Plane
MM
SM
User
Plane
UP
DN
UE
RAN
SRB
DRB
CP Tunnel
New Interface
New 6G Service
MM
SM
Control Plane
Service Plane

## Slide 3
Data Management with User Consent
Data management in service plane should support user consent mechanism (e.g., acquisition, revocation) for data collection, processing, exposure subject to user privacy
Data management in service plane should support authorization for NFs to access data in other plane
Motivation
6G architecture should support the means of data management to use data in different planes (i.e., Control Plane, Management Plane and Service Plane), in conjunction with user consent
RAN
Service
Plane
Sensing
Data Mgmt.
User Consent
Control
Plane
MM
SM
Management Plane (OAM)
MDT
AIML
Data
UE
User Consent
Function
Consumer NF, e.g. Sensing
Data Mgmt.
Function
User consent
Service Plane
In any plane
Producer NF,
data storage
In any plane

## Slide 4
6G System Architecture Study Objectives
1. Architecture and protocol of service plane for 6G services (e.g., sensing, network AI, AI agent, data management, user consent management, configurations for UE)
2. Data and signal transmission mechanisms for 6G services in the service plane
3. Discovery/selection mechanisms for service plane entities
4. Data management functionality with consideration of user consent
Proposed Key Objectives
Support of accommodation of 6G services in a separate plane from the control/user plane functions for independent scalability, evolution, and deployment of 6G services