## Slide 1: Way forward of AIML KI#2 handling
S2-2510222
Samsung

## Slide 2: Summary of KI#2 UC#2
The overall Agreed Principles for KI#2 UC#2 are relatively stable.
New company proposals:
  S2-2510045, SKT et al.: add OAM and AF as analytics consumers.
    [Proposed way forward]: discuss AF as a consumer. Not clear motivation of adding OAM as a consumer, as OAM does not determine QoS. -> [drafting session] move it to UC#1 discussion
  S2-2510061 Nokia: add ‘traffic pattern ID’ as input and output to both UC#1 and UC#2.
    [Proposed way forward]: discuss ‘traffic pattern ID’ under UC#1. -> [drafting session] several companies did not agree with this new parameter.
Proposed way forward for KI#2 UC#2:
  Editorial improvement based on contributions.
  Adopt the agreed principles as the conclusions for normative work.

## Slide 3: Comparison between UC#1 and UC#2
UC#1 is for abnormal traffic detection and prediction, and further mitigation.
Analytics consumers: PCF, SMF, UPF
NWDAF Input parameters: Information from the UPF or SMF to identify the abnormal traffic pattern that can contain:
  Source of traffic (e.g. IP packet filter(s), IP Protocol (TCP, UDP, etc.), application ID, etc.).
  Traffic flow filters.
  Identification of corresponding UEs.
  Information of traffic characteristics.
UC#2 is for QoS determination/ optimisation.
Analytics consumers: PCF
NWDAF Input parameters:
  Information identifying the associated application/service data flow(s), e.g. packet filter, application ID of the traffic flow.
  Information identifying the associated UEs.
  Information related to the data flow characteristics, including, N6 delay, congestion information, indication that UPF drops packets and packet drop rate, data volume, packet delay, data rate, periodicity, and packet interval.
Observation: there are common parameters for NWDAF input. However, the logic of the 2 UCs are different. For example, for UC#1, UPF will be required to perform data pre-processing for abnormal traffic.

## Slide 4: Comparison between UC#1 and UC#2
UC#1 NWDAF output parameters:
  Type of abnormal traffic, e.g. abnormal traffic due to DDoS, abnormal data packets patterns, unexpected traffic volume or burst.
  Volume, rate or burst size of abnormal traffic.
  Identifiers/addresses of affected UPF(s), UE(s), PDU session(s).
  Identifiers/ information of the source, e.g. IP packet filter(s), IP Protocol (TCP, UDP, etc.), application ID, etc.
UC#2 NWDAF output parameters:
  Maximum Burst Size/ Maximum Data Burst Volume, Maximum Bitrate, Guaranteed Bitrate, 5GS delay, Packet Error Rate, Periodicity.
  Corresponding information of the traffic flow, e.g. the Application ID and/or Packet Filter Set, identifier of the service data flow(s) of the target application(s).
  Identifiers of affected UEs, e.g. UE ID(s).
Observation: there are common parameters for general identification info, e.g. UE ID, traffic flow identification; however, the key output parameters for UC#1 and UC#2 are different.
Proposed way forward for KI#2 handling:
  Handle the conclusions for UC#1 and UC#2 separately during study phase.
  Discuss whether to use single or separate Analytics ID(s) in normative phase, e.g. based on potential CRs.
[drafting session] Need decision regarding the new analytics ID(s) during SI or or postpone it to normative phase? Potential SOH