## Slide 1
Source:
Tim Woodward
Motorola Solutions
tim.woodward@motorolasolutions.com
+1-480-966-2688
MCData SDS security
3GPP TSG SA3 MCSEC teleconference S3-170102
26 January 2017

## Slide 2: MCData SDS security elements
 | Private SDS on signaling plane | Group SDS on signaling plane | Private SDS on media plane | Group SDS on media plane
Protocol | SIP MESSAGE (rfc 3428) |  | XMPP (rfc 6120 & 6121) | 
Client-server and server-server confidentiality* (protects identities) | S/MIME using CSK or SPK |  | TLS | 
Client-server and server-server integrity* | UL: Signed with source private signing key DL: signed with server private signing key S-S: Signed with server private signing key |  | TLS | 
End to end SDS confidentiality | SDS encrypted on PCK | SDS encrypted on GCK | XMLenc using PCK | XMLenc using GCK
End to end SDS integrity | SDS signed with source private signing key | SDS signed with source private signing key | XMLDSig using source private signing key | XMLDSig using source private signing key
Key protection | PCK encrypted on target public key | n/a | PCK encrypted on target public key | n/a
* Not sure how this works with S/MIME

## Slide 3: MCData Messages with security
MIKEY-SAKKE payload
PCK or GMK-ID and Group ID
Encrypted on target public key or GCK
SDS payload
Encrypted on PCK or GCK
Signed with source private signing key
SIP Header
(addressing)
Identities
(source + target)
Signature over full SIP MESSAGE
S/MIME
using CSK
or SPK
SIP MESSAGE
(signaling plane)
XMPP MESSAGE
(media plane)
MIKEY-SAKKE payload
PCK or GMK-ID and Group ID
Encrypted on target public key or GCK
SDS payload
Encrypted on PCK or GCK
Signed with source private signing key
HTTP Header
(addressing)
Identities
(source + target)
XMLDSig over full MESSAGE
TLS
using CSK
or SPK
Signature included in outer layer encryption?

## Slide 4: Additional points
SIP MESSAGE method
  Is this SIP message type a problem for SIP border routers?
    What about clear versus encrypted?
  Can we protect it with S/MIME? Why not?
    The “MESSAGE” message type already indicates what’s in its payload, so do SIP border routers need to read the actual content like with REGISTER, PUBLISH, NOTIFY, etc?
    If the element/attribute name must be readable, then we are back to defining a unique XML end to end solution with an “SDS” element/attribute that has an XMLenc and XMLDSig protected value.