## Slide 1: FS_eXR (Feasibility Study on Enhancement of XR media service)
Shuai Zhao, intel
Shuai.zhao@intel.com

## Slide 2: Justifications
The study of TR 23.700-60 in SA2 introduced the PDU set concept and identified the potential approaches and benefits of applying such concepts into the 5G system to improve XR services transmission efficiency and better QoE. The concept of the PDU set has quite an impact on both UE and the network sides. To support media packet grouping, in the sense of PDU set, the 5G system not only needs to support media parameters per PDU set from the UE, it is also necessary for the 5G network middlebox to have new features to support new PDU set related metadata sent from UE.
From a video codec point of view, it is necessary to study how high-level network and low-level coding layer of video codecs parameters, when applicable, can be used for 5GS to identify the PDU set boundaries and their importance. The existing assumption of TR 23.700-60 is that XR media service is mostly using transport protocol of RTP/SRTP-based approaches. For RTP/RTSP based solution to be used for signaling and carrying extra XR media metadata into the 5G system, it is necessary to study how existing RTP/SRTP specifications can be applied or extended.
To improve QoE over 5G system based on PDU set granularity, it is necessary to study the traffic pattern of PDU set in streaming sessions. Study of QoS using 5QI for PDU set is necessary for QoS flow configuration based on PDU set traffic characteristics. For QoE measurement on PDU set, it is necessary to identify new QoE metrics.
Existing RTP-based solutions documented in TR 23.700-60 for PDU set identification is not suitable for modern low-delay real-time communication applications such as WebRTC. It is necessary to study how encrypted RTP applications can still be useful for PDU set related XR services in 5G system without increase 5G network middleboxes’ complexity such as using deep packet inspection (DPI).
Both RAN1 38.838 (Study on XR (Extended Reality) Evaluations for NR and RAN2 TR 33.835 investigated power saving and capacity enhancements techniques tailored for XR services, as well as means to provide XR-awareness in RAN. It might be necessary to provide recommendations on how PDU set related streaming can have any impact on those issues.

## Slide 3: Objective Summary
Enabler for XR services based on PDU set.
Enhancement for PDU set QoE
Enhancement for secure-RTP based PDU set XR streaming:
Enhancement for RTP/SDP cross-layer optimization for PDU set:
Generate a Technical report

## Slide 4: 3GPP SA2 FS_XRM RTP based solution
PDU Set: A PDU Set is composed of one or more PDUs carrying the payload of one unit of information generated at the application level (e.g. a frame or video slice for XRM Services), which are of same importance at application layer. All PDUs in a PDU Set are needed by the application layer to use the corresponding unit of information. In some cases, the application layer can still recover parts of the information unit, when some PDUs are missing.
In order to identify the PDU set boundary, the proposed solutions of #12 and #14 in 23700-60 [1] can be categorized into two groups of using:
IETF RTP [2] /SRTP [3] header
IETF framemarking [4] (using RTP header extension [5] mechanism)
The above-mentioned solution (i) is mainly targeted for video codecs including H264/H265/H266/VP8/VP9 using IETF payload format specification in reference [6-10]. Solution (ii) is merely useful for H.264/H.265 or VP8/9, with the assumption that IETF framemarking working group draft [4] will be published in due time.
The key insight of using solutions (i)(ii) for PDU boundary identification is when a non-encrypted RTP protocol is being used, not SRTP. With non-encrypted RTP, the assumption is the following [6.12.3.2 of 23700-60]:
UPF can identify the PDUs of one PDU Set via different ways, e.g. the RTP headers/payloads in case RTP is used, the traffic periodicity. The UPF then add marks in the GTP-U headers of DL packets to assist RAN for the PDU Set identification, e.g. the start/end indication of the PDU Set and PDU Set ID. The identification of PDU Set depends on what the PDU Set represents, e.g. a video frame or a video slice.
PDU Set Information identification
Notes: https://www.cs.columbia.edu/~hgs/rtp/faq.html
https://www.kurento.org/blog/rtp-i-intro-rtp-and-sdp

## Slide 5: Observations on PDU Set Information identification
In the case of non-secure RTP XR application:
  NALU-based header inspection (e.g., H264/H265/H266/VP8/VP8)
  Framemarking
  Cons:
    Solutions may work only for a few codes with NALU. Framemarking is expected to be experimental in nature
    Non-secure RTP may not be practical with real-time communication applications like WebRTC..
In the case of secured RTP (e.g., SRTP) XR application:
  SA2#153e agreed to support the option where the PDU Set Information is derived at the PSA UPF based on Deep Packet Inspection (DPI) of the RTP/SRTP header and payload based on “instruction from SMF”,
  Cons:
    DPI is computing “expensive” and the current approach is beyond the general five-tuple (IP/Port/App-protocol)
    Currently, there is no deployment recommendation on HOW such a DPI mechanism should be applied to WHAT RTP parameters.
Based on RTP-related solution in TR 23.700-60
Notes: S2-2210222

## Slide 6: Enhancement for PDU set QoE
Study and define PDU set parameters (e.g., PDU set size, delay, jitter, latency, burst/loss ratio)
Study and document the traffic pattern of PDU set based network flows by means of simulations and evaluations based on defined PDU set parameters.
Specify additional relevant KPIs and QoE Metrics for PDU set based XR media services.

## Slide 7: Enhancement for secure-RTP based (e.g., SRTP) PDU set XR streaming:
Study whether and how non-secure RTP-based solution can be applied to secure-RTP based XR application

## Slide 8: Enhancement for RTP/SDP cross-layer optimization for PDU set
Identify the use case of cross-layer signalling
  Note: Solution will be depended on 5G_RTP work progress and solution in TS 26.522
define a 3GPP-specific RTP header extension for PDU set usage.
  Note: in case of interoperability, collaboration with IETF may be necessary.
define SDP attributes and parameters for PDU set cross-layer communication
define APIs for signalling PDU set parameters to 5GC

## Slide 9: Generate a Technical report
Documenting the finding mentioned in above objectives.
Provide recommendations whether and how PDU/PDU set may be appropriate.
Identify potential normative work in 3GPP SA4.

## Slide 10: IETF RTP related specifications
RTP: RFC 3550/RFC3551(RFC8860)
RTP Generic Header Extension: RFC 8285
SRTP RFC 6904
IETF Maque WG:
Frame Marking RTP Header Extension
S-Frame: Secure Media Frames
Proxying UDP in HTTP: RFC 9298
RTP header from hint track TS 26.244 [23].
RTP payload format for h264/h265/h266/vp8/vp9/Av1-v1.0/h264-svc
IETF draft: Discarding Priority of RTP Video Packets, PPT
IETF masque WG: Multiplexed Application Substrate over QUIC Encryption
RFC 4585/8861: Sending Multiple RTP Streams in a Single RTP Session
RFC 6958 RTP Control Protocol (RTCP) Extended Report (XR) Block for Burst/Gap Loss Metric Reporting
RFC 8082 Using Codec Control Messages in the RTP Audio-Visual Profile with Feedback with Layered Codecs
More relevant draft may be added in future.

## Slide 11: 5G QoS, UPF, GTP-U Tunnels
Architecture Overview
PDU Session and Default QoS-Flow
User Plane Traffic and GTP-U Tunnels
IETF related GTP-relevant protocols:
  IETF 3GPP 5G UPF protocol arch analysis
  RFC8899 Packetization layer path MTU discovery (PMTUD)
3GPP TS29.281 General Packet Radio System (GPRS) Tunnelling Protocol User Plane (GTPv1-U)
Notes: https://derekcheung.medium.com/5g-core-pdu-session-and-qos-part-1-a12852e1b342
https://derekcheung.medium.com/5c-core-pdu-session-and-qos-part-2-52bb72cb0ff7
https://derekcheung.medium.com/5gc-part-3-user-plane-and-gtp-u-tunnels-53319463967
https://datatracker.ietf.org/meeting/102/materials/slides-102-dmm-user-plane-protocol-and-architectural-analysis-on-3gpp-5g-system-00

## Slide 12: IETF Media Over QUIC WG
Use Cases and Requirements for Media Transport Protocol Design
QuicR - Media Delivery Protocol over QUIC
  Protocol: https://datatracker.ietf.org/doc/draft-jennings-moq-quicr-proto/
  Architecture: https://datatracker.ietf.org/doc/draft-jennings-moq-quicr-arch/
Warp - Segmented Live Media Transport
MOQ Extensions for Relays to Support High-Throughput Low-Latency Traffic
Design Space Analysis of MoQ
RTP over QUIC
IETF MoQ

## Slide 13: RAN2 Study on XR (eXtended Reality) enhancements for NR
Both RAN1 38.838 (Study on XR (Extended Reality) Evaluations for NR and RAN2 TR 33.835 investigated power saving and capacity enhancements techniques tailored for XR services, as well as means to provide XR-awareness in RAN.
TS 38.835
Notes: https://portal.3gpp.org/desktopmodules/WorkItem/WorkItemDetails.aspx?workitemId=940087

## Slide 14: CDN/Edge support for PDU set