## Slide 1: Latency Measurement and Control in 5GMS
Source: Qualcomm Incorporated
Agenda Item: 8.7
Document for: Discussion and Agreement
3GPP TSG-SA4 Meeting #132 S4-250827
Fukuoka, JP, 19 -23 May 2025
tsto@qti.qualcomm.com

## Slide 2: Background
BBC in Project Timbre identified latency as an important measure
In the Project Timbre work that was presented to 5GMAG a few months ago (i.e. how well audio streaming works over mobile networks) it was outlined that the latency of each audio segment was a key indicator of quality of service for the listener.
It’s possible to measure the segment latency in the client app, as is being done in the project. It would also be helpful to be able to measure latency, of one kind or another, from the network side.
The information may be exposed as an API in the network.
https://www.bbc.co.uk/rd/blog/2024-03-project-timbre-investigating-mobile-coverage-for-live-radio-streaming-on-bbc-sounds

## Slide 3: Basic Problem Statement
In an Adaptive Streaming environment using Segments (typically CMAF objects), and a manifest such as DASH or HLS, the service provider wants to control the end-to-end latency, possibly also for synchronized playback across the clients, but also wants to measure the latency and report this information back to the network or service provider.
Latency is typically measure from glass-to-glass or measured from encoder to glass.
Information on the latency may include
  what the actually latency is
  If a desired target latency is met
  The deviation from the target latency
  The reason for the target latency: late arrival, network issues, user controlled, etc.
The network and/or service provider may use this information to
  Do a QoE measure for each client
  Do some network improvements if the latency is not met, e.g. Content Steering, QoS, etc.
  Aggregate the information across multiple/all users

## Slide 4: Basic Architecture
Network
Aligned with DASH-IF
Encoder
Packager
Manifest generator
Origin Server
Distribution (CDN, Broadcast)
Media Client
Time Sync Server
Reporting Server
API

## Slide 5: Setting up latency measurement
Clause 9.X.6.2.3:
  The Producer Reference Time supplies times corresponding to the production of associated media. This information permits among others to (i) provide media clients with information to enable consumption and production to proceed at equivalent rates, thus avoiding possible buffer overflow or underflow, and (ii) enable measuring and potentially controlling the latency between the production of the media time and the playout.
  The Producer Reference Time ('prft') as defined in ISO/IEC 14496-12.
  The information may be provided inband as part of the Segments in the ('prft'), in the MPD or both. In the context of the low-latency DASH service offerings, providing information in the MPD is strongly recommended, whereas providing inband information is left to the deployment.
  The producer reference time permits the DASH client to control the End-to-End Latency (EEL) or the Encoding+Distribution Latency (EDL), and permits the service provider to provide information to the client to control this value.
  If the CMAF Switching Set contains ('prft') information and the flags is set to 0 or the flags 8 and 16 are set, then the value of the timestamp in the producer reference time expresses the encoding time in wall-clock time of the corresponding presentation time. If this information is available, then it should be exposed to the MPD by adding a Producer Reference Time element ProducerReferenceTime as follows:
  - @id is set to a unique value in the context of the Media Presentation
  - @inband is set to true
  - @type to encoder for flag set to 0 or not present as this value is the default value..
  If the CMAF Switching Set contains ('prft') information and flags 8 and 16 are set, then the value of the timestamp in the producer reference time expresses the capture time in wall-clock time of the corresponding presentation time. If this information is available, then it should be exposed to the MPD by adding a Producer Reference Time element ProducerReferenceTime as follows:
  - @id is set to a unique value in the context of the Media Presentation
  - @inband is set to true
  - @type to captured for both, flag 8 and flag 16, being set.
  Regardless, whether the inband information is present or not, it is recommended to provide information in the MPD for the @wallclockTime and the @presentationTime.
  Assume that a value wall-clock WC is known that corresponds to a presentation time PT, either by the availability of a pair of for ntp_timestamp and media_time as contained in a ('prft') as defined in 8.16.5 of ISO/IEC 14496-12 or by other means. Also, it is assumed that the value of the @presentationTimeOffset PTO is known. The MPD packager should act as follows:
  - derive the wall-clock time WCA that corresponds to the PTO, namely WCA = WC + (PT – PTO)
  - convert the WCA into the format of a UTCTiming element format present in the MPD
  - add this UTCTiming element into the Producer Reference Time element ProducerReferenceTime
  - add the value of PTO to the @presentationTime
  - add the value of WCA to the @wallclockTime
  Note that multiple producer reference time elements may be added, for example one to support measuring End-to-End Latency (EEL) (@type="captured") and one to measure Encoding+Distribution Latency (EDL) (@type="encoder").
Prepublished v5 on Low-Latency Modes for DASH https://dash-industry-forum.github.io/docs/CR-Low-Latency-Live-r8.pdf

## Slide 6: Latency Measurement
Clause 9.X.5:
4. For DASH-IF low-latency clients shall compute the presentation latency within each Period based on a wall clock anchor WCA and a presentation time anchor PTA. WCA and PTA are determined as follows:
  a. If the ProducerReferenceTime element is present as defined in clause 9.X.4.2, then the
    i. The information of a UTCTiming element contained in this ProducerReferenceTime shall be used for clock-synchronization.
    ii. WCA is the value of the @wallClockTime in a format as specified by depending on the scheme of any UTCTiming element contained in this ProducerReferenceTime.
    iii. PTA is the value of the @presentationTime contained in this ProducerReferenceTime minus the value of the @presentationTimeOffset of the corresponding Representation. Note that this value is 0 for the first element, which may be the only element.
    iv. TS is the @timescale of the corresponding Representation.
    v. If the @inband attribute is set to TRUE, then the client should parse the Segments to re-verify the difference of PTA/TS and WCA based on the information in a 'prft' box included in Segments.
  b. Else
    i. WCA is the value of the PeriodStart, i.e., the sum of MPD@availailityStartTime and Period@start,
    ii. PTA is the value of the @presentationTimeOffset
  c. Then the presentation latency PL of a presentation time PT presented at wall clock time WC in seconds is determined as PL = (WC – WCA) - (PT – PTA)/TS.
Prepublished v5 on Low-Latency Modes for DASH https://dash-industry-forum.github.io/docs/CR-Low-Latency-Live-r8.pdf

## Slide 7: Latency Measurement
Clause 9.X.5:
5. It shall implement means to support the service description functionality (either in the DASH client signaled through MPD or by the means of an API, precedence is implementation specific). The parameter interpretation is as follows:
  a. The client when consuming in live mode, it should play the content within 500ms tolerance of the target latency taking into account the above computation for latency. However, the client should consider meeting the latency target also by taking into account knowledge of its own capabilities, the network conditions, and any relevant knowledge of past streaming performance. DASH-IF low latency clients should implement the Presentation time target and constraints in clause 10.20.4 of the DVB-DASH specification.
  b. If the max latency is set, the service provider indicates the maximum presentation latency in milliseconds. This value indicates a content provider’s desire for the content not to be presented if the latency exceeds the maximum latency. A client when consuming in live mode, should not exceed the described max latency and, if it happens, inform the application that this event happens. Examples to maintain the latency may be to switch to lower available bitrates, drop certain media components, or other means to maintain the latency, to the extreme to even terminate the service.
  c. If the min latency is set, the client shall not fall below the described min latency.
  d. If the playback speed element is present, clients should use these tools to adapt to the target latency but should not exceed the max/min playback rates. DASH-IF low latency clients should implement the catch-up modes in clause 10.20.6 of the DVB-DASH specification.
Prepublished v5 on Low-Latency Modes for DASH https://dash-industry-forum.github.io/docs/CR-Low-Latency-Live-r8.pdf

## Slide 8: Basic approach to address the problem of low-latency
Provide producer reference times
  Add to manifest
  Add prft into CMAF Segments
Synchronize client and server
  External means
  Use UTCTiming
Potentially create a service description for desired latency
Measure the latency
Report the latency/latency offset to the network
  DASH Metrics, CMCD
  Inband reporting or external reporting.
Use the reports in the network for optimization
Latency aggregation
  Aggregate the latency in the network
  Create network APIs that expose the observed latency.
This is aligned with DASH-IF Low-latency modes

## Slide 9: Basic measurement
A media client is time-synchronized to a network function that generates a producer reference time and carries this time in the media and the client the uses producer reference time information in the media to measure the latency and reports the observed latency of a media sample or derived information back to the network where the producer reference time is a pair of media time and wall-clock time, and the media time relates to the wall-clock time.
The details of the measurement is following:
  The information documented in the producer reference time is used as an anchor and media time is MTA and the wall-clock time is WCA
  A timescale is known from the media that documents the units per second as TS.
  Then media time latency MTL of a media time MT presented at wall clock time WC in seconds is determined as MTL = (WC – WCA) - (PT – PTA)/TS
Example: Let the timecale be set to 20. Assume the media time of a sample being 3740 and the presentation time is presented at 20:18:10.5 and the anchor of the wall-clock time is 20:15:00. Then the presentation latency of the sample is derived as 190.5s - 3740/20 s = 190.5s - 187s = 3.5s.

## Slide 10: Some specifics
The producer reference time may be
  the capture time of the media sample
  the encoding time of the media sample
  Any other relevant time relevant for the network provider
The Time Synchronization is accomplished by UTC Time Sync in DASH
Producer reference time can be carried in Segments, Manifest or is implicit (see DASH-IF)
Reporting of latency may be done in DASH metrics or CMCD
Latency metric may be measured, but also other information such as latency deviation from target latency, reasons for latency and so on
API for exposure may use NWDAF or any other defined API

## Slide 11: Instantation 5G Media Streaming

## Slide 12: Example: CMCD in 5G Media Streaming

## Slide 13: Summary
This was discussed in MPEG and SVTA
The extensions are minimum, more or less just making sure to address the metric
Proposal for 3GPP
  Add this as a potential key issue for Rel-20 AMD
  Define the necessary metrics and call flows to support the feature
  Leverage 3GPPs reporting
Implement in 5G-MAG Reference Tools