## Slide 1
Overview of Service Interactivity in ATSC
Charles Lo, Qualcomm Incorporated
Jan 26, 2015
S4-150048

## Slide 2: ATSC 2.0 Interactive Service Architecture
Broadcaster
ATSC 2.0 iTV Server
Broadcaster
ATSC 2.0 iTV Server
ATSC 2.0
Receiver
(TV Set)
Home Gateway
Home Network
ACR
Server
Triggers
Broadcaster
ATSC 2.0 iTV Server
Internet
TDO,
TPT,
Files
Triggers
Broadcasting
System
Broadcast
Network
Triggers
(DTVCC)
A/V,
TDO,
TPT,
Files
Broadcasting
System
Broadcasting
System
HTTP
Proxy
Server

## Slide 3: ATSC 2.0 Interactivity Framework (1 of 3)
Components of interactive services:
  TDO Parameter Table (TPT)
    Data structure containing information about the TDOs of a program and associated interactivity-related events initiated by Triggers
  TDO (Triggered Downloadable Object)
    Downloadable interactivity application plus related declarative content items (e.g. text, graphics, scripts and audio) to be displayed during the interactivity event
    Function and behavior are related to the program that it accompanies
  Interactivity Content Items
    Data files required by the interactivity apps
  Triggers
    Data objects, bound to a particular program segment, that perform location and timing-related signaling in support of interactivity

## Slide 4: ATSC 2.0 Interactivity Framework (2 of 3)
TPT structure
Element/Attribute |  |  |  |  | Card-inality | Data Type | Description and Value
TPT |  |  |  |  |  |  | 
 | @majorProtocolVersion |  |  |  | 0..1 | integer 0..15 | Major Protocol Version, default=“1”
 | @minorProtocolVersion |  |  |  | 0..1 | integer 0..15 | Minor Protocol version, default=“0”
 | @id |  |  |  | 1 | anyURI | segment_id = domain_name/program_id
 | @tptVersion |  |  |  | 1 | unsignedByte | Data version of this TPT
 | @expireDate |  |  |  | 0..1 | dateTime | Date after which this TPT will not be used
 | @updatingTime |  |  |  | 0..1 | unsignedShort | Time interval to check for TPT updates
 | @serviceID |  |  |  | 0..1 | unsignedShort | NRT service_id
 | @baseURL |  |  |  | 0..1 | anyURI | Base URL for all relative URLs in TPT
 | Capabilities |  |  |  | 0..1 | nrt:CapabilitiesType | Essential capabilities for the segment associated with this TPT
 | LiveTrigger |  |  |  | 0..1 |  | Info on Internet live trigger delivery
 |  | @URL |  |  | 1 | anyURI | URL of server for live triggers
 |  | @pollPeriod |  |  | 0..1 | unsignedByte | Short polling period in seconds
 | TDO |  |  |  | 1..N |  | TDO (app) for the segment associated with this TPT
 |  | @appID |  |  | 1 | unsignedShort | Application ID of this app, unique within the scope of this TPT
 |  | @appType |  |  | 0..1 | integer 0-15 | Application type (default: 1=”TDO”)
 |  | @appName |  |  | 0..1 | string | Display name (for viewer launch consent)
 |  | @globalID |  |  | 0..1 | anyURI | Globally unique app ID
 |  | @appVersion |  |  | 0..1 | unsignedByte | Version of this app
 |  | @cookieSpace |  |  | 0..1 | unsignedByte | Persistent storage needed; default=0
 |  | @frequencyOfUse |  |  | 0..1 | integer 0..15 | Code values per Table 6.3
 |  | @expireDate |  |  | 0..1 | dateTime | Expire date for caching this app
 |  | @testTDO |  |  | 0..1 | boolean | Flag for test app; default=”false”
 |  | @availInternet |  |  | 0..1 | boolean | Default=”true”
 |  | @availBroadcast |  |  | 0..1 | boolean | Default=”true”
 |  | URL |  |  | 1..N | anyURI | App URL(s)
 |  |  | @entry |  | 0..1 | boolean | Indicator of entry point; default = “false”
 |  | Capabilities |  |  | 0..1 | nrt:CapabilitiesType | Essential capabilities to present this app
 |  | ApplicationBoundary |  |  | 0..1 |  | Extensions to app boundary
 |  |  | OriginURL |  | 1..N | anyURI | Origin to be added to app boundary
 |  | ContentItem |  |  | 0..N |  | Content item used by this app
 |  |  | URL |  | 1..N | anyURI | URL(s) of content item
 |  |  |  | @entry | 0..1 | boolean | Indicator of entry point; default = “false”
 |  |  | @updatesAvail |  | 0..1 | boolean | Default=”false”
 |  |  | @pollPeriod |  | 0..1 | unsignedByte | Short polling period in seconds
 |  |  | @size |  | 0..1 | 24-bit integer | Size of content item, in kilobytes
 |  |  | @availInternet |  | 0..1 | boolean | Default=“true”
 |  |  | @availBroadcast |  | 0..1 | boolean | Default=“true”
 |  | Event |  |  | 1..N |  | Event targeted to this TDO
 |  |  | @eventID |  | 1 | unsignedShort | Unique identifier of this Event element within the scope of the TDO element.
 |  |  | @action |  | 1 | string | Allowed values are “prep”, “exec”, “susp”, and “kill”
 |  |  | @destination |  | 0..1 | unsignedByte | Device to which the event is directed (primary screen, second screen, or both)
 |  |  | @diffusion |  | 0..1 | unsignedByte | Period for applying diffusion, in seconds
 |  |  | Data |  | 0..N | base64Binary | Data to be used for this event
 |  |  |  | @dataID | 1 | unsignedShort | Unique identifier of this Data element within the scope of the Event element.

## Slide 5: ATSC 2.0 Interactivity Framework (3 of 3)
TDO, TPT and Triggers can be delivered in different ways, depending on the system architecture, broadcaster’s preference, and device capabilities, e.g.,
  Within the broadcast stream
    In NRT service as file objects delivered over FLUTE sessions
    Within DTV Closed Captioning (DTVCC) channel, via extension to CEA-708
  Over the Internet
    Delivery of Triggers using ACR (Automatic Content Recognition) process, via watermarking (WM) or fingerprinting (FP)
    Delivery of TDO, TPT and Triggers by broadcaster’s designated interactive TV server
Reason for DTVCC and ACR approaches
  For in-home distribution via Cable TV STB, auxiliary content (such as NRT service delivered on dedicated virtual channel) are stripped out
  In some scenarios, even the DTVCC channel is unavailable, for example when HDMI interface connects cable STB to TV

## Slide 6: TDO Delivery and Activation Options
Full Transport Stream (TS) available, no Internet access
Full TS available, Internet access is available
Partial TS available, triggers carried in DTVCC channel
Only A/V streams available, interactivity support via ACR and Internet access

## Slide 7: Option 1: Full TS Available, No Internet Access
TDO
SMT
service
service_id
IP Addr/Port
FLUTE TSI
1
2
4
Video ES
Audio ES
SSC
PSI/PSIP
FLUTE Session(s)
IP Net
5
DTV CC Caption Stream
3
6
FDT
TDO ref.
Content-Loc
TOI
7
7
TPT
Action
TDO ID
TDO_URL
(event data)
Event ID
Segment ID
8
(Activation Time)
Activation Trigger
TDO ID +Event ID
(Media Time)
Media Time Trigger
TPT URL
Notes: Receiver Steps (processing not intended to occur in chronological order by number):
Retrieve SMT from SSC in IP subnet to in turn
  determine entry points for FLUTE sessions
Retrieve Time Base Trigger from caption stream
Retrieve TPT from SSC in IP subnet
Retrieve FDT from FLUTE session
Match TDO_URLs in TPT with Content-Locations in FDT; retrieve TDOs
Retrieve Activation Trigger from caption stream
Apply Event referenced in Activation Trigger (at activation time)
  Activation Time may be explicit in Activation Trigger, or
  Activation Time may be arrival time of Activation Trigger
Note:
Other files referenced by TDO or TPT by URL are matched to Content-Location entries in FDT in a similar fashion

## Slide 8: Option 2: Full TS Available, Internet Access
TDO
Video ES
Audio ES
SSC
PSI/PSIP
FLUTE Session(s)
IP Net
2
DTV CC Caption Stream
1
3
TPT Server
TDO Server
7
TPT
Action
TDO ID
TDO_URL
(event data)
Event ID
4
5
(Media Time)
Time Base Trigger
TPT URL
(Activation Time)
Activation Trigger
TDO ID +Event ID
Difference from Option1:
TDO and TPT are acquired over Internet
as opposed to within NRT service
Notes: Receiver Steps:
Retrieve Time Base Trigger from caption stream
Download TPT over Internet using TPT URL referenced in Trigger
Download TDO and other content over Internet using URLs referenced in TPT
Retrieve Activation Trigger from caption stream
Apply Event referenced in Activation Trigger (at activation time)
  Activation Time may be explicit in Activation Trigger, or
  Activation Time may be arrival time of Activation Trigger

## Slide 9
Option 3 – Partial TS, DTVCC Carries Triggers
Video ES
Audio ES
DTV CC Caption Stream
TDO
2
1
(Media Time)
Time Base Trigger
TPT URL
3
TPT Server
TDO Server
7
TPT
Action
TDO ID
TDO_URL
(event data)
Event ID
(Activation Time)
Activation Trigger
TDO ID +Event ID
4
5
Notes: Receiver Steps:
Retrieve Time Base Trigger from caption stream
Download TPT over Internet using TPT URL referenced in Trigger
Download TDO and other content over Internet using URLs referenced in TPT
Retrieve Activation Trigger from caption stream
Apply Event referenced in Activation Trigger (at activation time)
  Activation Time may be explicit in Activation Trigger, or
  Activation Time may be arrival time of Activation Trigger

## Slide 10: Option 4: Only A/V Available, ACR and Internet Support for Interactivity
Video ES
Audio ES
1
ACR Server
TDO
2
3
TPT Server
TDO Server
4
7
TPT
Action
TDO ID
TDO_URL
(event data)
Event ID
Activation Time
AMT
TDO ID +Event ID
Activation
+
(Media Time)
Media Time Trigger
TPT URL
AMT: equivalent to bulk delivery of Activation Triggers: for a program segment, and delivered via HTTP along with the TPT for the segment in multi-part MIME message
Internet delivery of Media Time Triggers via Automatic Content Recognition (ACR) server due to receiver lacking access to Closed Caption Service #6. Receiver uses ACR to recognize video frames and synchronize the time base with them
Notes: Receiver Steps:
Send A/V samples to ACR server; retrieve Time BaseTrigger in response
Download AMT and TPT using TPT URL referenced in Trigger
Download TDOs and other content using URLs referenced in TPT
Apply Event referenced in Activation from AMT (at activation time)

## Slide 11: Trigger Timing Example: Live Content
TPT contains data for different interactive events, but playout times of those events cannot be known until the action in the program unfolds
Two types of Activation Triggers:
  Retiming Event Trigger used to dynamically adjust interactivity event time
  Immediate Event Trigger used to initiate immediate execution of event
9 Triggers associated with Program Segment 3:
Pre-Load Trigger enabling receiver to acquire TPT and interactive content for Segment 3
Media Time Trigger indicates current Media Time (in msec) relative to Segment 3
Retiming Trigger indicates Event_2 in TPT should be retimed to occur at Media Time 240
Another Media Time Trigger
Retiming Trigger indicates Event_5 in TPT should be retimed to occur at Media Time 444
Another Media Time Trigger
“
Immediate Trigger indicating Event_12 in TPT to be executed immediately
Retiming Trigger indicates Event_89 in TPT should be retimed to occur at Media Time 900
Execution time of “Event” trigger

## Slide 12: ATSC 3.0 Interactivity
ATSC 3.0 interactivity is likely to leverage basic 2.0 functionality
Key focus currently is to specify Watermarking based ACR solution for redistribution support
  Ongoing technical work to review and select solution among responses to Call for Proposal on audio and/or video watermarking technologies for automatic content recognition that could enable certain interactivity feature of ATSC 3.0 Standard
High level working draft on Redistribution support cites many sections currently defined for interactivity in ATSC 2.0

## Slide 13: Summary, Issues and Suggested Next Steps
ATSC has defined a technical solution framework for interactivity services in ATSC 2.0, likely to be adopted for ATSC 3.0
ATSC defines dynamic and asynchronous broadcast notification mechanism via Triggers, currently not defined in MBMS or 3GP-DASH specs
  Event mechanism as defined in MPEG-DASH may be functionally equivalent?
  Might consider its adoption in 3P-DASH – not just for interactivity support, but general purpose notification messaging
Support for personalized service interactivity is currently not specified in ATSC
Service interactivity solution at application/presentation layer is more aligned with CE-HTML than HTML5
Should study other broadcast or broadband TV interactivity mechanisms
What aspects of ATSC interactivity might be considered or adoption as solution components for 3GPP interactive services?

## Slide 15
Back-up Slides