## Slide 1
Wire line & Wireless PM File Formats
Standard File Formats
  Wireless – 3GPP
    Ref --- 3GPP 32.432 & 435
  Wire Line - MTOSI
    Ref -- SD! -30 ( attached )
Proprietary File Formats
  Currently many of the Network Elements and E/NMS do not support either of the standard File formats , instead they have proprietary File Formats which not only result in Integration Tax but also can potentially result in loss of information .
In a PM Integration Project, Integrating multiple File formats , is one of the most time consuming activity and standardization to even multiple but limited formats can substantially improve overall project duration and effort

## Slide 2
3GPP & MTOSI PM File Formats – High Level Comparison
Aspect | 3GPP | MTOSI | Comments
Number of Information Models | 3( with/without positioning, with MEASInfoId) | 1 | 3GPP Ims are almost simillar
Specified Implementations | XML, ASN.1 | XML,ASN.1 | In both casesa XML FF are volumnous
Normalization of Information | Highly Normalized | partial | Efficient transport. But does it significantly slow down Preperation, Parsing & Storage ?
Information completeness | Partial | exhaustive | Is the information really required in each data file ? Can this information extracted from Job info.
Payload/total data | High | Medium | Payload = Counter values , all other info describes/identifies. Higher ratio is preferred
leverage blank counter information | No | Yes | A lot of times (up to 70% of time counters are not measured ), so a FF which tries to leverage this fact can be more efficient

## Slide 3
3GPP & MTOSI PM File Formats – High Level Comparison (Contd )
Aspect | 3GPP | MTOSI | Comments
Support for RT/NRT, prioritized data transmission ( NRT requires support at multiple stages including FF ) | No | No | some possible support 1. priority counters on top 2. Abiliyt to split file to contain priority counters and easy merge
Support for Service Management ( Multiple NE, multiple MO type info) | No | No | It should be possible to retrieve info of different NE s and mo Types.
LtE network & NRT PM data generation & flow support | Not the originally designed for | Was the initial intent | Characterized by large volume of small data files- FF should have very low overhead, should allow easy concatenation and processing
Suspect Flage | At MOID Level | At PI /KPI instance level | Probably MOID level is sufficient ( If one PI is suspect all are suspect)

## Slide 4
PM File Formats – Suggested Guideline
1. There is scope for improving on both the prevailing wireless & wire line formats.
2.FF Requirements for PM data form NE to E/NMS and E/NMS to SM are different. And hence two independent IMs need to be specified.
3.The two IM s can most probably be merged so that the model reduces to the required FF with very little overhead
4.The FF IM should be independent from its implementation specification /solution set.
5. Transport efficiency should not be the only criteria, one should also look at generation, processing & storage efficiency
6. Information can be" normalized on time axis" , i.e send only information that is changing, this is opposed to the idea that a File instance has sufficient information so that it can be processed independently of all other information sources ( Job , meta data at producer etc )