## Slide 1: 3GPP / SA5 activities on Energy Efficiency and Energy Saving Management
Presentation to ETSI TC EE
May 2018

## Slide 2: 3GPP Structure
TSG RAN Radio Access Network
RAN WG1 Radio Layer 1 spec
RAN WG2 Radio Layer 2 spec Radio Layer 3 RR spec
RAN WG3 lub spec, lur spec, lu spec UTRAN O&M requirements
RAN WG4 Radio Performance Protocol aspects
RAN WG5 Mobile Terminal Conformance Testing
RAN WG6 GSM EDGE Radio Access Network
TSG SA Service & Systems Aspects
SA WG1 Services
SA WG2 Architecture
SA WG3 Security
SA WG4 Codec
SA WG5 Telecom Management
SA WG6 Mission-critical applications
TSG CT Core Network & Terminals
CT WG1 MM/CC/SM (lu)
CT WG3 Interworking with external networks
CT WG4 MAP/GTP/BCH/SS
CT WG6 Smart Card Application Aspects
Project Co-ordination Group (PCG)

## Slide 3
Organizational Partners (SDOs)
Organizational Partners
  ARIB (Japan)
  ATIS (USA)
  CCSA (China)
ETSI (Europe)
TTA (Korea)
TTC (Japan)
TSDSI (India)

## Slide 4
~400 Companies from 39 Countries
50.000 delegate days per year
40.000 documents per year
1.200 specs per Release
New Release every ~18 months
3GPP Facts and Figures
Chart: 
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
R99 | 1408 | 4398 | 2266 | 1004 | 581 | 512 | 111 | 42 | 23 | 5 | 5 | 1 | 0 | 0 | 0 | 0
Rel-4 | 376 | 2828 | 1900 | 690 | 257 | 122 | 63 | 48 | 22 | 20 | 13 | 11 | 8 | 7 | 2
Rel-5 | 27 | 644 | 3274 | 2842 | 2162 | 1357 | 509 | 94 | 25 | 22 | 7 | 7 | 5 | 3 | 2
Rel-6 | 172 | 1088 | 2458 | 3721 | 2074 | 1078 | 212 | 74 | 19 | 17 | 10 | 4 | 4
Rel-7 | 1 | 20 | 663 | 2529 | 3132 | 1262 | 492 | 176 | 91 | 43 | 25 | 15
Rel-8 | 49 | 777 | 4609 | 7073 | 2347 | 706 | 347 | 184 | 91 | 46 | 22 | 6
Rel-9 | 49 | 2918 | 4991 | 3252 | 1366 | 376 | 165 | 70 | 26 | 17
Rel-10 | 47 | 1722 | 3800 | 3103 | 1636 | 584 | 267 | 50 | 13
Rel-11 | 32 | 1152 | 4178 | 3525 | 2186 | 622 | 163 | 22
Rel-12 | 6 | 102 | 2254 | 5181 | 4287 | 1530 | 127
Rel-13 | 8 | 200 | 2648 | 5571 | 1214
Rel-14 | 24 | 2315 | 3269
R99
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13
R14
Approved CRs per year per Release

## Slide 5: 3GPP 5G Timeline
5G release timeline
Two phases for the normative 5G work
  Rel-15 (a.k.a. "5G phase 1")
    to be completed by June 2018
    aim at a first phase of expected 5G deployments in 2020
    New: Rel15 “late drop” introduced for NR with completion date Dec. 2018
  Rel-16 (a.k.a. "5G phase 2")
    to be completed by December 2019
    meet the ITU IMT-2020 submission requirements
June 2018
December 2019
March 2017

## Slide 6: 3GPP/SA5
ToR: The WG will specify the requirements, architecture and solutions for provisioning and management of the network (RAN, CN, IMS) and its services.

## Slide 7: 3GPP Reference Management Model
TS 32.101: Telecommunication management; Principles and high level requirements

## Slide 8: Mapping with ETSI NFV MANO
TS 28.500: Telecommunication management; Management concept, architecture and requirements for mobile networks that include virtualized network functions

## Slide 9: Pre-5G activities on Energy Efficiency
Work Item ‘Control and monitoring of Power, Energy and Environmental (PEE) parameters in Radio Access networks (RAN)’
  TS 28.304: Control and monitoring of Power, Energy and Environmental (PEE) parameters Integration Reference Point (IRP); Requirements
  TS 28.305: Control and monitoring of Power, Energy and Environmental (PEE) parameters Integration Reference Point (IRP); Information Service (IS)
  TS 28.306: Control and monitoring of Power, Energy and Environmental (PEE) parameters Integration Reference Point (IRP); Solution Set (SS) definitions
Can be seen as an ‘instantiation’ of ETSI ES 202 336-1 and 202 336-12 to GERAN, UTRAN and E-UTRAN

## Slide 10: Stage 1 - Overall architecture
DM: Domain Manager (a.k.a. Element Management System (EMS))
NM-RMS: Network Management layer – Remote Management Server
VS-RMS: Vendor-Specific Remote Management Server

## Slide 11: Stage 1 – Use Cases and Requirements

## Slide 12: Stage 2 – Object Model (1/2)

## Slide 13: Stage 2 – Object Model (2/2)

## Slide 14: Stage 2 – Interfaces

## Slide 15: Stage 2 - Example operation: Initiating a PEE measurement collection job

## Slide 16: Stage 3 – REST Solution Set

## Slide 17: Stage 3 – OpenAPI JSON specification

## Slide 18: Pre-5G activities on Energy Saving Management – Stage 1 (Use Cases)
3dTower.em
f
3dTower.emf
3dTower.em
f
3dTower.emf
3dTower.em
f
3dTower.emf
eNB
BTS / (e)NB
eNB in ES
UE
eNodeB Overlaid
Capacity limited network
The coverage area of a group of eNBs is taken care of by one or more of its eNBs while the others go into energy saving state.
This use case applies for Intra-RAT ONLY.
An eNB can only enter into an energy saving state if there is radio coverage by other radio systems – be it another eNB or an entity of another radio access technology - for the whole coverage area of the eNB in question.
This use case applies both for Intra- and Inter-RAT.
TS 32.551: Telecommunication management; Energy Saving Management (ESM); Concepts and requirements

## Slide 19: Pre-5G activities on Energy Saving Management – Architectures
NM-centralized architecture:
  NM instructs network elements / cells to enter or quit energySaving state (e.g. according to a schedule determined by network statistics)
  NM can be notified of any change
Distributed (/EM-centralized architecture):
  eNBs move themselves to/from energySaving state autonomously (in case of ‘capacity limited network’,
  NM sets policies and conditions under which the cells will move to energySaving state
  Examples for policies/conditions:
    IDs of NEs / cells to be considered
    Time period during which energy saving is allowed on selected NEs / cells
    Load thresholds to determine from when on energy saving shall be triggered
  NM can be notified of any change
energySaving state: in an off-peak-traffic situation, some functions of a cell or a network element are powered-off or restricted in resource usage in other ways, whereas the cell or network element is still controllable.

## Slide 20: 5G activities on Energy Efficiency
Draft TR 32.972: Telecommunication management; Study on system and functional aspects of energy efficiency in 5G networks (http://www.3gpp.org/ftp//Specs/archive/32_series/32.972/ )
  Scope: 5G
  Content:
    State-of-Art of high-level EE KPIs definitions, and measurement methods, by other SDOs / WGs
    Identification of normative work to be initiated re. the energy efficiency of 5G networks
Study Item supported by:
Supporting IM name
ORANGE
AT&T
Deutsche Telekom
KPN
Telecom Italia
Vodafone
NTT DOCOMO
China Mobile
Ericsson
Nokia
Huawei
ZTE
Intel
NEC

## Slide 21: Collaboration
LS sent out by 3GPP/SA5 to NGMN, ITU-T SG5, ETSI TC ATTM, ETSI TC EE, 3GPP RAN, SA, CT, proposing a responsibility matrix
  ETSI TC EE (in collaboration with ITU-T SG5) to:
    Define high-level EE KPIs (high-level = not specific to one single network domain / technology)
    Specify measurement methods
  3GPP, as an ‘applicative’ SDO, to:
    Identify network domain / technology specific measurement required to be able to calculate high-level EE KPIs
    Apply recommended measurement methods on its own architecture / protocols / collection method.

## Slide 22: Points for discussion
Is 3GPP energySaving state (Enum {isNotEnergySaving, isEnergySaving}) a sort of Energy Aware State (cf. GAL)?
Would there be any benefits in introducing intermediate state values, to allow for advanced energy saving modes?
With the arrival of virtualization, any measurement method for the Energy Consumption of a VNF / VNFC?
With the separation of Control Plane (CP) from User Plane (UP), does DV / EC still apply well for CP network functions?
Any EE KPI definition, with corresponding measurement method, at Network Slice level?

## Slide 23
www.3gpp.org
contact@3gpp.org
Thank You!