## Slide 1: Supporting document for S5-19123 Proposed New SID on Management and orchestration aspects with integrated satellite components in a 5G networks
Cyril MICHEL, THALES,
cyril.michel@thalesaleniaspace.com

## Slide 2: Specific characteristics of satellite systems
High (few hundreds for Low Earth orbiting satellites) to very high altitude (35 786 km for geostationary satellite).
Large to very large footprints of physical radio coverage, from few hundreds of km to several thousands, with broadcasting capabilities over several states.
One to several thousands of spacecraft can be integrated into a single constellation of satellites to provide continuity of service
End to End delays as provided in a session be significantly higher than for terrestrial networks, whilst satellite network will contribute to reachability and reliability.

## Slide 3: Example of radio coverage of satellite systems
As extracted from TR 22.822 (Study on using Satellite Access)

## Slide 4: Satellite specifics are already addressed in the specifications of the 5G system at service level
TS 22.261 (Service requirements for next generation new services and markets) includes various requirements associated with satellite systems, for instance:
“
6.3.2.3 Satellite access
The 5G system shall be able to provide services using satellite access.
A 5G system with satellite access shall support different configurations where the radio access network is either a satellite NG-RAN or a non-3GPP satellite access network, or both.
To provide services using satellite access, the air interface of the 5G system shall support a one-way latency of up to 280 ms.
“
TS 22.261 requires also that a 5G system providing service with satellite access shall be able to support GEO / MEO /LEO based satellite access with up to the end-to-end latency associated to these types of constellations.

## Slide 5: Conclusion
Is is thus proposed to create a New SID in WG SA5 with the objective at:
  Identifying the main key issues associated with the business model, management and orchestration the integration of a satellite component in the 5G network and to provide the associated solutions.
  This study shall aim at minimising the impacts and the complexity of the satellite integration in the existing business model, management and orchestration of the current 5G network.

## Slide 6: Annex: Other on-going study items relating to satellite (to be completed in 2019)
“Study on architecture aspects for using satellite access in 5G”
  => 3GPP TR 23.737
“Solutions for NR to support non-terrestrial networks (NTN)”
  => 3GPP TR 38.821