## Slide 1
Rakuten Mobile, Orange, China Unicom, FiberCop, TELUS, Mavenir Pending list (review ongoing): AT&T?, DoCoMo?, KDDI?, CMCC?, Samsung?
Cloud Native NF - Data Streaming Connection based vs Pub-Sub/Message Bus based

## Slide 2: Solution 1 – Connection based approach
2. Each NF MnF establish a direct and persistent connection with a server node to send and receive data
3. A load balancer distributes the connections to multiple server nodes in semi-persistent manner (re-establishing the connections are needed).
NF
MnF Producer
NF
MnF Producer
server node
(high availability)
server node
server node
server node
(high availability)
Data aggregation and distribution
OAM
Application
NF
MnF
NF
MnF Producer
NF
MnF
NF
MnF
Connection load balancer
Container workload instances
Management System
1. A MnF collects the data from multiple micro-service workloads first
4. Data aggregation/distribution layer collect traffic from multiple server nodes and distribute integrated data to back-end applications implementing the OAM functions.
5. High node and connection availability for scaling and resiliency to single point failure

## Slide 3: Solution 2 – Message bus/pub-sub based approach
Kafka Message broker
Kafka message broker
Server node
NF
MnF
NF
MnF
OAM
Application
NF
MnF
Management System
Publish
Container workload instances
message broker
1. NF or its workload instances send data to the message broker in parallel via MnF using message bus-based protocol
subscribe
2. Load balancing function distribute datas to multiple message broker server nodes in full dynamic manner
Load balancing
3. Message bus automatically deliver data to the subscriber applications implementing the OAM functions.
Message bus framework
4. High broker availability for scaling and resiliency to single point failure

## Slide 4: Key Differences - Connection based VS Pub-Sub based Systems
Connection-based system | Pub-sub based system
Direct Communication: Clients establish a direct connection with a server to send and receive data. Point-to-Point: Communication is typically one-to-one, with each client having a dedicated connection to a server. Multiple container workloads send data through a single connection point or several limited connection points. Need data aggregation and distribution layer to integrate data from multiple server nodes and broadcast individually to the receiving OAM applications. Scalability: Rebalancing connections during scaling in/out need reconnection resulting in service interruption. As the number of clients or servers increases, managing connections can become complex (due to tight coupling), resource-intensive and disruption to running services. Imbalanced or wasted resource usage can happen due to the due to stateful and persistent connections. Fault Handling/Resiliency The endpoints actively monitor the connection for failures. This involves heartbeat messages or TCP keep-alive mechanisms introducing additional overhead. The direct connection creates a single point of failure (SPOF). Reconnection, re-authentication or session re-establishment are needed during failures which leads to service interruption or disruption. SPOF may be resolved by establishing redundant connections between clients and servers enabling failing-over. However, if a failure occurs during data transmission, data may be lost. Vendors need to implement their own mechanisms for ensuring data integrity (e.g., acknowledgements, sequence numbers, retransmissions) between client and server side (coupling) . Implementing robust reconnection logic, session management, and data integrity mechanisms can add significant complexity, coupling, and proprietary to the client and server applications. Security WebSocket security focuses on securing a real-time communication channel, relying on SSL/TLS for encryption and vendor application-layer authentication and authorization. | Decoupled Communication: Publishers send messages to a broker, which then distributes them to interested subscribers. Publishers don't need to know who the subscribers are and vice versa. One-to-Many and Many-to-Many: Multiple container workloads can send data in parallel. Pub-sub naturally supports fan-out, where a single message is delivered to multiple subscribers. This is much more efficient than broadcasting messages individually to each receiving applications. Scalability: Load balancing is done dynamically, no stateful connection need to be maintained. Pub-sub systems can scale more easily because the broker handles the message distribution, and publishers and subscribers are decoupled. Message brokers are designed to be horizontally scalable - add more brokers to the cluster to increase throughput and capacity. Systems like Kafka also allow partitioning of topics across multiple brokers. This allows processing messages in parallel and increase throughput. Fault Handling/Resiliency Many pub-sub systems offer message persistence. Messages are stored on disk (or in memory) by the broker until they are successfully delivered to subscribers. This ensures that messages are not lost if a subscriber is temporarily unavailable. Message brokers are often deployed in clusters or with replication to provide high availability. If one broker fails, another broker can take over. If a subscriber fails to acknowledge receipt of a message, the broker can redeliver the message. Robust data integrity and fault tolerance mechanisms are implemented by the messaging middleware decoupling the client and server side, reducing complexity and avoiding proprietary. Security Message bus security focuses on securing a distributed system for data streaming. Most message bus framework comes with strong built-in authentication and authorization mechanisms, e.g. SASL, ACLs, along with SSL/TLS for encryption.

## Slide 5: Key Differences - Connection based VS Pub-Sub based Systems
Feature | Persistent connection-based system | Pub-sub based system
Communication | Direct | Indirect (via broker)
Scalability | Limited | Good
Fault Handling/Resiliency | Limited | Good
Coupling between producer and consumer (when doing cloud-native at large scale) | Tight | Loose
Development and integration Complexity (when doing cloud-native at large scale) | High | Low
Resource usage efficiency (when doing cloud-native at large scale) | Low | High
Security | Basic | Good
Example Use Cases | Client-server web applications, Real-time chat applications, online gaming, streaming video, file transfer | real-time analytics, Event-driven, distributed architecture, micro service communications
Example Technology | WebSocket, TCP socket | Kafka, RabbitMQ, Redis Pub/Sub+ Quotas + Auditing

## Slide 6: Which one is more suitable for cloud-native NF and its management?
NF
MnF
NF
MnF
OAM
Application
NF
MnF
Container workload instances
NF
NF
gNB
OAM System
Message bus framework
Conventional Deployment
Cloud-native Deployment
Edge/central cloud
Conventional deployment is closer to a client-server web application type of use case (See page 5).
Connection based approach is more suitable
Web client
Web server
Cloud-native deployment is closer to distributed and microservice communication use case (See page 5)
Pub-sub based approach is more suitable especially when cloud-native is done at scale

## Slide 7: Commercial benefits for operators using message bus communications
Message bus provides significant commercial benefits for operators’ businesses, especially when dealing with large-scale, real-time data processing and event-driven architectures.
Better user experience: Enables businesses to process and analyze data in real time, allowing for faster decision-making and improved responsiveness to network changes. Real-time insights lead to better user experiences. Faster response to operational issues reduces downtime and improves efficiency.
Scalability and cost efficiency: Reduces the need for expensive, monolithic systems to handle large-scale data. Cost-effective scaling ensures businesses can grow without incurring exponential infrastructure costs.
Decoupling of system and interoperability: This simplifies system architecture and reduces dependencies. Faster development cycles and improved interoperability between NF and OAM suppliers reduces integration costs and complexity, saving time and money in the long run.
Improved resiliency and data integrity: Minimizes downtime and data loss, which can be costly for businesses. Ensures consistent and reliable user experiences, improving brand reputation.
Unified data platform: single platform for collecting, storing, and distributing data across multiple systems (e.g., databases, analytics tools, NWDAF, MDT, AI/ML microservices). Reduces the need for multiple data integration tools and adaptations (e.g. WebSocket to message bus), lowering operational costs. Simplifies data pipelines, making it easier to manage and maintain.
Integration with Existing Tools: Integrates seamlessly with a wide range of tools and systems in the cloud, including databases, analytics platforms, and cloud services, reducing the cost and effort of building custom integrations. Leverages existing investments in tools and infrastructure in the cloud.
Future-Proofing the Business: Message bus's ability to handle diverse use cases (e.g., PM metrics, messaging, log aggregation, stream processing) makes it a versatile platform for evolving business needs. Protects investments by providing a platform that can adapt to future requirements.
Security: Use built-in, integrated and by-design security architecture and mechanisms for cloud native environment to achieve towards zero-trust framework，lower security framework investment, lower operational cost and better security related interoperability.

## Slide 8: Impact to 3GPP management system and SBI API standard
MnS producer
MnS consumer
Message bus communication
Management data job control (e.g., PM or trace job creation, PM metric subscription, conveying end-point information)
Service view
Function view
Kafka Message broker
Kafka message broker
Server node
NF
MnF
NF
MnF
OAM
Application
NF
MnF
MnF
Publish
Container workload instances
message broker
subscribe
LB
Message bus framework
Implementation example details
A new Streaming Data Reporting Service API needs to be added for the MnS consumer send request to the MnS producer to establish message bus communication session (e.g. topics).
After the message bus communication session is established, the MnS producer starts reporting the management data using message bus publishing protocol to the MnS consumer.
There is minor impact to the TS 28.532 streaming data reporting service APIs to support the additional pub-sub/message bus based streaming protocol.
There is no impact to other MnS and SBA architecture. This is purely transport layer change (Websocket send -> message bus publishing).
There is no backward compatibility impact, no change to existing WebSocket related APIs.

## Slide 9: Impact to 3GPP management system and SBI standard – more details
Solution today (WebSocket only)
Additional solution for message bus-based streaming
message bus publishing
there is no change to the existing Streaming Data Reporting Service APIs which establish a WebSocket streaming connection between MnS producer and MnS consumer.
A new Streaming Data Reporting Service API will be added for the MnS consumer send request to the MnS producer to establish a message bus streaming session instead of a connection.
E.g. for Kafka, the logical streaming session is equivalent to Kafka topic, and the streaming session establishment request contains a streamInfoList(TS28.532),topic ID, consumer’s broker endpoint information and optionally a partition information.
After the streaming session is established, the MnS producer start reporting the management data using message bus publishing protocol, e.g. Kafka, referring to the ID and endpoint information provided by the MnS consumer.

## Slide 10: Technology agonistic and compatibility with WebSocket based Pub-Sub pattern implementation
messaging server
messaging server
NF
MnF
NF
MnF
OAM
Application
NF
MnF
MnF
Publishing: e.g.
WebSocket send
Kafka send
Redis Pub
RabbitMQ Pub
Container workload instances
messaging server
subscribe
LB
Messaging framework
MnS producer
MnS consumer
Publishing
Messaging session establishment
SBI Service view
The SBI solution can be made technology agnostic, supporting all types of message bus implementations (e.g. Kafka, RabbitMQ)
Pub-sub/message bus-based communication is a design pattern rather than a specific transport technology.
WebSocket can also implement the pub-sub/message bus-based pattern with load balancer, data aggregator and distributor shown above, e.g. Socket.IO.
The solution also support WebSocket based communication without any change at the NF side (message broking is handled at the management system side).
Aggr.
Distr.

## Slide 11: Relationship with SBMA and other services
MnF
(data sharing agent)
Kafka message broker
Server node
Message broker
Publishing
MnF
Subscribing
MnF
e.g. NSSMF,
Analytic, AI/ML
MnF
MnF
MnF
e.g. NFMF
Kafka message broker
Server node
Message broker
MnF
Publishing
OAM application
Subscribing
OAM application
e.g. SO, SA, GUI, NF analytic
NF
Rel-19 CMO focus and scope
MnF internal implementation
SBI exposure
Rel-20 SBMA scope
Extend same streaming service API based on message bus publishing
New streaming service API
Based on message bus subscription
Publishing
Enable cloud-native NF to stream PM/log/analytic data base on message publishing
Enable generalized solution set for both NFs and internal services in 3GPP management system
Normative output:
Define use case and requirement on NF management
Identify architecture impact to NF and NF management
Normative output:
Identify further architecture impact in SBMA
Define Stage 3 API solution set

## Slide 12: Key Messages to be Endorsed
Cloud-native NF, comparing against conventional NF, is closer to distributed and microservice communication use case rather than client-server web application use case (see page 6).
Pub-sub/message broker-based approach is more suitable especially when cloud-native is done at scale (see page 5 and 6).
The 3GPP standard and NF industry should evolve to leverage these recently developed cloud technologies (e.g. K8S, message bus).
In the cloud industry, supporting multiple communication mechanisms for cloud applications is very normal - primary communication mechanism for better performance and fallback mechanism to ensure largest compatibility.
Similarly, for cloud native NFs, propose to add message bus as an additional data streaming method for better performance in large scale cloud environment and keep WebSocket as fallback mechanism for backward compatibility.
The solution can be made technology agnostic supporting all types of message bus implementations, and also WebSocket based pub-sub pattern implementation without any change at the NF side (message routing is handled at the management system side).
The CMO scope can focus on the study of enabling Cloud-native NF to stream PM/log/analytics data based on message publishing and define requirements for NF management while streaming across services within 3GPP management system and a generalized API solution set can be further studied in SBMA scope in Rel-20.

## Slide 13: Integration with Generic-OAM Functions
Collect performance metrics, logs from individual VNF/VNFC instances using e.g. Prometheus
Send aggregated information from the VNF metrics aggregator function via message bus publishing
Kafka message broker
Server node
OAM
Application
Management System/MnF
Messaging server
subscribe
Load balancing
Messaging framework
Send 3GPP NF metrics and logs using message bus publishing and 3GPP SBI
Aggr. And Distr.
NF
MnF
NF
MnF
NF
MnF
VNFC instances expose VNF-specific metrics and logs, such as number of active sessions, packets sent, etc.
VNF metric/log aggregator can collect metrics/logs from each individual VNF/VNFC instances and provide aggregated information to management system.
Same messaging framework can be used to support both 3GPP NF-specific metrics/logs and VNF-specific metrics/logs.
Enable unified data lake framework for analytic/AIML and correlation between application and deployment specific metrics/logs

## Slide 14: Integration with OpenTelemetry
NF
MnF
OpenTelemetry Collector
Collect VNF-specific metrics/logs from individual VNF/VNFC instances using e.g. Prometheus
Send aggregated information via message bus publishing
Kafka message broker
Server node
OAM
Application
Management System/MnF
Messaging server
subscribe
Load balancing
Messaging framework
Send 3GPP NF metrics and logs using message bus publishing
OpenTelemetry Collector
Aggr. And Distr.
NF Deployments/VNF
Same messaging framework can be used to support all three domains
  3GPP NF-specific metrics/logs
  VNF-specific metrics/logs
  Infrastructure-specific metrics/logs
Enable unified messaging framework for analytic/AIML and correlation among application, deployment and infra specific metrics/logs
Container workload instances
Cloud Infra
Collect Infra-specific metrics/logs
Collect 3GPP NF specific metrics/logs from individual workloads