## Slide 1: discussion on public warning application over 5G system
< Shuang Li ,Yingying Zhang>
<3GPP, China Broadnet>

## Slide 2: Background
Public warning
Set-top box , TV, and emergency loudspeaker could receive emergency warning information immediately, in the form of text message or voice. For instance: prominent warning message on TV screen, or blaring alarm from loudspeaker.
The requirements is in TS 22.286.
WARNING:…
WARNING:…
Voice: “earthquake…”
Voice: “earthquake…”
STB
Phone
V2X vehicle
Public camera
“earthquake…”
“earthquake…”
CBS based PWS
via SIB
Only text with restricted length
No ACK
Less media type of warning
PWS architecture with different representation from 23.041
SBA based architecture
RP based architecture
Explore more possibilities of PWS over 5GS/5MBS !!!
However, unidirectional broadcast without acknowledgement. In some scenarios, the plain text is not sufficient as it is easily neglected by people and not viewed in real time and interactive multimedia services are demanded.
In addition, the 5MBS broadcast mode could be utilized to broadcast PW notifications to cell phone users across different operators’ 5G networks in order to provide better public services.

## Slide 3
Basic use case – flood warning
The National Emergency Center finds that A city will be hit by heavy rainfall within 24 hours, which may cause flood disasters.
They transmit the flood warning to all people in A city through the emergency system, to inform mountaineering tourist, fishermen, resident in low-lying place move to safe area as soon as possible.
To mobilize more prople to evacuate immediately, the real-time multimedia notification with sound/vibration showing flood video and escape route indication will make them more clear about the dangerous situation and get effective assistance to survive through multimedia and interactive services
In emergency circumstances, acknowledge is ment from the users is desired to make sure that the targets in the area is well notified,which is also beneficial for further actions to reduce avoidable casualties.
fig. flood in A city
Video.:Rainstorm flood disaster self-rescue strategy for e.g.
Video.:A real-time flood disaster video for e.g.
fig. flood warning

## Slide 4
Basic use case - earthquake
The National Emergency Center detect a disater is coming, and they transmit the disater notification to all the people through the emergency system.
Based on the location information,The emergency system calculates the extent of harm caused by the disater, and then send precise and personalized emergency notification for people in different places.
For example, if the Emergency system detects a grade 3 earthquake will struck Chengdu, different emergency notification will be sent to people in different places:
- to Chengdu: A grade 3 earthquake will struck Chengdu 20s later. Please go out to open space as quickly as possible.
- to Mianyang: A grade 3 earthquake will struck Chengdu in 20s. A 2.8 grade secondary wave will arrive Mianyang 50s later.
UE could receive the emergency notification (video, voice, text message etc.) immediately, and the notification can’t be interrupted by any process of the phone.
e.g.:an earthquake warning include guide line to the nest shelter.

## Slide 5
Requirement and Summary: Public Warning over 5GS/5MBS
Support customized public warning content per different area;
Support of acknowledgement of the public warning
Support of the priority of the Public Warning Notification management, e.g.., it is not interrupted by other actions on the phone
Support of delivery of public warning content in an efficient way, e.g., make use of 5G MBS
Support of the public warning notification settings, e.g., on, off, on-demand
Identify the existing functionalities/service API provided by SA6 which can be reused.
As a complementary, the PWS over 5GS/5MBS can provide more information in multiple media types e.g., video, audio, map and so on.

## Slide 6
Other clarifications
Relationship with PWS via CBS
  PWS over 5GS/5MBS is an complementary of PWS via CBS

## Slide 7: FS_PWS_App: Study on public warning application over 5G system
Continuation or New Item: New Item
Study Item/Work Item/Both: Both
Source of requirements: SA1 (TS 22.268) and SA6 originated Architectural requirements
Expected Output: New TR for Study item and New TS for Work item
Anticipated start date/meeting: SA6#59-adhoc/Jan-24 (start of Study), SA6#62/Aug-24 (start of Normative)
Target Completion: SA6#62/Aug-24 (End of study) , SA6#64/Nov-24 (End of Normative)
Estimated TUs: 8 TUs (SID) + 6 TUs (WID)
Rapporteurship: China Broadnet
Supporting IMs: China Broadnet,CMCC, China Telecom,China Unicom, ZTE,CALTTA, CATT,HuaWei,

## Slide 8: FS_PWS_App: discussion on public warning application over 5G system
Description:
  3GPP SA1 has specified service requirements for Public Warning System (PWS) requirements in TS 22.268.
  In 5GS, the CBS mechanism is specified to support the PWS. However, the PWS over CBS has some limitations, e.g., only text with restricted length, unidirectional broadcast without acknowledgement. In some scenarios, the plain text is not sufficient as it is easily neglected by people and not viewed in real time and interactive multimedia services are demanded. For example, when the flood occurs, people within relevant areas may ignore or underestimate the danger from the plain text notification and still go to the mountains for hiking, camping. Some people may be unwilling to leave the area even if text message is received. In such cases, the real-time multimedia notification on mobile phone with sound/vibration showing flood video and escape route indication will make them more clear about the dangerous situation and get effective assistance to survive through multimedia and interactive services. Also, the acknowledgement from the users is desired to make sure that the targets in the area is well notified. Such acknowledgement is also beneficial for further actions to reduce avoidable casualties.
  In addition, the 5MBS broadcast mode could be utilized to broadcast PW notifications to cell phone users across different operators’ 5G networks in order to provide better public services.
  As a complementary, the PWS over 5GS/5MBS can provide more information in multiple media types e.g., video, audio, map and so on.

## Slide 9: FS_PWS_App: discussion on on public warning application over 5G system
Objectives: The objectives of the study include:
1. Analyse requirements of public warning over 5GS/5MBS including SA1, SA6 and other SDO, industry organizations.
2. Based the requirements, develop keys, corresponding architecture requirements and solution recommendations to support the PWS over 5GS/5MBS considering the following aspects (but not limited to):Support customized public warning content per different area;
  a. Support customized public warning content per different area;
  b. Support of acknowledgement of the public warning
  c. Support of the priority of the Public Warning Notification management, e.g.., it is not interrupted by other actions on the phone
  d. Support of delivery of public warning content in an efficient way, e.g., make use of 5G MBS
  e. Support of the public warning notification settings, e.g., on, off, on-demand
  f. Identify the existing functionalities/service API provided by SA6 which can be reused.
Dependency on other working groups:
  No
Impacts to 3GPP/Industry work if this is not accepted into Rel-19:
  Less sufficient tools for PWS.

## Slide 10
THANKS!