## Slide 1: Discussion on media delivery mapping between SEALDD and SA4
Jian Zhang
Huawei, Hisilicon

## Slide 2: Outline
Background
Media delivery procedure in SA4
Media delivery mapping between SEALDD and SA4
Summary and way forward

## Slide 3: Background
VAL client(s)/5GMS or RTC aware application
media session handler
media player/framework
SEALDD client
Transmission adaptation over 5G
SEALDD-C
3GPP network system
5GMS/RTC AF
5GMS/RTC AS
SEALDD server
Transmission adaptation over 5G
N33/N5
N6
SEALDD-UU
VAL server(s)/5GMS or RTC application provider
SEALDD-S
VAL-UU
VAL UE
The functionality mapping between SEALDD and SA4
In last meeting, the agreed CR (S6-233387) clarified the media delivery functionality mapping between SEALDD and SA4
The SEALDD as a general data delivery enabler, the following principles is utilized when supporting media type:
  The functionality/protocol defined in SA4 can be reused and further enhanced by SEALDD for supporting media type traffic

## Slide 4: Background
Regarding of media delivery procedure, in SEALDD, we have specified the regular data transmission procedure, mainly including the following procedures:
  Regular transmission request/response between VAL server and SEALDD server to negotiate the SEALDD-S connection information
  Regular transmission connection establish request/response between SEALDD client and SEALDD server to negotiate the SEALDD-UU connection information
Figure 9.2.2.2-1: SEALDD enabled regular data transmission connection establishment procedure (TS 23.433)
Based on the agreed functionality mapping and current specified SEALDD procedure, this discussion paper focuses on the media delivery procedure mapping between SEALDD and SA4, and clarify how the specified SEALDD transmission procedure to support the general media streaming defined in SA4

## Slide 5: Media delivery procedure in SA4 (Uplink)
Procedure#1: Uplink Media Streaming Procedure (TS 26.501)
Figure 6.1-1: High-level call flow for uplink media streaming (TS 26.501)
The uplink media streaming mainly includes：
  Step 1: providing content publishing configuration (e.g. path, protocol, entry point, the egest push/pull mode)
  Step 2: Internal interaction between 5GMSd AS and 5GMSd AF.
  Step 3: 5GMSu Application Provider provides Service Access Information to the 5GMS-Aware Application
  Step 4: the Service Access Information is provided to the 5GMSu Client.
  Step 5: uplink media streaming instantization
  Step 6: requests the 5GMSu Client to start an uplink streaming session
  Step 7: the 5GMSu Client requests Service Access Information from the 5GSMu AF
  Step 8: the Egest Session activation for the uplink streaming session.
  Step 9: Uplink media streaming starts from the 5GMSu Client to the 5GMSu AS
  Step 10: Uplink media preparation/operation in 5GMSu AS
  Step 11: Media streaming egest starts from the 5GMSu AS to the 5GMSu Application Provider
Regular transmission request/response in SEALDD-S in steps 1-2
Not involved
Provisioning transmission session between VAL server and VAL client in step 3
SEALDD service request in SEALDD-C in step 4
Regular transmission connection establishment request in SEALDD-Uu in step 6
SEALDD service request in SEALDD-C in step 4
Regular transmission connection establishment request/response in SEALDD-Uu in steps 6-7
SEALDD connection establishment in step 9
Uplink application traffic transmission in SEALDD-Uu and SEALDD-S below step 9
Notes: 补充Interface定义方面，

## Slide 6: Media delivery mapping between SEALDD and SA4 (Uplink)
Scenario | SA4 procedure | Related SEALDD procedure | Related parameter mapping
Uplink media streaming in Figure 6.1-1 of TS 26.501 | Step 1: 5GMS provisioning in M1u | Steps 1-2: Regular transmission request/response in SEALDD-S | Negotiate the access information in M1u/M2u (SEALDD-S), and optionally, in M4u/M5u (SEALDD-Uu)
 | Step 2: Internal interaction in M3u | Not involved | Not involved, no parameter mapping required
 | (Option#1) Step 3: Service access information acquisition | Step 3: Provisioning transmission session between VAL server and VAL client | Provide the M1u/M2u (SEALDD-S) for media egest and the M4u/M5u (SEALDD-Uu) to 5GMSu-aware Application (VAL client)
 | (Option#1) Step 4: UE APIs in M6u/M7u | Step 4: SEALDD service request in SEALDD-C | Provide the access information in M1u/M2u (SEALDD-S), and in M4u/M5u (SEALDD-Uu)
 | (Option#1) Step 5: Uplink streaming initialization in M5u | Step6: Regular transmission connection establishment request in SEALDD-Uu | Uplink transmission request in M5u (SEALDD-Uu)
 | (Option#2) Step 6: UE APIs in M6u/M7u | Step 4: SEALDD service request in SEALDD-C | Request the service and access information
 | (Option#2) Step 7: Service access information acquisition | Steps 6-7: Regular transmission connection establishment request/response in SEALDD-Uu | Service access information in M1u/M2u (SEALDD-S), and in M4u/M5u (SEALDD-Uu) obtained from 5GMSu AF(SEALDD server)
 | Step 8: Media session handling | Step 9: SEALDD connection establishment | No parameter mapping required
 | Steps 9-11: Uplink media streaming transmission in M4u and M2u | Below step 9: Uplink application traffic transmission in SEALDD-Uu and SEALDD-S | No parameter mapping required
The procedure mapping for uplink media delivery between SEALDD and SA4 can be captured as in the following table:

## Slide 7: Media delivery procedure in SA4 (Downlink)
Procedure#2: Downlink Media Streaming Procedure (TS 26.501)
Figure 5.1-1: High-level procedure for downlink media streaming (TS 26.501)
The downlink media streaming mainly includes：
  Step 1: Provisioning the usage of the 5G Media Streaming System, including the service access information for M5d/M4d for client-side access, and the service access information for M2d for media ingestion.
  Step 2: Internal interaction between 5GMSd AS and 5GMSd AF.
  Step 3: Media content ingestion from 5GMSd application provider
  Step 4: Service announcement information to 5GMSd-aware application including service access information or reference for M5d/M4d
  Step 5: Streaming begin, and the service access information is provided to 5GMSd Client
  Step 6: retrieve the service access information by using the access reference
  Step 7: Media Session Handling API for measurement, reporting, etc.
  Step 8: downlink media streaming content reception in client
Regular transmission request/response in SEALDD-S in steps 1-2
Not involved
Connection establishment in SEALDD-S in step 8
Provisioning transmission session between VAL server and VAL client in step 3
SEALDD service request in SEALDD-C in step 4
Regular transmission connection establishment request/response in SEALDD-Uu in steps 6-7
SEALDD connection establishment in SEALDD-Uu in step 9
Application traffic transmission in SEALDD-Uu below step 9
Notes: 补充Interface定义方面，

## Slide 8: Media delivery mapping between SEALDD and SA4(Downlink)
Scenario | SA4 procedure | Related SEALDD procedure | Related parameter mapping
Downlink media streaming in Figure 5.1-1 of TS 26.501 | Step 1: 5GMS provisioning in M1d | Steps 1-2: Regular transmission request/response in SEALDD-S | Negotiate the access information in M1d/M2d (SEALDD-S), and optionally, in M4d/M5d (SEALDD-Uu)
 | Step 2: Internal interaction in M3d | Not involved | Not involved, no parameter mapping required
 | Step 3: 5GMS ingest in M2d | Step 8: Connection establishment in SEALDD-S | No parameter mapping required
 | Step 4: Service access information Announcement | Step 3: Provisioning transmission session between VAL server and VAL client | Provide the M4d/M5d (SEALDD-Uu) to 5GMSd-aware Application (VAL client)
 | Step 5: UE APIs in M6d/M7d | Step 4: SEALDD service request in SEALDD-C | Provide the access information in M4d/M5d (SEALDD-Uu)
 | (Optional) Step 6: Service access information acquisition | Steps 6-7: Regular transmission connection establishment request/response in SEALDD-Uu | Service access information in M4d/M5d (SEALDD-Uu) obtained from 5GMSd AF(SEALDD server)
 | Step 7: Media session handling | Step 9: SEALDD connection establishment in SEALDD-Uu | No parameter mapping required
 | Step 8: Downlink media streaming transmission in M4d | Below step 9: Downlink application traffic transmission in SEALDD-Uu | No parameter mapping required
The procedure mapping for downlink media delivery between SEALDD and SA4 can be captured as in the following table:

## Slide 9: Conclusion and Proposal
The Media delivery mapping between SEALDD and SA4 as captured in the related CR (S6-233687), should be agreed to support media type traffic.
The regular data transmission procedure specified in SEALDD can support the media streaming delivery in SA4, by performing the required parameter mapping.
Notes: Mapping关系slide6对应CR被agreed