## Slide 1: Discussion on EAS traffic influence trigger considering UPF information
Huawei, Hisilicon
Yajie

## Slide 2
EAS traffic influence trigger considering UPF information
Potential Deployment
  The UPF#1 and UPF#2 may be associated with DNAI#1
  When the EES#1 trigger the traffic influence based on DNAI (e.g. DNAI#1) information
Current traffic influence based on DNAI information
  Issue: the User plane path still cannot be optimized, since the traffic influence is per DNAI, so that the delay between UPF#1 and UPF #2 still remains
Potential enhancement
  EAS can provide associated UPF information to EES; then the EES can trigger 5GC to perform traffic influence to optimize the user path per UPF
UE#1
Case#1: Current traffic influence
DNAI#1
UPF#1
UPF#2
EES#1
EAS#2
UE#1
DNAI#1
UPF#1
UPF#2
EES#1
EAS#2
Case#2: potential enhancement
Notes: Observation#1
#2
Way forward

## Slide 3
Way Forward
Enhance the traffic influence mechanism
EAS profile should be enhanced with the UPF information
Notes: Observation#1
#2
Way forward

## Slide 4: The end